PRESCRIPTIVE METHOD FOR RESIDENTIAL COLD-FORMED

STEEL FRAMING

Second Edition

Prepared for

The U.S. Department of Housing

and Urban Development

Office of Policy Development and Research

Washington, DC

Co-Sponsored by

The American Iron and Steel Institute

Washington, DC

and

The National Association of Home Builders

Washington, DC

by

NAHB Research Center, Inc.

400 Prince George's Boulevard

Upper Marlboro, MD 20774-8731

August 1997

PRESCRIPTIVE METHOD FOR

RESIDENTIAL COLD-FORMED

STEEL FRAMING

Second Edition

Prepared for

The U.S. Department of Housing

and Urban Development

Office of Policy Development and Research

Washington, DC

Co-Sponsored by

The American Iron and Steel Institute

Washington, DC

and

The National Association of Home Builders

Washington, DC

by

NAHB Research Center, Inc.

400 Prince George's Boulevard

Upper Marlboro, MD 20774-8731

August 1997

Disclaimer

While the material presented in this document has been prepared in accordance with recognized engineering principles and sound judgment, this document should not be used without first securing competent advice regarding its suitability for any specific application.  The use of this document is subject to approval by the local code authority.  Although the information in this document is believed to be accurate, neither the authors, nor reviewers, nor the U.S. Department of Housing and Urban Development of the U.S. Government, nor the American Iron and Steel Institute, nor the NAHB Research Center, nor any of their employees or representatives makes any warranty, guarantee, or representation, expressed or implied, with respect to the accuracy, effectiveness, or usefulness of any information, method, or material in this document, nor assumes any liability for the use of any information, methods, or materials disclosed herein, or for damages arising from such use.

Foreword

For centuries homebuilders in the United States have made wood their material of choice because of its satisfactory performance, abundant supply, and relatively low cost.  However, recent increases and unpredictable fluctuations in the price of framing lumber, as well as concerns with its quality, are causing builders and other providers of affordable housing to seek alternative building products.

Use of cold-formed steel framing in the residential market has increased over the past several years.  Its price stability; consistent quality; similarity to conventional framing; success in the commercial market; and resistance to fire, rot, and termites have attracted the attention of many builders and designers.  But lack of prescriptive construction requirements has prevented this alternative material from gaining wider acceptance among homebuilders and code officials.

This second edition of the Prescriptive Method for Residential Cold-Formed Steel Framing is the result of a 4-year research and development program sponsored by the U.S. Department of Housing and Urban Development (HUD) through a cooperative agreement with the National Association of Home Builders (NAHB) and the American Iron and Steel Institute (AISI).  The program was conducted by the NAHB Research Center with assistance from steering, advisory, and engineering committees.  These committees represented the interests and expertise of steel manufacturers, steel producers, code officials, academics, researchers, professional engineers, and builders experienced in cold-formed steel framing.

By facilitating the construction of steel-framed housing, this report and the companion volume, Commentary on the Prescriptive Method for Residential Cold-Formed Steel Framing, expand housing affordability through competition from new methods and materials.  It also provides cold-formed steel suppliers and consumers with standardized requirements for steel framing materials that will enhance market acceptance and promote consistent user application.  Finally, the report provides code officials and inspectors with the guidance necessary to perform their duties in the home construction process when cold-formed steel is utilized.

Paul A. Leonard

Deputy Assistant Secretary for

Policy Development

Acknowledgments

This report was prepared by the NAHB Research Center under sponsorship of the U.S. Department of Housing and Urban Development (HUD).  We wish to recognize the National Association of Home Builders (NAHB) and the American Iron and Steel Institute (AISI) whose co-funding and participation made this project possible.  Special appreciation is extended to William Freeborne of HUD for guidance throughout the project.

The preparation of this report required the talents of many dedicated professionals.  The principal authors were Nader R. Elhajj, P.E. and Kevin Bielat with review by Jay Crandell, P.E.  Appreciation is especially extended to members of the steering committee (listed below) who provided guidance on this document and who, with their input, made this work complete.

Kevin Bielat; NAHB Research Center

Delbert F. Boring, P.E.; AISI

Roger Brockenbrough; RL Brockenbrough

& Associates, Inc

Jay Crandell, P.E.; NAHB Research Center

Nader Elhajj, P.E.; NAHB Research Center

William Freeborne; HUD

Richard Haws, P.E.; American Buildings

Company

Jonathan Humble, AIA; AISI

Jeffrey Klaiman, CSI, CDT; Dale / Incor

Bill Knorr; Knorr Steel Framing Systems

Dr. Roger LaBoube, P.E.; University of

Missouri-Rolla

Jay Larson, P.E.; Bethlehem Steel Corp.

Mike Meyers; U.S. Steel

Mark Nowak; NAHB Research Center

Neal Peterson, P.E.; Devco Engineering, Inc.

Gregory Ralph; Dietrich Industries, Inc.

Dr. Paul Seaburg, P.E.; University of

Nebraska, Lincoln

David Smith, P.E.

Kurt Stochlia; ICBO Evaluation Service, Inc.

Geoff Stone, AISI

Mark Tipton; Met Homes

Ken Vought; USS - POSCO

Tim Waite, P.E.; T.J. Waite & Associates

Steve Walker, P.E.

The NAHB Research Center appreciates and recognizes the Light Gauge Steel Engineers Association (LGSEA) for their support and the following individuals and companies who provided steel, tools, and other materials to support various research and testing efforts.

Steve Argo and Bill Sauerwein of Black & Decker

Ray Frobosilo of Super Stud Building Products, Inc.

Ken Gilbert of Quick Drive USA, Inc.

Michael Kerner of Marino\Ware

Jeffrey Klaiman of Dale / Incor

Jay Larson of Bethlehem Steel Corp.

Robert Madsen and Neal Peterson of Devco Engineering, Inc.

Dean H. Peyton of Anderson-Peyton Structural Engineering Consultants

Gregory Ralph of Dietrich Industries, Inc.

Bill Reese of Grabber Construction Products

Michelle Shiira and Art Linn of Simpson Strong-Tie Company, Inc.

Marge Spencer of Compass International

Acknowledgments (continued)

Appreciation is also extended to the following members of the steering committee who participated in the development of the first edition of the Prescriptive Method for Residential Cold-Formed Steel Framing:

Joe Bertoni

Kevin Bielat; NAHB Research Center

Delbert F. Boring, P.E.; AISI

Roger Brockenbrough; RL Brockenbrough

& Associates, Inc

Jay Crandell, P.E.; NAHB Research Center

Ed DiGirolamo; The Steel Network

Nader Elhajj, P.E.; NAHB Research Center

John D. Ewing; USS - POSCO

William Freeborne; HUD

Richard Haws, P.E.; AISI

Bill Knorr; Knorr Steel Framing Systems

Dr. Roger LaBoube, P.E.; University of 	Missouri-Rolla

Mike Meyers; U.S. Steel

Mark Nowak; NAHB Research Center

Dr. Teoman Pekoz; Cornell University

Neal L. Peterson, P.E.; Devco Engineering

Gregory Ralph; Dietrich Industries, Inc.

Dr. Paul Seaburg; Pennsylvania State 	University

David Smith, P.E.

Kurt Stochlia; ICBO Evaluation Service, Inc.

Mark Tipton; Met Homes

Ken Vought; USS - POSCO

Tim Waite, P.E.; T.J. Waite & Associates

Steve Walker, P.E.

Julian White, Jr.; Dale / Incor

Riley Williams; Mitchell and Best

Roger Wildt, P.E.; Bethlehem Steel

CONTENTS

List of Tables	ix

List of Figures	xi

Executive Summary	xiii

INTRODUCTION	1

1.0	GENERAL	1

1.1	Purpose	1

1.2	Approach	1

1.3	Scope	1

1.4	Definitions	3

2.0	MATERIALS, SHAPES, AND STANDARD SIZES	9

2.1	Types of Cold-Formed Steel	9

2.2	Physical Dimensions	9

2.3	Uncoated Material Thickness	11

2.4	Bend Radius	11

2.5	Yield Strength	11

2.6	Corrosion Protection	11

2.7	Web Holes	12

2.8	Cutting, Notching, and Hole Patching	16

2.9	Bearing Stiffeners	17

2.10	Clip Angles	17

2.11	Fasteners	18

3.0	LABELLING	19

4.0	FOUNDATION	20

5.0	STEEL FLOOR FRAMING	21

5.1	Floor Construction	21

5.2	Floor to Foundation or Bearing Wall Connection	21

5.3	Allowable Joist Spans	21

5.4	Joist Bracing	21

5.5	Floor Cantilevers	22

5.6	Splicing	22

5.7	Framing of Floor Openings	22

5.8	Floor Trusses	22

6.0	STRUCTURAL STEEL WALL FRAMING	35

6.1	Wall Construction	35

6.2	Wall to Foundation or Floor Connection	35

6.3	Load Bearing Walls	35

6.4	Stud Bracing	36

6.5	Splicing	36

6.6	Corner Framing	36

6.7	Headers	36

6.8	Wall Bracing	37

6.9	Hold-down Requirements	38

6.10	Wind Uplift	38

7.0	NON-STRUCTURAL STEEL WALL FRAMING	68

7.1	Non-Load Bearing Studs	68

7.2	Construction Details	68

8.0	STEEL ROOF FRAMING	70

8.1	Roof Construction	70

8.2	Allowable Ceiling Joist Spans	70

8.3	Ceiling Joist Bracing	70

8.4	Allowable Rafter Spans	71

8.5	Rafter Bottom Flange Bracing	71

8.6	Splicing	72

8.7	Framing of Openings	72

8.8	Roof Trusses	72

8.9	Roof Tie-Downs	72

9.0	MECHANICAL, UTILITIES, AND INSULATION	90

9.1	Plumbing	90

9.2	Electrical Systems	90

9.3	HVAC Systems and Duct Work	90

9.4	Insulation	90

10.0	GENERAL CONSTRUCTION GUIDELINES	90

11.0	REFERENCES	92

LIST OF TABLES

Table 1.1	Applicability Limits 	2

Table 2.1	Cold-Formed Steel Member Sizes	10

Table 2.2	Minimum Thickness of Cold-Formed Steel members	11

Table 2.3	Minimum Coating Requirements	12

Table 2.4	Maximum Hole Dimensions and Spacing in Floor and Ceiling Joist Webs	14

Table 2.5	Maximum Hole Dimensions and Spacing for Structural Members

Other Than Floor and Ceiling Joists	15

Table 2.6	Minimum Screw Sizes For Steel-to-Steel and Structural Floor

Sheathing to Steel Connections	19

Table 5.1	Floor to Foundation or Bearing Wall Connection Requirements	31

Table 5.2	Floor Fastening Schedule	32

Table 5.3	Allowable Spans for Cold-Formed Steel Floor Joists - Single Span	33

Table 5.4	Allowable Spans for Cold-Formed Steel Floor Joists - Multiple Spans	34

Table 6.1	Wall to Foundation or Floor Connection Requirements 	46

Table 6.2	Steel Stud Thickness for 8' Walls Supporting Roof and Ceiling Only, 33 ksi	47

Table 6.3	Steel Stud Thickness for 8' Walls Supporting One Floor, Roof and

Ceiling, 33 ksi	48

Table 6.4	Steel Stud Thickness for 9' Walls Supporting Roof and Ceiling Only, 33 ksi	49

Table 6.5	Steel Stud Thickness for 9' Walls Supporting One Floor, Roof and

Ceiling, 33 ksi	50

Table 6.6	Steel Stud Thickness for 10' Walls Supporting Roof and Ceiling Only, 33 ksi	51

Table 6.7 	Steel Stud Thickness for 10' Walls Supporting One Floor, Roof and

Ceiling, 33 ksi	52

Table 6.8	Steel Stud Thickness for 8' Walls Supporting Roof and Ceiling Only, 50 ksi	53

Table 6.9	Steel Stud Thickness for 8' Walls Supporting One Floor, Roof and

Ceiling, 50 ksi	54

Table 6.10	Steel Stud Thickness for 9' Walls Supporting Roof and Ceiling Only, 50 ksi	55

Table 6.11	Steel Stud Thickness for 9' Walls Supporting One Floor, Roof and

Ceiling, 50 ksi	56

Table 6.12	Steel Stud Thickness for 10' Walls Supporting Roof and Ceiling Only, 50 ksi	57

Table 6.13 	Steel Stud Thickness for 10' Walls Supporting One Floor, Roof and

Ceiling, 50 ksi	58

Table 6.14	Wall Fastening Schedule	59

Table 6.15a,b	Allowable Header Spans for Headers Supporting Roof and Ceiling Only	60,61

Table 6.16a,b	Allowable Header Spans for Headers Supporting One Floor, Roof

and Ceiling 	62,63

Table 6.17a,b	Allowable Header Spans for Headers Supporting One Floor, Roof

and Ceiling, with Center Load Bearing Beam. 	64,65

Table 6.18	Total Number of Jack and King Studs Required at Each End of an Opening	66

Table 6.19	Number of Screws Required for Header to King Stud Connection 	66

Table 6.20 	Minimum Percent Length of Full-Height Structural Sheathing Along

Exterior Wall Lines	67

LIST OF TABLES (Continued)

Table 8.1	Roof Framing Fastening Schedule  	77

Table 8.2	Number of Screws Required for Ceiling Joist to Rafter Connections	78

Table 8.3	Number of Screws Required at Each Leg of Clip Angle For Rafter

to Ridge Member Connection	78

Table 8.4	Allowable Spans for Cold-Formed Steel Ceiling Joists, Single Spans

With Bearing Stiffeners (No Attic Storage)	79

Table 8.5	Allowable Spans for Cold-Formed Steel Ceiling Joists, Two Equal Spans

With Bearing Stiffeners (No Attic Storage)	80

Table 8.6	Allowable Spans for Cold-Formed Steel Ceiling Joists, Single Spans

With Bearing Stiffeners (Limited Attic Storage)	81

Table 8.7	Allowable Spans for Cold-Formed Steel Ceiling Joists, Two Equal Spans

With Bearing Stiffeners (Limited Attic Storage)	82

Table 8.8	Allowable Spans for Cold-Formed Steel Ceiling Joists, Single Spans

Without Bearing Stiffeners (No Attic Storage)	83

Table 8.9	Allowable Spans for Cold-Formed Steel Ceiling Joists, Two Equal Spans,

Without Bearing Stiffeners (No Attic Storage)	84

Table 8.10	Allowable Spans for Cold-Formed Steel Ceiling Joists, Single Spans

Without Bearing Stiffeners (Limited Attic Storage)	85

Table 8.11	Allowable Spans for Cold-Formed Steel Ceiling Joists, Two Equal Spans

Without Bearing Stiffeners (Limited Attic Storage)	86

Table 8.12	Allowable Horizontal Rafter Spans	87

Table 8.13	Wind Speed to Equivalent Snow Load Conversion	88

Table 8.14	Uplift Loads on Roof-to-Wall Connections for Selection of Roof Tie-Downs	89

LIST OF FIGURES

Figure 1.1	C-Shaped Member Configuration	3

Figure 1.2	In-Line Framing Detail	5

Figure 1.3	Track Section Configuration	6

Figure 1.4	Schematic of Typical Steel Framed Building	8

Figure 2.1	C-Shaped Member Dimensions	9

Figure 2.2	Track Section Dimensions	10

Figure 2.3	Floor and Ceiling Joist Web Holes	13

Figure 2.4	Holes in Studs and Other Structural Members	13

Figure 2.5	Joist Web Hole Patch	16

Figure 2.6	Stud Web Hole Patch	17

Figure 2.7	Bearing Stiffener	18

Figure 5.1	Steel Floor Construction	23

Figure 5.2	Steel Floor Bracing 	24

Figure 5.3	Floor to Exterior Load Bearing Wall Connection	25

Figure 5.4	Floor to Wood Sill Connection	25

Figure 5.5	Floor to Foundation Connection	26

Figure 5.6	Cantilevered Floor to Foundation Connection	26

Figure 5.7	Cantilevered Floor to Wood Sill Connection	27

Figure 5.8	Cantilevered Floor to Exterior Load Bearing Wall Connection	28

Figure 5.9	Continuous Span Joist Supported on an Interior Load Bearing

Wall	28

Figure 5.10	Lapped Joist Supported on Interior Load Bearing Wall	29

Figure 5.11	Track Splice	29

Figure 5.12	Floor Opening	30

Figure 5.13	Floor Header to Trimmer Connection	30

Figure 6.1	Steel Wall Construction	39

Figure 6.2	Wall to Foundation Connection	40

Figure 6.3	Wall to Wood Sill Connection 	40

Figure 6.4	Stud Bracing with Sheathing Material 	41

Figure 6.5	Stud Bracing with Strapping Only 	41

Figure 6.6	Stud Bracing with Strapping and Sheathing Material  	42

Figure 6.7	Track Splice	42

Figure 6.8	Corner Framing	43

Figure 6.9	Box Beam Header Detail	44

Figure 6.10	Back-to-Back Header Detail	44

Figure 6.11	Structural Sheathing Fastening Pattern	45

Figure 7.1	Typical Interior Non-Load Bearing Wall Detail	69

LIST OF FIGURES  (Continued)

Figure 8.1	Steel Roof Construction	73

Figure 8.2	Heel Joint Connection	74

Figure 8.3	Ridge Member Connection	74

Figure 8.4	Bearing Stiffener	75

Figure 8.5	Spliced Ceiling Joists	75

Figure 8.6	Roof or Ceiling Opening	76

Figure 8.7	Header to Trimmer Detail	76

Executive Summary

The Prescriptive Method for Residential Cold-Formed Steel Framing (Prescriptive Method) was developed as a guideline for the construction of one- and two-family residential dwellings using cold-formed steel framing.  It provides a complete prescriptive approach to build typical homes with cold-formed steel framing.  This document standardizes the basic cold-formed steel members, provides labeling guidelines, and gives minimum corrosion protection requirements.  It also includes floor joist span tables, ceiling joist span tables, rafters span tables, wall stud tables, wall bracing requirements, and connection requirements.  The requirements are supplemented with construction details where required. A commentary is available under separate cover and serves the following purposes:

(	documentation of rationale and decisions behind various provisions;

(	guidance on the use of the provisions; and

(	documentation of engineering calculations and judgments.

This second edition includes improvements upon the previous edition in the following areas:

(	Added and revised definitions;

(	Expanded hole (web penetration) sizes for floor joists;

(	Revised hole (web penetration) spacing requirements for studs;

(	Wall bracing requirements for high wind and seismic conditions, (See Commentary);

(	Roof Uplift (tie-down) requirements;

(	New wall stud tables for 50 ksi steels;

(	New header table for bottom story of a two-story building with center load bearing

beam;

(	New floor and wall anchoring details;

(	Added details for non-load bearing walls; and,

(	Ceiling joist tables not requiring web stiffeners.

The Prescriptive Method is consistent with the intent of current U.S. building code provisions, engineering standards, and industry specifications, but it is not written as a regulatory document.  To the greatest extent possible, the Prescriptive Method is written in a style to facilitate code adoption.

INTRODUCTION

The Prescriptive Method for Residential Cold-Formed Steel Framing (Prescriptive Method) is provided as a guideline to facilitate the use of cold-formed steel framing in the construction of one- and two-family residential dwellings.  The second edition of the Prescriptive Method expands on and enhances the requirements of the provisions of the first edition.  It provides a complete prescriptive approach to build typical homes with cold-formed steel framing; therefore, engineering will not be necessary for most applications.  The provisions in this document were developed by applying accepted engineering practices.  It is intended to be compatible with building code provisions, but it is not written as a regulatory instrument.  However, users of this document should verify its compliance with local code requirements.  The user is advised to refer to the applicable building code requirements where the provisions of this document are not applicable or where engineered design is called out.

1.0	GENERAL

1.1	Purpose

The purpose of this document is to provide prescriptive requirements for the construction of residential buildings framed with cold-formed steel.  These provisions include definitions, span tables, fastener schedules, and other related information appropriate for use by home builders, design professionals, and building code officials.

1.2	Approach

These requirements are based primarily on the American Iron and Steel Institute’s (AISI) Specification for the Design of  Cold-Formed Steel Structural Members [1] for member strength, the provisions for building loads from the American Society of Civil Engineers’ (ASCE) Minimum Design Loads for Buildings and Other Structures [2], the Standard Building Code [3], the Uniform Building Code [4], and the BOCA National Building Code [5].

These provisions are intended to represent sound engineering and construction practice.  This document is not intended to restrict the use of good judgment or exact engineering analysis of specific applications which may result in improved designs and economy.  A commentary documenting the rationale for and the derivation of the requirements contained in this document is available under a separate cover [6].

1.3	Scope

These provisions apply to the construction of detached one- or two-family dwellings, townhouses, and other attached single-family dwellings not more than two stories in height using in-line framing practices.  Steel-framed construction in accordance with this prescriptive method shall be limited by the applicability limits set forth in Table 1.1.  The limitations are intended to define an appropriate use of this document for a majority of one- and two-family dwellings.  Intermixing of these provisions with other construction materials, such as wood, in a single structure shall be in accordance with the applicable building code requirements for that material and the applicability limits set forth in Table 1.1.

Table 1.1

Applicability Limits

| ATTRIBUTE | LIMITATION |
| --- | --- |
| General |
| Building Dimension |

Maximum width 1 is 36 feet (11 m)

| Maximum length 2 is 60 feet (18 m) |
| --- |
| Number of Stories | 2 story |
| Design Wind Speed | 110 mph maximum (177 km/sec) fastest-mile wind speed [ except as noted for wall bracing] 3 |
| Wind Exposure |

Exposures C  (open terrain)

| Exposures A/B (suburban/wooded) |
| --- |
| Ground Snow Load | 70 psf (3.35 kN/m2) maximum ground snow load |
| Seismic Zone | Zone 4 maximum [ except as noted for wall bracing] 3 |
| Floors |
|  | Floor dead load | 10 psf (0.48 kN/m2) maximum |

Floor  live load

First floor

Second floor (sleeping rooms)

40 psf (1.92 kN/m2) maximum

| 30 psf (1.44 kN/m2) maximum |
| --- |
| Cantilever | 24 inches (610 mm) maximum |
| Walls |
|  | Wall dead load | 10 psf (0.48 kN/m2) maximum |
| Load bearing wall height | 10 feet (3 m) maximum |
| Roofs |

Roof dead load

12 psf (0.48 kN/m2) maximum total load

| [7 psf (0.34 kN/m2) maximum for roof covering only] |
| --- |
| Roof live load | 70 psf (3.35 kN/m2) maximum ground snow load |
| Ceiling dead load | 5 psf (0.24 kN/m2) maximum |
| Roof slope | 3:12 to 12:12 |
| Rake overhang | 12 inches (305 mm) maximum |
| Soffit overhang |

24 inches (610 mm) maximum

Attic live load  (for attics with storage)

Attic live load (for attics without storage)

20 psf (0.96 kN/m2) maximum

10 psf (0.48 kN/m2) maximum

For SI:  1 inch = 25.4 mm, 1 psf = 0.0479 kN/m2,  1 mph = 1.61 km/hr = 0.447 m/sec,  1 foot = 0.3 m.

1	Building width is in the direction of horizontal framing members supported by the wall studs.

2	Building length is in the direction perpendicular to floor joists, ceiling joists, or roof trusses.

3	See the Commentary for additional guidance on wall bracing requirements in high wind and

seismic conditions [6].

1.4	Definitions

Accepted Engineering Practice: An engineering approach that conforms with accepted principles, tests, technical standards, and sound judgment.

Approved:  Approval by a code official or design professional.

Attic:  The enclosed space between the ceiling joists of the top floor and the roof rafters of a building not intended for occupancy, but sometimes used for storage.

Axial Load:  The longitudinal force acting on a member.  Examples are the gravity loads carried by columns or studs.

Blocking:  Solid block or piece of material placed between structural members to provide lateral bracing as in bridging and/or edge support for sheathing.

Bridging:  Cross bracing or blocking placed between joists to provide lateral support.

Buckling: A kink, wrinkle, bulge, or otherwise loss of the original shape of a member due to compressive, bending, bearing, or shear loads.

Ceiling Joist: A horizontal structural framing member which supports a ceiling and attic loads.

C-Shape:  A basic cold-formed steel shape used for structural framing members (such as studs, joists, headers, beams, girders, and rafters).  The name comes from the member's "C" shaped cross-sectional configuration consisting of a web, flange and lip.  It is also called a “C-section”.  Figure 1.1 shows this cross-section and defines the different parts of the C-Shape. Web depth measurements are taken to the outside of the flanges. Flange width measurements also use outside dimensions.

Figure 1.1	C-Shaped Member

Configuration

Clip Angle:  An L-shaped short piece of metal (normally with a 90 degree bend).  It is typically used for connections.

Cold-forming:  A process where light-gauge steel members are manufactured by (1) press-braking blanks sheared from sheets or cut length of coils or plates, or by (2) continuous roll forming of cold- or hot-rolled coils of sheet steel; both forming operations are performed at ambient room temperature, that is, without any addition of heat such as would be required for hot forming.

Cripple Stud:  A stud that is placed between a header and a window sill (or jamb) or a window sill and a bottom track to provide a backing to attach finishing and sheathing material.

Design Professional: An architect or engineer, registered or licensed to practice professional architecture or engineering, as defined by the statutory requirements of the laws of the state in which a project is to be constructed.

Endwall:  The exterior wall of a building which is perpendicular to the roof ridge and parallel to floor framing, roof rafters or trusses.  Normally the shorter dimension of a rectangular building’s footprint.

Facia:  A track member applied to the rafter ends as an edge member for attachment of roof sheathing, exterior finishes, or gutter.

Flange:  The part of a C-Shape or track that is perpendicular to the web.

Flat Strap:  Sheet steel cut to a specified width without any bends.  Typically used for bracing and transfer of loads by tension.

Floor Joist: A horizontal structural framing member that supports floor loads.

Header: A horizontal built-up structural framing member used over wall or roof openings to transfer loads above the opening to adjacent vertical framing members.

In-Line Framing:  Framing method where all vertical and horizontal load carrying members are aligned.  Refer to Figure 1.2.

Jack Stud:  A vertical structural member that does not span the full height of the wall and provides bearing for headers.  Sometimes referred to as trimmer studs.

King Stud: A vertical structural member that spans the full height of the wall and supports vertical loads and lateral loads. Usually located at both ends of a header adjacent to the jack studs.

Lip:  The part of a C-Shape which extends from the flange at the open end.  The lip increases the strength characteristics of the member and acts as a stiffener to the flange.

Figure 1.2	In-Line Framing Detail

Loads, Live and Dead:  Dead loads are the weight of the walls, partitions, framing, floors, ceilings, roofs, and all other permanent construction entering into and becoming a part of a building. Live loads are transient and sustained loads usually created by people and furnishing, respectively.

Material Properties (steel):  The chemical, mechanical, and physical properties of steel before or after the cold-forming process.

Material Thickness (steel):  The base metal thickness excluding any protective coatings. Thickness is now commonly expressed in mils (1/1000 of an inch).

Metallic Coated Steel: Steel that has a metallic coating for protection against corrosion.  The level of protection provided is measured by the weight of the metallic coating applied to the surface area of the steel.  Typical metallic coatings are galvanizing, galvalume, or galfan which are zinc based.

Mil: A unit of measurement used in measuring the thickness of thin steel elements. One mil equals 1/1000 of an inch (e.g. 33 mil = 0.033 inch).

Multiple Span: The span made by a continuous member having intermediate supports.

Non-Load Bearing Walls  (Non-structural walls):  Refer to Walls.

Punchout (or hole) :  An opening in the web of a steel framing member allowing for the installation of plumbing, electrical, and utilities.  A punchout or hole may be made during the manufacturing process or in the field with a hand punch, hole saw, or other suitable tool.

Rafter: A structural framing member (usually sloped) which supports roof loads.

Rake Overhang:  The horizontal projection of the roof measured from the outside face of a gable endwall to the outside edge of the roof.

Ridge:  The horizontal line formed by the joining of the top edges of two sloping roof surfaces.

Seismic Zone:	Seismic Zones designate areas with varying degrees of seismic risk and associated seismic design parameters (i.e. effective peak ground acceleration).  Seismic Zones 1, 2, 3, and 4 correspond to effective peak ground acceleration of 0.1g, 0.2g, 0.3g, and 0.4g, respectively (1g is the acceleration of the earth's gravity at sea level).

Shearwall:  A vertical wall assembly capable of resisting lateral forces to prevent racking from wind or seismic loads acting parallel to the plane of the wall.

Sidewall:  The exterior wall of a building parallel to the roof ridge which supports roof rafters or trusses.

Single Span:  The span made by one continuous structural member without any intermediate supports.

Span: The clear horizontal distance between bearing supports.

Structural Sheathing: The covering (e.g. plywood or oriented strand board) used directly over structural members (e.g. studs or joists) to distribute loads, brace walls, and generally strengthen the assembly.

Stud: Vertical structural element of a wall assembly which supports vertical loads and/or transfers lateral loads.

Track:  Used for applications such as

top and bottom plate for walls and

band or rim joists for flooring systems.

A track has a web and two flanges, but

no lips. Track web depth measurements

are taken to the inside of the flanges.

Refer to Figure 1.3.

Figure 1.3       Track Section Configuration

Truss: 	An engineered structural component designed to efficiently carry its own weight and superimposed design loads.  The truss members form a triangular structural framework.

Walls:

Structural or load bearing: Wall systems subject to loads that exceed the limits for a non-structural system (e.g. wall studs).

Non-Structural or  non-load bearing: Wall systems that are limited to 10 psf (0.479 kN/m2) maximum lateral (transverse) load and/or limited, exclusive of sheathing materials, to 100 pounds (450 N) per lineal foot (0.3 m) or 200 pounds (900 N) maximum superimposed vertical load per member (e.g. interior partitions).

Web:  The part of a C-Shape or track that connects the two flanges.

Web Crippling:  The localized permanent (inelastic) deformation of the web member subjected to concentrated load or reaction at bearing supports.

Web Stiffener:  Additional material that is attached to the web to strengthen the member against web crippling.  Also called a bearing stiffener.

Wind Exposure:  Wind exposure is determined by site conditions that affect the actual wind speeds experienced at a given site.  For the purpose of this document, Exposures A/B represent urban or suburban areas or wooded terrain and Exposure C represents open terrain with scattered obstructions.

Wind Speed:  Wind speed is the design wind speed related to winds that are expected to be exceeded once every 50 years at a given site (i.e. 50 year-return period).  Wind speeds in this document are given in units of miles per hour (mph) by "fastest-mile" measurements.

Yield Strength:  A characteristic of the basic strength of the steel material.   It is the highest unit stress that the material can endure before permanent deformation occurs as measured by a tensile test in accordance with ASTM A 370 [7].

Figure 1.4 is provided as an overall view of residential steel framing and the basic components.

1

Figure 1.4	Schematic of Typical Steel Framed Building

2.0	MATERIALS, SHAPES, AND STANDARD SIZES

2.1	Types of Cold-Formed Steel

2.1.1	Structural Members

Load bearing steel framing members shall be cold-formed to shape from structural quality sheet steel complying with the requirements of one of the following:

1	ASTM A 653 [8]:  Grades 33, 37, 40, & 50 (Class 1 and 3); or

2.	ASTM A 792 [9]:  Grades 33, 37, 40, & 50A; or

3.	ASTM A 875 [10]:  Grades 33, 37, 40, & 50 (Class 1 and 3); or

4.	Steels that comply with ASTM A 653 [8], except for tensile and elongation requirements, shall be permitted provided the ratio of tensile strength to yield point is at least 1.08 and the total elongation is at least 10 percent for a two-inch gage length or 7 percent for an eight-inch gauge length.

2.1.2	Non-Structural Members

Non-structural members shall comply with ASTM C-645 [12] and Section 7.0.

2.2	Physical Dimensions

Cold-formed structural steel members shall comply with Figure 2.1 and the dimensional requirements specified in Table 2.1.  In addition, tracks shall comply with Figure 2.2 and shall have a minimum of 1-1/4 inch (32 mm) flanges.  Members with different geometrical shapes shall not be used with these provisions without the approval of a design professional.  Dimensional Tolerances shall be in accordance with ASTM C955 [11] for load bearing members and ASTM C645 [12] for non-load bearing members.

Figure 2.1	C-Shaped Member 			    Dimensions

Figure 2.2	Track Section Dimensions

Table 2.1

Cold-Formed Steel Member Sizes

Nominal

| Member Size | Industry Designator1 | Web Depth (inches) | Minimum Flange Width (inches) | Maximum Flange Width (inches) |
| --- | --- | --- | --- | --- |

Minimum

Lip Size

| (inches) |
| --- |
| 2 x 4 | 350S162-t | 3.5 | 1.625 | 2 | 0.5 |
| 2 x 6 | 550S162-t | 5.5 | 1.625 | 2 | 0.5 |
| 2 x 8 | 800S162-t | 8 | 1.625 | 2 | 0.5 |
| 2 x 10 | 1000S162-t | 10 | 1.625 | 2 | 0.5 |
| 2 x 12 | 1200S162-t | 12 | 1.625 | 2 | 0.5 |

For SI:  1 inch = 25.4 mm.

1	"t" is the uncoated material thickness in mils.  "S" indicates a C-Shaped member for stud and joist 	applications.  Track sections shall use the designator "T" instead of "S".

2.3	Uncoated Material Thickness

The material thickness of steel framing members in their end-use shall meet or exceed the minimum (uncoated) thickness values given in Table 2.2.

Table 2.2

Minimum Thickness of Cold-Formed Steel Members

Designation

(mils)

Minimum

Steel Thickness

(inches)

Reference

Gauge

| Number |
| --- |
| 18 | 0.018 | 25 |
| 27 | 0.027 | 22 |
| 33 | 0.033 | 20 |
| 43 | 0.043 | 18 |
| 54 | 0.054 | 16 |
| 68 | 0.068 | 14 |
| 97 | 0.097 | 12 |

For SI:  1 inch = 25.4 mm,  1 mil = 0.0254 mm.

2.4	Bend Radius

The maximum bend radius shall be the greater of  3/32 inch (2.4 mm) or two times the material thickness (2t).

2.5	Yield Strength

The yield strength of steel shall be determined in accordance with ASTM A370 [7].  Unless otherwise specified as 50 ksi (345 MPa), the minimum yield strength (or yield point) of cold-formed steel for C-Shapes, tracks, flat straps, and other members shall be 33 ksi (228 MPa).

2.6	Corrosion Protection

Cold-formed structural steel framing members identified in accordance with this document shall have a minimum metallic coating complying with Table 2.3.

Table 2.3

Minimum Coating Requirements

| Steel Component | Reference ASTM Standard |
| --- | --- |

A653 / A 653M

[8]

A 792 / A 792M

[9]

A 875 / A 875M

| [10] |
| --- |
| Structural | G60 | AZ50 | GF60 |
| Non- structural | G40 | AZ50 | GF45 |

Other approved metallic coatings shall be permitted provided the alternate coatings can be demonstrated to have a corrosion resistance that is equal to or greater than the corresponding hot-dipped galvanized coatings (i.e. G40 and G60) and provide protection at cut edges, scratches, etc., by cathodic or sacrificial protection.

The minimum coating designations shown in Table 2.3 assume normal exposure conditions and construction practices.  Cold formed steel members used in buildings located in harsh environments (e.g. coastal areas) may require greater corrosion protection (e.g. G90).

Steel framing members shall be located within the building envelope and adequately shielded from direct contact with moisture from the ground or the outdoor climate.

2.6.1	Compatibility With Other Metals

Copper materials shall not be used in direct contact with metallic coated steel members or components.  Metallic coated steel shall not be embedded in concrete, unless approved for that purpose.

2.7	Web Holes

Holes in webs (or punchouts) of floor and ceiling joists shall comply with the requirements of Figure 2.3 and Table 2.4.  Holes in webs of studs, headers, rafters, and other structural steel members shall comply with the requirements of Figure 2.4 and Table 2.5.  Holes shall be permitted only along the centerline of the web of the framing member.  Holes with minimum edge (or end) distances violating the values shown in Tables 2.4 or 2.5 shall be patched in accordance with Section 2.8.

Figure 2.3	Floor and Ceiling Joist Web Holes

Figure 2.4	   Holes in Studs and Other Structural Members

Table 2.4

Maximum Hole Dimensions and Spacing in Floor & Ceiling Joist Webs

Nominal Member Size

Maximum Hole Depth 1

(inches)

Maximum Hole Length 2

(inches)

Minimum Hole Spacing 3

(inches)

Minimum Edge Distance 4

| (inches) |
| --- |
| 2 x 6 x 33 |
| 2 x 6 x 43 |
| 2 x 6 x 54 | 2 | 5.25 | 16.5 | 3 |
| 2 x 6 x 68 |
| 2 x 6 x 97 |
| 2 x 8 x 33 | 1.5 | 4 | 24 | 10 |
| 2 x 8 x 43 |
| 2 x 8 x 54 | 3 | 6 | 24 | 3.5 |
| 2 x 8 x 68 |
| 2 x 8 x 97 |
| 2 x 10 x 43 | 1.5 | 4 | 24 | 10 |
| 2 x 10 x 54 |
| 2 x 10 x 68 | 4 | 6 | 24 | 3.5 |
| 2 x 10 x 97 |
| 2 x 12 x 43 | 1.5 | 4 | 24 | 10 |
| 2 x 12 x 54 |
| 2 x 12 x 68 | 4.75 | 6 | 24 | 3.5 |
| 2 x 12 x 97 |

For SI:	1 inch = 25.4 mm

1		The dimension of the hole measured across the depth of the joist web.

2		The dimension of the hole measured along the length of the joist.

3		Spacing is the center-to-center distance between holes.

4		Edge distance is measured from the edge of the hole to the edge of bearing support.

Table 2.5

Maximum Hole Dimensions and Spacing for Structural Members

Other Than Floor & Ceiling Joists

Nominal Member Size

Maximum Hole Depth 1

(inches)

Maximum Hole Length 2

(inches)

Minimum Hole Spacing 3

(inches)

Minimum End Distance 4

| (inches) |
| --- |
| 2 x 4 x 33 |
| 2 x 4 x 43 |
| 2 x 4 x 54 | 1.5 | 4 | 7 | 10 |
| 2 x 4 x 68 |
| 2 x 4 x 97 |
| 2 x 6 x 33 |
| 2 x 6 x 43 |
| 2 x 6 x 54 | 1.5 | 4 | 11 | 10 |
| 2 x 6 x 68 |
| 2 x 6 x 97 |
| 2 x 8 x 33 |
| 2 x 8 x 43 |
| 2 x 8 x 54 | 1.5 | 4 | 16 | 10 |
| 2 x 8 x 68 |
| 2 x 8 x 97 |
| 2 x 10 x 43 |
| 2 x 10 x 54 | 1.5 | 4 | 20 | 10 |
| 2 x 10 x 68 |
| 2 x 10 x 97 |
| 2 x 12 x 43 |
| 2 x 12 x 54 | 1.5 | 4 | 24 | 10 |
| 2 x 12 x 68 |
| 2 x 12 x 97 |

For SI:	1 inch = 25.4 mm

1		The dimension of the hole measured across the depth of the member.

2		The dimension of the hole measured along the length of the member.

3		Spacing is the center-to-center distance between holes.

4		End distance is measured from the edge of the hole to the end of the member.

2.8	Cutting, Notching, and Hole Patching

Flanges and lips of  joists, studs, headers, rafters, ceiling joists, and other structural members shall not be cut or notched.  Web holes violating the minimum edge (or end) distance, maximum hole depth, maximum hole length, or minimum spacing requirements set forth in Tables 2.4 and 2.5 shall be patched with a solid steel plate, stud, joist, or track section in accordance with Figures 2.5 or 2.6.  The steel patch shall be of a thickness equivalent to or greater than the receiving member and shall extend a minimum of 1-inch (25 mm) beyond all edges of the hole.  The steel patch shall be fastened to the web of the receiving member with #8 screws (minimum) spaced no greater than 1-inch (25 mm) center-to-center along the edges of the patch with minimum edge distance of 1/2 inch (13 mm).

Structural members shall be replaced when web holes exceed the following size limits:

the depth of the hole, measured across the web, exceeds half the depth of the web; and,

the length of the hole measured along the web, exceeds 6 inches (152 mm) or the depth of the web, whichever is greater.

Figure 2.5	Joist Web Hole Patch

Figure 2.6	Stud Web Hole Patch

2.9	Bearing Stiffeners

A bearing stiffener (also referred to as web stiffener) shall be fabricated from a minimum 33 mil (0.836 mm) C-Shaped member or 43 mil (1.09 mm) track section.  Each stiffener shall be fastened to the web of the member it is stiffening with a minimum of four #8 screws equally spaced as shown in Figure 2.7. Bearing stiffeners shall extend across the depth of the web and shall be installed on one side of the member.

2.10	Clip Angles

Clip angles shall be a minimum of 2 inches x 2 inches by 33 mil (51 mm x 51 mm x 0.84 mm), unless otherwise noted.  All clip angle materials shall comply with Sections 2.1.1, 2.5, and 2.6.

Figure 2.7 	    Bearing Stiffener

2.11	Fasteners

Fasteners shall comply with Sections 2.11.1 and 2.11.2.  Other fastening techniques, such as the use of pneumatically driven fasteners, powder actuated fasteners, crimping, clinching, or welding, shall be permitted when approved.

2.11.1	Screws

For all connections, screws shall extend through the steel a minimum of three exposed threads. Screws shall penetrate individual components of connections without causing permanent separation between the components.  Screws shall be installed in a manner such that the threads and/or holes are not stripped.  All self-drilling tapping screws, on exterior building surfaces, shall have a Type II coating in accordance with ASTM B633 [13] or equivalent corrosion protection.

Screws for steel-to-steel connections shall be installed with a minimum edge distance and center to center spacing of 1/2 inch (13 mm), and shall be self-drilling tapping in compliance with SAE J78 [14]. The minimum screw size for steel to steel connections shall comply with Table 2.6.

Structural sheathing shall be attached to steel framing (i.e. studs and joists) with minimum #8 self-drilling tapping screws in compliance with SAE J78 [14].  Screws attaching structural sheathing to steel joists and wall framing shall have a minimum head diameter of 0.292 inch (7 mm) with countersunk heads, shall be installed with a minimum edge distance of 3/8 inch (9 mm) and shall comply with Table 2.6.  Gypsum board shall be attached to steel joists or steel wall framing with minimum #6 screws conforming to ASTM C 954 [15] and shall be installed in accordance with the applicable building code requirements for interior wall and ceiling finishes.

Table  2.6

Minimum Screw Sizes For Steel-to-Steel

and Structural Floor Sheathing-to-Steel Connections

| Point Style | Minimum Screw Size | Total Thickness of Steel 1 (inches) |
| --- | --- | --- |
| 2 | # 8 | 0.100 max. |
| 2 | # 10 | 0.110 max. |
| 2 | # 12 | 0.140 max. |
| 3 | # 8 | 0.140 max. |
| 3 | # 10 | 0.175 max. |
| 3 | # 12 | 0.210 max. |

For SI:	1 inch = 25.4 mm.

1	The combined thickness of all connected steel members.

2.11.2	Bolts

Bolts shall meet or exceed the requirements of ASTM A307 [16].  Bolts shall be installed with nuts and washers.  Center-to-center spacing of bolt holes connecting sheet metal material to concrete shall be a minimum of three bolt diameters.  Distance from the center of the bolt hole to the edge of the connecting member shall not be less than one and one-half bolt diameters.

3.0	LABELLING

Load-bearing steel framing members shall have a legible label, stamp, stencil, or embossment, spaced at a minimum of 48 inches on center along the length of the member, with the following minimum information:

a.	Manufacturer's identification;

b.	Minimum uncoated steel thickness in decimal inches (example 0.043 in.);

c.	Minimum coating designation; and,

d.	Minimum yield strength in kips per square inch (ksi).

An example of an acceptable label :  ABC 0.043 G60 33 ksi

4.0	FOUNDATION

The building foundation shall comply with the applicable building code.  Steel framing shall be attached to the foundation structure according to the requirements of Sections 5 and 6 of this document.  Foundation anchor bolts shall be located not more than 12 inches (305 mm) from corners or the termination of bottom tracks (e.g. at door openings or corners).

5.0		STEEL FLOOR FRAMING

5.1		Floor Construction

Cold-formed steel framing members shall comply with the provisions of Section 2.0.  Steel floors shall be constructed in accordance with this section and Figure 5.1.

5.1.1	Applicability Limits

The applicability limits of Section 1.3 and Table 1.1 shall apply.

5.1.2	In-Line Framing.

Load bearing steel floor framing, wall framing, and ceiling/roof framing shall be constructed in-line with the vertical load bearing members (i.e. studs) located below.  A maximum tolerance of 3/4 inch (19 mm) between the centerlines of the in-line members shall be permitted in accordance with Figure 1.2.

5.2		Floor to Foundation or Bearing Wall Connection

Cold-formed steel floor framing shall be anchored to foundations, wood sills, or load bearing walls in accordance with Table 5.1 and Figures 5.1 through 5.10.  Fastening of steel joists to other framing members shall be in accordance with Table 5.2.

5.3		Allowable Joist Spans

The clear span of cold-formed steel floor joists shall not exceed the limits set forth in Table 5.3 for single spans and Table 5.4 for multiple spans.  When continuous joist members are used for multiple spans, the interior bearing supports shall be located within two feet (0.6 m) of mid-span of the steel joists, and the individual spans shall not exceed the applicable spans in the table.  Floor joists shall have a bearing support length of not less than 1.5 inches (38 mm) for exterior wall supports and 3.5 inches (89 mm) for interior wall supports.  Bearing stiffeners shall be installed at each joist bearing location in accordance with Section 2.9. The thickness of joist tracks shall be a minimum of 33 mils (0.84 mm) thick except when used as part of floor header or trimmer in accordance with Section 5.7.

5.4		Joist Bracing

The top flanges of floor joists shall be laterally braced by the application of floor fastened to the joists in accordance with Table 5.2.  Floor joists with spans that exceed 12 feet (3.7 m) shall have the bottom flanges laterally braced in accordance with one of the following:

Gypsum board installed with minimum #6 screws in accordance with the

applicable building code, or

Continuous steel strapping installed in accordance with Figure 5.1 and 5.2.  Steel straps shall be at least 1-1/2 inches (38 mm) in width and 33 mils (0.84 mm) in thickness.  Straps shall be fastened to the bottom flange of each joist with at least one #8 screw and shall be fastened to blocking with at least two #8 screws. Blocking or bridging (X-bracing) shall be installed between joists at a maximum spacing of 12 feet (3.7m) measured along the continuous strapping (perpendicular to the joist run).  Blocking or bridging shall also be located at the termination of all straps.

5.5  	Floor Cantilevers

Floor cantilevers for the second floor of a two-story building or the first floor of a one-story building shall not exceed 24 inches (610 mm) as illustrated in Figure 5.1.  Cantilevers shall support interior floor loading only.  Cantilevers, not exceeding 24 inches (610 mm) and supporting one floor and roof (first floor of a two story building), shall be permitted provided that all cantilevered joists are doubled (nested or back-to-back).  The doubled cantilevered joists shall extend a minimum of 6 feet (1.8 m) toward the inside and shall be fastened with a minimum of two #8 screws spaced at 24 inches (610 mm) on center through the webs (for back-to-back) or flanges (for nested joists).  Approved design is required for cantilevered areas supporting uniform live loads greater than 40 psf (1.92 kN/m2).

5.6	Splicing

Joists and other structural members shall not be spliced without an approved design.  Splicing of tracks shall conform with Figure 5.11.

5.7	Framing of Floor Openings

Openings in floors shall be framed with header and trimmer joists.  Header joist spans shall not exceed 8 feet (2.4 m) in length.  Header and trimmer joists shall be fabricated from joist and track sections, which shall be of a minimum size and thickness as the adjacent floor joists and shall be installed in accordance with Figures 5.1, 5.12, and 5.13.  Each header joist shall be connected to trimmer joists with a minimum of four 2 inch x 2 inch (51 mm x 51 mm) clip angles.  Each clip angle shall be fastened to both the header and trimmer joists with four #8 screws evenly spaced on each leg of the clip angle. The clip angles shall have a thickness not less than that of the floor joist.

5.8		Floor Trusses

Cold-formed steel floor trusses shall be designed, braced, and installed in accordance with an approved design.  Truss members shall not be notched, cut, or altered in any manner unless by an approved design.  All trusses shall be aligned with load carrying members (i.e. studs) in the wall.  Refer to AISI publication RG-9518 [17] “Design Guide For Cold-Formed Steel Trusses” for additional guidance.

Figure 5.1		Steel Floor Construction

Figure 5.1 (cont’d)	  	Steel Floor Construction

Figure 5.2		Steel Floor Bracing

Figure  5.3		Floor to Exterior Load Bearing Wall Connection

Figure 5.4		Floor to Wood Sill Connection

Figure 5.5		Floor to Foundation Connection

Figure 5.6		Cantilevered Floor to Foundation Connection

Figure 5.7		Cantilevered Floor to Wood Sill Connection

Figure 5.8		Cantilevered Floor to Exterior Load Bearing Wall Connection

Figure 5.9		Continuous Span Joist Supported on an Interior Load Bearing Wall

Figure 5.10		Lapped Joist Supported on Interior Load Bearing Wall

Figure 5.11		Track Splice

Figure 5.12		Floor Opening

Figure 5.13		Floor Header to Trimmer Connection

Table 5.1

Floor to Foundation or Bearing Wall Connection Requirements

| Framing Condition | Wind Speed (mph), Exposure, and Seismic Zones 1,2 |
| --- | --- |
|  | Up to 90 A/B or 70 C or Seismic Zones 0, 1, 2, & 3 | Up to 110 A/B or 90 C or Seismic Zone 4 | Up to 110 C |
| Floor joist to wall track of exterior steel load bearing wall per Figure 5.3 | 2 - #8 screws | 3- #8 screws | 4- #8 screws |
| Joist track or end joist to bearing wall top track per Figure 5.3 | 1- #8 screw at 24" o.c | 1- #8 screw at 24" o.c. | 1- #8 screw at 12" o.c. |
| Floor joist track or end joist to wood sill per Figure 5.4 | Steel plate spaced at 4’ o.c. with 4-No. 8 screws and 4-10d or 6-8d common nails | Steel plate spaced at 2’ o.c. with 4-No. 8 screws and 4-10d or 6-8d common nails | Steel plate spaced at 1’ o.c. with 4-No. 8 screws and 4-10d or 6-8d common nails |
| Floor joist track or end joist to foundation per Figure 5.5 | 1/2" minimum diameter anchor bolt and clip angle spaced at 6’ o.c. with 8- #8 screws | 1/2" minimum diameter anchor bolt and clip angle spaced at 4’ o.c. with 8- #8 screws | 1/2" minimum diameter anchor bolt and clip angle spaced at 2’ o.c. with 8- #8 screws |
| Cantilevered joist to foundation per Figure 5.6 | 1/2" minimum diameter anchor bolt and clip angle spaced at 6’ o.c. with 8- #8 screws | 1/2" minimum diameter anchor bolt and clip angle spaced at 4’ o.c. with 8- #8 screws | 1/2" minimum diameter anchor bolt and clip angle spaced at 2’ o.c. with 8- #8 screws |
| Cantilevered joist to wood sill per Figure 5.7 | Steel plate spaced at 4’ o.c. with 4-No. 8 screws and 4-10d or 6-8d common nails | Steel plate spaced at 2’ o.c. with 4-No. 8 screws and 4-10d or 6-8d common nails | Steel plate spaced at 1’ o.c. with 4-No. 8 screws and 4-10d or 6-8d common nails |
| Cantilevered joist to wall track per Figure 5.8 | 1/2" minimum diameter anchor bolt and clip angle spaced at 6’ o.c. with 8- #8 screws | 1/2" minimum diameter anchor bolt and clip angle spaced at 4’ o.c. with 8- #8 screws | 1/2" minimum diameter anchor bolt and clip angle spaced at 2’ o.c. with 8- #8 screws |

For SI:	1 inch = 25.4 mm,    1 psf = 0.0479 kN/m2,    1 mph = 1.61 km/hr,  1 foot = 0.3m.

1		Use the highest of the wind speed and exposure or the seismic requirements for a given site.

2		All screw sizes shown are minimum

Table 5.2

Floor Fastening Schedule1

| Description of Building Elements | Number and Size of Fasteners | Spacing of Fasteners |
| --- | --- | --- |
| Floor joist to track of an interior load bearing wall per Figures 5.9 and 5.10 | 2 - #8 screws | Each joist |
| Floor joist to track at end of joist | 2- #8 screws | One per flange or two per bearing stiffener |
| Subfloor sheathing to floor joists | #8 screws2 | 6 inches on center on edges and 10 inches on center at intermediate supports |

For SI:	1 inch = 25.4 mm

1	All screw sizes shown are minimum.

2	Head styles shall be bugle-head, flat-head, or similar with a minimum head diameter of 0.29 inch

(7 mm).

Table  5.3

Allowable Spans For Cold-Formed Steel Floor Joists1,2,3,4

Single Span

33 ksi Steel

| Nominal Joist | 30 psf Live Load |
| --- | --- |
|  | 40 psf Live Load |

Size 5

| S | Spacing (inches) |
| --- | --- |
|  | Spacing (inches) |
|  | 12 | 16 | 24 | 12 | 16 | 24 |
| 2 x 6 x 33 | 11'-7" | 10'-7" | 9'-1" | 10'-7" | 9'-7" | 8'-1" |
| 2 x 6 x 43 | 12'-8" | 11'-6" | 10'-0" | 11'-6" | 10'-5" | 9'-1" |
| 2 x 6 x 54 | 13'-7" | 12'-4" | 10'-9" | 12'-4" | 11'-2" | 9'-9" |
| 2 x 6 x 68 | 14'-6" | 13'-2" | 11'-6" | 13'-2" | 12'-0" | 10'-6" |
| 2 x 6 x 97 | 16'-1" | 14'-7" | 12'-9" | 14'-7" | 13'-3" | 11'-7" |
| 2 x 8 x 33 | 15'-8" | 13'-3" | 8'-10" | 14'-0" | 10'-7" | 7'-1" |
| 2 x 8 x 43 | 17'-1" | 15'-6" | 13'-7" | 15'-6" | 14'-1" | 12'-3" |
| 2 x 8 x 54 | 18'-4" | 16'-8" | 14'-7" | 16'-8" | 15'-2" | 13'-3" |
| 2 x 8 x 68 | 19'-8" | 17'-11" | 15'-7" | 17'-11" | 16'-3" | 14'-2" |
| 2 x 8 x 97 | 21'-10" | 19'-10" | 17'-4" | 19'-10" | 18'-0" | 15'-9" |
| 2 x 10 x 43 | 20'-6" | 18'-8" | 15'-3" | 18'-8" | 16'-8" | 13'-1" |
| 2 x 10 x 54 | 22'-1" | 20'-1" | 17'-6" | 20'-1" | 18'-3" | 15'-11" |
| 2 x 10 x 68 | 23'-8" | 21'-6" | 18'-10" | 21'-6" | 19'-7" | 17'-1" |
| 2 x 10 x 97 | 26'-4" | 23'-11" | 20'-11" | 23'-11" | 21'-9" | 19'-0" |
| 2 x 12 x 43 | 23'-5" | 20'-3" | 14'-1" | 20'-11" | 16'-10" | 11'-3" |
| 2 x 12 x 54 | 25'-9" | 23'-4" | 19'-7" | 23'-4" | 21'-3" | 17'-6" |
| 2 x 12 x 68 | 27'-8" | 25'-1" | 21'-11" | 25'-1" | 22'-10" | 19'-11" |
| 2 x 12 x 97 | 30'-9" | 27'-11" | 24'-5" | 27'-11" | 25'-4" | 22'-2" |

For SI:    1 inch = 25.4 mm,    1 psf = 0.0479 kN/m2,  1 foot = 0.3m.

1		Table provides the maximum clear span in feet and inches.

2		Bearing stiffeners shall be installed at all support points and concentrated loads.

3		Deflection criteria: L/480 for live loads; L/240 for total loads.

4		Floor dead load = 10 psf  (0.479 kN/m2)

5		For actual size refer to Table 2.1.

Table 5.4

Allowable Spans For Cold-Formed Steel Floor Joists1,2,3,4,5,6

Multiple Spans

33 ksi Steel

| Nominal Joist | 30 psf Live Load |
| --- | --- |
|  | 40 psf Live Load |
| Size 7 | Spacing (inches) |
|  | Spacing (inches) |
|  | 12 | 16 | 24 | 12 | 16 | 24 |
| 2 x 6 x 33 | 12'-10" | 10'-6" | 7'-10" | 11'-0" | 9'-0" | 6'-7" |
| 2 x 6 x 43 | 15'-8" | 13'-6" | 11'-0" | 14'-0" | 12'-1" | 9'-10" |
| 2 x 6 x 54 | 17'-7" | 15'-3" | 12'-5" | 15'-9" | 13'-8" | 11'-2" |
| 2 x 6 x 68 | 19'-6" | 17'-2" | 14'-0" | 17'-8" | 15'-4" | 12'-6" |
| 2 x 6 x 97 | 21'-7" | 19'-7" | 16'-8" | 19'-7" | 17'-10" | 14'-11" |
| 2 x 8 x 33 | 12'-9" | 10'-2" | 7'-1" | 10'-9" | 8'-6" | 5'-8" |
| 2 x 8 x 43 | 19'-5" | 16'-8" | 12'-6" | 17'-5" | 14'-3" | 10'-8" |
| 2 x 8 x 54 | 23'-0" | 19'-11" | 16'-3" | 20'-6" | 17'-9" | 14'-6" |
| 2 x 8 x 68 | 25'-10" | 22'-5" | 18'-3" | 23'-2" | 20'-0" | 16'-4" |
| 2 x 8 x 97 | 29'-4" | 26'-7" | 21'-11" | 26'-7" | 24'-0" | 19'-7" |
| 2 x 10 x 43 | 20'-3" | 16'-5" | 12'-1" | 17'-3" | 13'-11" | 10'-2" |
| 2 x 10 x 54 | 25'-6" | 22'-1" | 18'-0" | 22'-10" | 19'-9" | 15'-6" |
| 2 x 10 x 68 | 30'-6" | 26'-5" | 21'-7" | 27'-4" | 23'-8" | 19'-3" |
| 2 x 10 x 97 | 35'-4" | 31'-9" | 25'-11" | 32'-1" | 28'-5" | 23'-2" |
| 2 x 12 x 43 | 19'-8" | 15'-9" | 11'-3" | 16'-7" | 13'-3" | 9'-0" |
| 2 x 12 x 54 | 27'-8" | 23'-9" | 17'-10" | 24'-9" | 20'-4" | 15'-2" |
| 2 x 12 x 68 | 32'-7" | 28'-3" | 23'-0" | 29'-2" | 25'-3" | 20'-7" |
| 2 x 12 x 97 | 41'-3" | 36'-7" | 29'-10" | 37'-5" | 32'-9" | 26'-9" |

For SI:    1 inch = 25.4 mm,    1 psf = 0.0479 kN/m2,  1 foot = 0.3m.

1		Table provides the maximum clear span in feet and inches to either side of the interior support.

2		Interior bearing supports for multiple span joists shall consist of structural (bearing) walls or beams.

3		Bearing stiffeners shall be installed at all support points and concentrated loads.

4		Deflection criteria: L/480 for live loads; L/240 for total loads.

5		Floor dead load = 10 psf  (0.479 kN/m2)

6		Interior supports shall be located within two feet (610 mm) of mid span provided that each of the

resulting spans does not exceed the appropriate maximum span shown in the table above.

7		For actual size refer to Table 2.1.

6.0	STRUCTURAL STEEL WALL FRAMING

6.1	Wall Construction

Cold-formed steel structural walls shall be constructed in accordance with this section and Figure 6.1. Cold-formed steel framing members shall comply with the provisions of Section 2.0.

6.1.1	Applicability Limits

The applicability limits of section 1.3 and Table 1.1 shall apply.

6.1.1	In-Line Framing

Load bearing steel stud (interior and exterior) walls shall be located directly in-line with joists, trusses or rafters supported above with a maximum tolerance of 3/4-inch (19 mm) between their centerlines in accordance with Figure 1.2.  Interior load bearing steel walls shall be supported on foundations or shall be located directly above a load bearing wall or floor girder.

6.2	Wall to Foundation or Floor Connection

Steel-framed walls shall be anchored to foundations or floors in accordance with Table 6.1 and Figures 6.2 and 6.3.  Uplift connectors shall be provided in accordance with Section 6.10.

6.3	Load Bearing Walls

Load bearing walls shall be constructed in accordance with Figure 6.1.  Steel studs shall be selected from Tables 6.2 through 6.7 for steels with minimum yield strength of 33 ksi (228 MPa) or Tables 6.8 through 6.13 for steels with minimum yield strength of 50 ksi (228 MPa).  Fastening requirements shall be in accordance with Section 2.11 and Table 6.14.  Tracks shall have a minimum steel thickness equivalent to or greater than the wall studs.  Exterior walls with a minimum of 1/2-inch (13 mm) gypsum board installed in accordance with Table 6.14 on the interior surface and wood structural sheathing panels of minimum 7/16-inch (11 mm) thick oriented strand board or 15/32-inch (12 mm) thick plywood installed in accordance with Section 6.8.2 on the outside surface shall be permitted to use the next thinner stud size, from Tables 6.2 through 6.7, but not less than 33 mils (0.84 mm).  Interior load bearing walls with a minimum of 1/2-inch (13 mm) gypsum board installed in accordance with Table 6.14 on both sides of the wall shall be permitted to use the next thinner stud from Tables 6.2 through 6.7, but not less than 33 mils (0.84 mm).  Stud thickness for walls supporting one floor, roof and ceiling are based on a second floor live load of 30 psf (1.44 kN/m2).  Second floor live loads of 40 psf (1.92 kN/m2) shall be permitted provided that the next higher snow load category is used to select the stud size from Tables 6.2 through 6.13.

6.4	Stud Bracing

The flanges of load bearing steel studs shall be laterally braced in accordance with one of the following methods:

1.	Gypsum board or structural sheathing on both sides of load bearing walls installed in accordance with Table 6.14 and Figure 6.4.

2.		Horizontal steel strapping shall be installed in accordance with Figure 6.5 on both sides at mid-height for 8-foot (2.4 m) walls, and third-heights for 9- and 10-foot (2.7 and 3.0 m) walls.  Horizontal steel straps shall be at least 1-1/2 inches in width and 33 mils in thickness (38 mm x 0.84 mm). Straps shall be attached to the flanges of studs with at least one #8 screw.  In-line blocking shall be installed between studs at the termination of all straps and at 12-foot (37 m) intervals along the strap; straps shall be fastened to the blocking with at least two #8 screws.

3.	A combination of methods 1 and 2 in accordance with Figure 6.5.

Adequate temporary or permanent stud bracing shall be provided to resist loads during construction.

6.5	Splicing

Studs and other structural members shall not be spliced without an approved design.  Splicing of tracks shall conform with Figure 6.7.

6.6	Corner Framing

Corner studs and the top track shall be installed in accordance with Figure 6.8.  Other approved corner framing details shall be permitted.

6.7	Headers

Headers shall be installed above wall openings in all exterior walls and interior load bearing walls in accordance with Figures 6.9 and 6.10 and Tables 6.15 through 6.17.  Header spans for house widths between those tabulated may be determined by interpolation.  Headers shall be formed from two, equal sized C-shaped members in a back-to-back or box-type configuration.  Steel tracks used to form the headers shall be of a minimum thickness of 33 mils (0.84 mm).  The number of jack and king studs, installed on each side of the header, shall comply with Table 6.18.  Jack, king, and cripple studs shall be of the same dimension and thickness as the adjacent wall studs.  Headers shall be connected to king studs in accordance with Table 6.19.  One-half of the total number of screws shall be applied to the header and one half to the king stud by use of C-shaped or track member in accordance with Figure 6.9 for box-type headers or a minimum 2-inch x 2-inch (51 mm x 51 mm) clip angle in accordance with Figure 6.10 for back-to-back headers.  The clip angle, track, or C-shape shall extend the depth of the header minus 1/2-inch (13 mm) and shall have a minimum thickness not less than the wall studs.  Jack and king studs shall be interconnected with structural sheathing in accordance with Figures 6.9 and 6.10.  Headers are not required for openings in interior non-load bearing walls.

6.8	Wall Bracing

Exterior steel-framed walls shall be braced with diagonal steel straps or structural sheathing in accordance with Sections 6.8.1 or 6.8.2.

6.8.1	Strap Bracing (X-brace)

Diagonal steel straps or “X-braces” and their connections shall be designed and installed in accordance with an approved design.

6.8.2	Structural Sheathing

Structural sheathing shall be installed on all exterior wall surfaces in accordance with Figure 6.1 and Section 6.8.3.  Structural sheathing panels shall consist of minimum 7/16-inch (11 mm) thick oriented strand board or 15/32-inch (12 mm) thick plywood.  Full height structural sheathing shall extend from the bottom to the top of the wall without interruption by openings.

The minimum length of full height sheathing along exterior wall lines shall be determined in accordance with Table 6.20.  The minimum percentage of full-height sheathing shall include only those sheathed wall sections between openings, which are a minimum of 48 inches (1.1 m) wide.  The minimum percentage of full-height structural sheathing shall be multiplied by 1.10 for 9 foot (2.7m) high walls and multiplied by 1.20 for 10 foot (3.0 m) high walls.  In addition, structural sheathing shall be:

1.	installed with the long dimension parallel to the stud framing (i.e. vertical 				orientation) and shall cover the full vertical height of wall; and,

2.	applied to each end (corners) of each of the exterior walls with a minimum 			48 inch (1.2 m) wide panel.

In conditions where design wind speeds are in excess of 90 mph (144 km/hr) Exposure C or 100 mph (160 km/hr) Exposure A/B and in seismic Zone 3 or greater, the amount and type of structural sheathing shall be determined by accepted engineering practices.  Additional guidance on wall bracing design and requirements for high wind and seismic conditions is found in the Commentary [6].

6.8.3	Structural Sheathing Fastening

All edges and interior areas of structural sheathing panels shall be fastened to framing members and tracks in accordance with Figure 6.11 and Table 6.14.  The panels shall be installed with the long dimension parallel to the stud framing and shall extend the full vertical height of the wall.

6.9	Hold-down Requirements

In conditions where wind speeds are in excess of 90 mph (144 km/hr) Exposure C or 100 mph (160 km/hr) Exposure A/B, and in Seismic Zones 3 and 4, hold-down brackets shall be provided in accordance with an approved design.

6.10	Wind Uplift

In high wind conditions, an approved uplift connector (i.e. strap or bracket) shall be used to attach individual wall studs and king studs to floor joist tracks or directly to foundations below the wall in accordance with Figure 6.1 and Table 6.1.  The wind uplift requirements only apply to walls directly connected to the roof, not to lower story walls of two-story construction.  Uplift requirements for roof-to-wall connections are provided in Section 8.9.

Figure 6.1	Steel Wall Construction

Figure 6.2	Wall to Foundation Connection

Figure 6.3	Wall to Wood Sill Connection

Figure 6.4	Stud Bracing with Sheathing Material Only

Figure 6.5	Stud Bracing with Strapping Only

Figure 6.6	Stud Bracing with Strapping and Sheathing Material

Figure 6.7	Track Splice

Figure  6.8	Corner Framing

Figure 6.9		Box-Beam Header Detail

Figure 6.10		Back-to-Back Header Detail

Figure 6.11	Structural Sheathing Fastening Pattern

Table 6.1

Wall to Foundation or Floor Connection Requirements

| Framing Condition |
| --- |
| Wind Speed (mph), Exposure, & Seismic Zones1,2,3 |
|  | Up to 70 A/B or Seismic Zones 0, 1, 2 | Up to 90 A/B 70 C or Seismic Zone 3 | Up to 110 A/B or 90 C or Seismic Zone 4 | Up to 110 C |

Wall bottom track

| to floor joist or track |
| --- |
| 1 - #8 screw at 12" oc | 1 - #8 screw at 12" oc | 2 - #8 screw at 12" oc | 2 - #8 screw at 12" oc |
| Wall bottom track to foundation per Figure 6.2 |
| 1/2" minimum diameter anchor bolt at 6' oc | 1/2" minimum diameter anchor bolt at 4' oc | 1/2" minimum diameter anchor bolt at 4' oc | 1/2" minimum diameter anchor bolt at 4' oc |
| Wall bottom track to wood sill per Figure 6.3 |
| Steel plate spaced at 4' oc, with 4 - #8 screws and 4 - 10d or 6 - 8d common nails | Steel plate spaced at 3' oc, with 4 - #8 screws and 4 - 10d or 6 - 8d common nails | Steel plate spaced at 2' oc, with 4 - #8 screws and 4 - 10d or 6 - 8d common nails | Steel plate spaced at 2' oc, with 4 - #8 screws and 4 - 10d or 6 - 8d common nails |
| Wind uplift connector capacity 3 |
| N/R | N/R | 50 lbs. per foot of wall length | 200 lbs. per foot of wall length |

For SI:	1 inch = 25.4 mm, 1 psf = 0.0479 kN/m2,  1 mph = 1.61 km/hr,  1 foot = 0.3 m,  1 lb. = 4.4 N.

1		Use the greater of the wind speed and exposure or the seismic requirements for a given site.

2		All screw sizes shown are minimum.

3	N/R = uplift connector not required.  For 16-inch (406 mm) and 24-inch ( 610 mm) stud 		spacing, the uplift load shall be multiplied by 1.3 and 2.0, respectively.  Uplift connectors are 		in addition to other connection requirements and shall be applied in accordance with Section 		6.10.

Table 6.2

Steel Stud Thickness for 8' Walls Supporting Roof and Ceiling Only

(One Story or Second Floor of a Two Story Building)

33 ksi Steel

| Wind |
| --- |
| Mem | Member | Stud Thickness (mils)1,2 |
|  | Speed |
| ber | Spacing | Building Width (feet)4,5 |
|  | Size3 | (inches) | 24 |
| 28 |
| 32 |
| 36 |
|  | Exp. A/B | Exp. C |
|  | Ground Snow Load (psf) |
| Ground Snow Load (psf) |
| Ground Snow Load (psf) |
| Ground Snow Load (psf) |
|  | 20 | 30 | 50 | 70 | 20 | 30 | 50 | 70 | 20 | 30 | 50 | 70 | 20 | 30 | 50 | 70 |
| 70 |
| 2x4 | 16 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 |
| mph |
|  | 24 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 43 |
| 2x6 | 16 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 |
|  | 24 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 |
| 80 | 70 | 2x4 | 16 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 |
| mph | mph |
| 24 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 43 | 33 | 33 | 43 | 43 |
| 2x6 | 16 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 |
|  | 24 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 |
| 90 | 80 | 2x4 | 16 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 |
| mph | mph |
| 24 | 33 | 33 | 43 | 43 | 33 | 33 | 43 | 43 | 33 | 43 | 43 | 43 | 43 | 43 | 43 | 43 |
| 2x6 | 16 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 |
|  | 24 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 |
| 100 | 90 | 2x4 | 16 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 |
| mph | mph |
| 24 | 43 | 43 | 43 | 43 | 43 | 43 | 43 | 54 | 43 | 43 | 54 | 54 | 43 | 43 | 54 | 54 |
| 2x6 | 16 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 |
|  | 24 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 |
| 110 | 100 | 2x4 | 16 | 33 | 33 | 43 | 43 | 33 | 43 | 43 | 43 | 43 | 43 | 43 | 43 | 43 | 43 | 43 | 43 |
| mph | mph |
| 24 | 54 | 54 | 54 | 54 | 54 | 54 | 54 | 68 | 54 | 54 | 68 | 68 | 54 | 54 | 68 | 68 |
| 2x6 | 16 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 |
|  | 24 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 43 | 33 | 33 | 33 | 43 | 33 | 33 | 43 | 43 |
|  | 110 | 2x4 | 16 | 43 | 43 | 43 | 43 | 43 | 43 | 43 | 43 | 43 | 43 | 43 | 54 | 43 | 43 | 43 | 54 |
|  | mph |
| 24 | 68 | 68 | 68 | 68 | 68 | 68 | 68 | 68 | 68 | 68 | 68 | 68 | 68 | 68 | 68 | 97 |
| 2x6 | 16 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 |
|  | 24 | 33 | 43 | 43 | 43 | 43 | 43 | 43 | 43 | 43 | 43 | 43 | 43 | 43 | 43 | 43 | 43 |

For SI:	1 inch = 25.4 mm,    1 psf = 0.0479 kN/m2,    1 mph = 1.61 km/hr,  1 foot = 0.3 m.

1	Deflection criteria: L/240

2	Design load assumptions:		Roof dead load is 12 psf  (0.575 kN/m2)

Attic live load is 10 psf  (0.479 kN/m2)

3	For actual sizes of members, refer to Table 2.1.

4	Building width is in the direction of horizontal framing members supported by the wall studs.

5	Exterior load bearing walls with a minimum of 1/2 inch (13 mm) gypsum board on the inside and 7/16

inch (11 mm) OSB or plywood on the outside, and interior load bearing walls with a minimum of 1/2 inch

(13 mm) gypsum board on both sides may use the next thinner stud but not less than 33 mils (0.84 mm)

Table 6.3

Steel Stud Thickness for 8' Walls Supporting One Floor, Roof and Ceiling

(First Story of a Two Story Building)

33 ksi Steel

| Wind |
| --- |
| Mem | Member | Required Stud Thickness (mils)1,2 |
|  | Exposure |
| ber | Spacing | Building Width (feet)4,5,6 |
|  | Size3 | (inches) | 24 |
| 28 |
| 32 |
| 36 |
|  | Exp. A/B | Exp. C |
|  | Ground Snow Load (psf) |
| Ground Snow Load (psf) |
| Ground Snow Load (psf) |
| Ground Snow Load (psf) |
|  | 20 | 30 | 50 | 70 | 20 | 30 | 50 | 70 | 20 | 30 | 50 | 70 | 20 | 30 | 50 | 70 |
| 70 |
| 2x4 | 16 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 43 | 33 | 33 | 33 | 43 |
| mph |
|  | 24 | 43 | 43 | 43 | 43 | 43 | 43 | 43 | 43 | 43 | 43 | 43 | 54 | 43 | 43 | 54 | 54 |
| 2x6 | 16 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 |
|  | 24 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 43 | 33 | 33 | 43 | 43 | 33 | 43 | 43 | 54 |
| 80 | 70 | 2x4 | 16 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 43 | 33 | 33 | 43 | 43 |
| mph | mph |
| 24 | 43 | 43 | 43 | 54 | 43 | 43 | 54 | 54 | 54 | 54 | 54 | 54 | 54 | 54 | 54 | 54 |
| 2x6 | 16 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 43 |
|  | 24 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 43 | 33 | 33 | 43 | 43 | 43 | 43 | 43 | 54 |
| 90 | 80 | 2x4 | 16 | 33 | 33 | 33 | 33 | 33 | 33 | 43 | 43 | 43 | 43 | 43 | 43 | 43 | 43 | 43 | 43 |
| mph | mph |
| 24 | 54 | 54 | 54 | 54 | 54 | 54 | 54 | 54 | 54 | 54 | 54 | 68 | 54 | 54 | 68 | 68 |
| 2x6 | 16 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 |
|  | 24 | 33 | 33 | 33 | 33 | 33 | 33 | 43 | 43 | 43 | 43 | 43 | 43 | 43 | 43 | 43 | 54 |
| 100 | 90 | 2x4 | 16 | 43 | 43 | 43 | 43 | 43 | 43 | 43 | 43 | 43 | 43 | 43 | 43 | 43 | 43 | 43 | 54 |
| mph | mph |
| 24 | 54 | 54 | 54 | 68 | 54 | 68 | 68 | 68 | 68 | 68 | 68 | 68 | 68 | 68 | 68 | 68 |
| 2x6 | 16 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 |
|  | 24 | 33 | 43 | 43 | 43 | 43 | 43 | 43 | 43 | 43 | 43 | 43 | 43 | 43 | 43 | 43 | 54 |
| 110 | 100 | 2x4 | 16 | 43 | 43 | 43 | 54 | 43 | 54 | 54 | 54 | 54 | 54 | 54 | 54 | 54 | 54 | 54 | 54 |
| mph | mph |
| 24 | 68 | 68 | 68 | 68 | 68 | 68 | 97 | 97 | 97 | 97 | 97 | 97 | 97 | 97 | 97 | 97 |
| 2x6 | 16 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 43 |
|  | 24 | 43 | 43 | 43 | 43 | 43 | 43 | 43 | 54 | 43 | 43 | 54 | 54 | 54 | 54 | 54 | 54 |
|  | 110 | 2x4 | 16 | 54 | 54 | 54 | 54 | 54 | 54 | 54 | 54 | 54 | 54 | 54 | 68 | 54 | 54 | 68 | 68 |
|  | mph |
| 24 | 97 | 97 | 97 | 97 | 97 | 97 | 97 | 97 | 97 | 97 | 97 | 97 | 97 | 97 | 97 | 97 |
| 2x6 | 16 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 43 | 33 | 33 | 43 | 43 | 43 | 43 | 43 | 43 |
|  | 24 | 43 | 43 | 54 | 54 | 54 | 54 | 54 | 54 | 54 | 54 | 54 | 54 | 54 | 54 | 54 | 54 |

For SI:1 inch = 25.4 mm,    1 psf = 0.0479 kN/m2,    1 mph = 1.61 km/hr,  1 foot = 0.3 m.

1	Deflection criteria: L/240

2	Design load assumptions:

Second floor dead load is 10 psf  (0.48 kN/m2) 	Attic live load is 10 psf  (0.48kN/m2)

Second floor live load is 30 psf  (1.44 kN/m2)	Roof dead load is 12 psf  (0.58 kN/m2)

3	For actual sizes of members, refer to Table 2.1.

4	Building width is in the direction of horizontal framing members supported by the wall studs.

5	Exterior load bearing walls with a minimum of 1/2 inch (13 mm) gypsum board on the inside and 7/16

inch (11 mm) OSB or plywood on the outside, and interior load bearing walls with a minimum of 1/2 inch  	(13 mm) gypsum board on both sides may use the next thinner stud but not less than 33 mils (0.84 mm).

6	For second story floors with 40 psf live load, select the stud size from the next higher ground snow load

column.

Table 6.4

Steel Stud Thickness for 9' Walls Supporting Roof and Ceiling Only

(One Story or Second Floor of a Two Story Building)

33 ksi Steel

| Wind |
| --- |
| Mem | Member | Required Stud Thickness (mils)1,2 |
|  | Exposure |
| ber | Spacing | Building Width (feet)4,5 |
|  | Size3 | (inches) | 24 |
| 28 |
| 32 |
| 36 |
|  | Exp. A/B | Exp. C |
|  | Ground Snow Load (psf) |
| Ground Snow Load (psf) |
| Ground Snow Load (psf) |
| Ground Snow Load (psf) |
|  | 20 | 30 | 50 | 70 | 20 | 30 | 50 | 70 | 20 | 30 | 50 | 70 | 20 | 30 | 50 | 70 |
| 70 |
| 2x4 | 16 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 |
| mph |
|  | 24 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 43 |
| 2x6 | 16 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 |
|  | 24 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 |
| 80 | 70 | 2x4 | 16 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 |
| mph | mph |
| 24 | 33 | 33 | 43 | 43 | 33 | 33 | 43 | 43 | 33 | 43 | 43 | 43 | 43 | 43 | 43 | 43 |
| 2x6 | 16 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 |
|  | 24 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 |
| 90 | 80 | 2x4 | 16 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 |
| mph | mph |
| 24 | 43 | 43 | 43 | 43 | 43 | 43 | 43 | 43 | 43 | 43 | 43 | 54 | 43 | 43 | 43 | 54 |
| 2x6 | 16 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 |
|  | 24 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 |
| 100 | 90 | 2x4 | 16 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 43 | 33 | 33 | 43 | 43 | 33 | 33 | 43 | 43 |
| mph | mph |
| 24 | 54 | 54 | 54 | 54 | 54 | 54 | 54 | 54 | 54 | 54 | 54 | 54 | 54 | 54 | 54 | 68 |
| 2x6 | 16 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 |
|  | 24 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 43 |
| 110 | 100 | 2x4 | 16 | 43 | 43 | 43 | 43 | 43 | 43 | 43 | 43 | 43 | 43 | 43 | 54 | 43 | 43 | 43 | 54 |
| mph | mph |
| 24 | 68 | 68 | 68 | 68 | 68 | 68 | 68 | 68 | 68 | 68 | 68 | 68 | 68 | 68 | 68 | 97 |
| 2x6 | 16 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 |
|  | 24 | 33 | 43 | 43 | 43 | 43 | 43 | 43 | 43 | 43 | 43 | 43 | 43 | 43 | 43 | 43 | 43 |
|  | 110 | 2x4 | 16 | 54 | 54 | 54 | 54 | 54 | 54 | 54 | 54 | 54 | 54 | 54 | 54 | 54 | 54 | 54 | 54 |
|  | mph |
| 24 | 97 | 97 | 97 | 97 | 97 | 97 | 97 | 97 | 97 | 97 | 97 | 97 | 97 | 97 | 97 | 97 |
| 2x6 | 16 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 |
|  | 24 | 43 | 43 | 43 | 43 | 43 | 43 | 43 | 43 | 43 | 43 | 43 | 54 | 43 | 43 | 43 | 54 |

For SI:   1 inch = 25.4 mm,    1 psf = 0.0479 kN/m2,    1 mph = 1.61 km/hr,  1 foot = 0.3 m.

1	Deflection criteria: L/240

2	Design load assumptions:		Roof dead load is 12 psf  (0.575 kN/m2)

Attic live load is 10 psf  (0.479 kN/m2)

3	For actual sizes of members, refer to Table 2.1.

4	Building width is in the direction of horizontal framing members supported by the wall studs.

5	Exterior load bearing walls with a minimum of 1/2 inch (13 mm) gypsum board on the inside and 7/16

inch (11 mm) OSB or plywood on the outside, and interior load bearing walls with a minimum of 1/2 inch

(13 mm) gypsum board on both sides may use the next thinner stud but not less than 33 mils (0.84 mm).

Table 6.5

Steel Stud Thickness for 9' Walls Supporting One Floor, Roof and Ceiling

(First Story of a Two Story Building)

33 ksi Steel

| Wind |
| --- |
| Mem | Member | Required Stud Thickness (mils)1,2 |
|  | Exposure |
| ber | Spacing | Building Width (feet)4,5 |
|  | Size3 | (inches) | 24 |
| 28 |
| 32 |
| 36 |
|  | Exp. A/B | Exp. C |
|  | Ground Snow Load (psf) |
| Ground Snow Load (psf) |
| Ground Snow Load (psf) |
| Ground Snow Load (psf) |
|  | 20 | 30 | 50 | 70 | 20 | 30 | 50 | 70 | 20 | 30 | 50 | 70 | 20 | 30 | 50 | 70 |
| 70 |
| 2x4 | 16 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 43 |
| mph |
|  | 24 | 43 | 43 | 43 | 43 | 43 | 43 | 43 | 54 | 43 | 43 | 54 | 54 | 54 | 54 | 54 | 54 |
| 2x6 | 16 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 |
|  | 24 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 43 | 33 | 33 | 43 | 43 | 33 | 33 | 43 | 43 |
| 80 | 70 | 2x4 | 16 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 43 | 33 | 43 | 43 | 43 | 43 | 43 | 43 | 43 |
| mph | mph |
| 24 | 43 | 54 | 54 | 54 | 54 | 54 | 54 | 54 | 54 | 54 | 54 | 54 | 54 | 54 | 68 | 68 |
| 2x6 | 16 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 |
|  | 24 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 43 | 33 | 33 | 43 | 43 | 43 | 43 | 43 | 43 |
| 90 | 80 | 2x4 | 16 | 43 | 43 | 43 | 43 | 43 | 43 | 43 | 43 | 43 | 43 | 43 | 43 | 43 | 43 | 43 | 43 |
| mph | mph |
| 24 | 54 | 54 | 54 | 54 | 54 | 54 | 54 | 54 | 54 | 54 | 54 | 54 | 54 | 54 | 68 | 68 |
| 2x6 | 16 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 |
|  | 24 | 33 | 33 | 43 | 43 | 43 | 43 | 43 | 43 | 43 | 43 | 43 | 43 | 43 | 43 | 43 | 54 |
| 100 | 90 | 2x4 | 16 | 43 | 43 | 43 | 43 | 43 | 43 | 43 | 54 | 43 | 43 | 54 | 54 | 54 | 54 | 54 | 54 |
| mph | mph |
| 24 | 68 | 68 | 68 | 68 | 68 | 68 | 68 | 68 | 68 | 68 | 68 | 97 | 68 | 68 | 97 | 97 |
| 2x6 | 16 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 |
|  | 24 | 43 | 43 | 43 | 43 | 43 | 43 | 43 | 43 | 43 | 43 | 43 | 54 | 43 | 43 | 54 | 54 |
| 110 | 100 | 2x4 | 16 | 54 | 54 | 54 | 54 | 54 | 54 | 54 | 54 | 54 | 54 | 54 | 68 | 54 | 54 | 68 | 68 |
| mph | mph |
| 24 | 97 | 97 | 97 | 97 | 97 | 97 | 97 | 97 | 97 | 97 | 97 | 97 | 97 | 97 | 97 | 97 |
| 2x6 | 16 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 43 | 33 | 33 | 43 | 43 | 33 | 43 | 43 | 43 |
|  | 24 | 43 | 43 | 54 | 54 | 54 | 54 | 54 | 54 | 54 | 54 | 54 | 54 | 54 | 54 | 54 | 54 |
|  | 110 | 2x4 | 16 | 68 | 68 | 68 | 68 | 68 | 68 | 68 | 68 | 68 | 68 | 68 | 68 | 68 | 68 | 68 | 68 |
|  | mph |
| 24 | 97 | 97 | 97 | 97 | 97 | 97 | 97 | -- | 97 | 97 | -- | -- | -- | -- | -- | -- |
| 2x6 | 16 | 33 | 33 | 43 | 43 | 43 | 43 | 43 | 43 | 43 | 43 | 43 | 43 | 43 | 43 | 43 | 43 |
|  | 24 | 54 | 54 | 54 | 54 | 54 | 54 | 54 | 54 | 54 | 54 | 54 | 68 | 54 | 54 | 68 | 68 |

For SI:  1 inch = 25.4 mm,    1 psf = 0.0479 kN/m2,    1 mph = 1.61 km/hr,  1 foot = 0.3 m.

1	Deflection criteria: L/240

2	Design load assumptions:

Second floor dead load is 10 psf  (0.48 kN/m2) 	Attic live load is 10 psf  (0.48 kN/m2)

Second floor live load is 30 psf  (1.44 kN/m2)	Roof dead load is 12 psf  (0.58 kN/m2)

3	For actual sizes of members, refer to Table 2.1.

4	Building width is in the direction of horizontal framing members supported by the wall studs.

5	Exterior load bearing walls with a minimum of 1/2 inch (13 mm) gypsum board on the inside and 7/16

inch (11 mm) OSB or plywood on the outside, and interior load bearing walls with a minimum of 1/2 inch

(13 mm) gypsum board on both sides may use the next thinner stud but not less than 33 mils (0.84 mm).

6	For second story floors with 40 psf live load, select the stud size from the next higher ground snow load

column.

Table 6.6

Steel Stud Thickness for 10' Walls Supporting Roof and Ceiling Only

(One Story or Second Floor of a Two Story Building)

33 ksi Steel

| Wind |
| --- |
| Mem | Member | Required Stud Thickness (mils)1,2 |
|  | Exposure |
| ber | Spacing | Building Width (feet)4,5 |
|  | Size3 | (inches) | 24 |
| 28 |
| 32 |
| 36 |
|  | Exp. A/B | Exp. C |
|  | Ground Snow Load (psf) |
| Ground Snow Load (psf) |
| Ground Snow Load (psf) |
| Ground Snow Load (psf) |
|  | 20 | 30 | 50 | 70 | 20 | 30 | 50 | 70 | 20 | 30 | 50 | 70 | 20 | 30 | 50 | 70 |
| 70 |
| 2x4 | 16 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 |
| mph |
|  | 24 | 33 | 33 | 33 | 43 | 33 | 33 | 43 | 43 | 33 | 33 | 43 | 43 | 33 | 43 | 43 | 43 |
| 2x6 | 16 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 |
|  | 24 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 |
| 80 | 70 | 2x4 | 16 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 |
| mph | mph |
| 24 | 43 | 43 | 43 | 43 | 43 | 43 | 43 | 54 | 43 | 43 | 43 | 54 | 43 | 43 | 54 | 54 |
| 2x6 | 16 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 |
|  | 24 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 |
| 90 | 80 | 2x4 | 16 | 33 | 33 | 33 | 43 | 33 | 33 | 43 | 43 | 33 | 33 | 43 | 43 | 33 | 33 | 43 | 43 |
| mph | mph |
| 24 | 54 | 54 | 54 | 54 | 54 | 54 | 54 | 54 | 54 | 54 | 54 | 54 | 54 | 54 | 54 | 68 |
| 2x6 | 16 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 |
|  | 24 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 43 |
| 100 | 90 | 2x4 | 16 | 43 | 43 | 43 | 43 | 43 | 43 | 43 | 43 | 43 | 43 | 43 | 43 | 43 | 43 | 43 | 54 |
| mph | mph |
| 24 | 68 | 68 | 68 | 68 | 68 | 68 | 68 | 68 | 68 | 68 | 68 | 68 | 68 | 68 | 68 | 68 |
| 2x6 | 16 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 |
|  | 24 | 33 | 33 | 43 | 43 | 33 | 33 | 43 | 43 | 33 | 43 | 43 | 43 | 43 | 43 | 43 | 43 |
| 110 | 100 | 2x4 | 16 | 54 | 54 | 54 | 54 | 54 | 54 | 54 | 54 | 54 | 54 | 54 | 54 | 54 | 54 | 54 | 68 |
| mph | mph |
| 24 | 97 | 97 | 97 | 97 | 97 | 97 | 97 | 97 | 97 | 97 | 97 | 97 | 97 | 97 | 97 | 97 |
| 2x6 | 16 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 |
|  | 24 | 43 | 43 | 43 | 43 | 43 | 43 | 43 | 54 | 43 | 43 | 54 | 54 | 43 | 43 | 54 | 54 |
|  | 110 | 2x4 | 16 | 68 | 68 | 68 | 68 | 68 | 68 | 68 | 68 | 68 | 68 | 68 | 68 | 68 | 68 | 68 | 68 |
|  | mph |
| 24 | 97 | 97 | 97 | -- | 97 | 97 | -- | -- | 97 | 97 | -- | -- | 97 | -- | -- | -- |
| 2x6 | 16 | 33 | 33 | 33 | 43 | 33 | 33 | 43 | 43 | 33 | 33 | 43 | 43 | 33 | 43 | 43 | 43 |
|  | 24 | 54 | 54 | 54 | 54 | 54 | 54 | 54 | 54 | 54 | 54 | 54 | 54 | 54 | 54 | 54 | 68 |

For SI:   1 inch = 25.4 mm,    1 psf = 0.0479 kN/m2,    1 mph = 1.61 km/hr,  1 foot = 0.3 m.

1	Deflection criteria: L/240

2	Design load assumptions:		Roof dead load is 12 psf  (0.58 kN/m2)

Attic live load is 10 psf  (0.48 kN/m2)

3	For actual sizes of members, refer to Table 2.1.

4	Building width is in the direction of horizontal framing members supported by the wall studs.

5	Exterior load bearing walls with a minimum of 1/2 inch (13 mm) gypsum board on the inside and 7/16

inch (11 mm) OSB or plywood on the outside, and interior load bearing walls with a minimum of 1/2 inch

(13 mm) gypsum board on both sides may use the next thinner stud but not less than 33 mils (0.84 mm).

Table 6.7

Steel Stud Thickness for 10' Walls Supporting One Floor, Roof and Ceiling

(First Story of a Two Story Building)

33 ksi Steel

| Wind |
| --- |
| Mem | Member | Required Stud Thickness (mils)1,2 |
|  | Exposure |
| ber | Spacing | Building Width (feet)4,5,6 |
|  | Size3 | (inches) | 24 |
| 28 |
| 32 |
| 36 |
|  | Exp. A/B | Exp. C |
|  | Ground Snow Load (psf) |
| Ground Snow Load (psf) |
| Ground Snow Load (psf) |
| Ground Snow Load (psf) |
|  | 20 | 30 | 50 | 70 | 20 | 30 | 50 | 70 | 20 | 30 | 50 | 70 | 20 | 30 | 50 | 70 |
| 70 |
| 2x4 | 16 | 33 | 33 | 33 | 43 | 33 | 33 | 43 | 43 | 43 | 43 | 43 | 43 | 43 | 43 | 43 | 43 |
| mph |
|  | 24 | 54 | 54 | 54 | 54 | 54 | 54 | 54 | 54 | 54 | 54 | 54 | 68 | 54 | 54 | 68 | 68 |
| 2x6 | 16 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 |
|  | 24 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 43 | 33 | 33 | 43 | 43 | 43 | 43 | 43 | 54 |
| 80 | 70 | 2x4 | 16 | 43 | 43 | 43 | 43 | 43 | 43 | 43 | 43 | 43 | 43 | 43 | 43 | 43 | 43 | 43 | 54 |
| mph | mph |
| 24 | 54 | 54 | 68 | 68 | 68 | 68 | 68 | 68 | 68 | 68 | 68 | 68 | 68 | 68 | 68 | 97 |
| 2x6 | 16 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 |
|  | 24 | 33 | 33 | 43 | 43 | 43 | 43 | 43 | 43 | 43 | 43 | 43 | 43 | 43 | 43 | 43 | 54 |
| 90 | 80 | 2x4 | 16 | 43 | 43 | 43 | 43 | 43 | 43 | 54 | 54 | 43 | 54 | 54 | 54 | 54 | 54 | 54 | 54 |
| mph | mph |
| 24 | 68 | 68 | 68 | 68 | 68 | 68 | 68 | 97 | 68 | 68 | 97 | 97 | 97 | 97 | 97 | 97 |
| 2x6 | 16 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 |
|  | 24 | 43 | 43 | 43 | 43 | 43 | 43 | 43 | 43 | 43 | 43 | 43 | 54 | 43 | 43 | 54 | 54 |
| 100 | 90 | 2x4 | 16 | 54 | 54 | 54 | 54 | 54 | 54 | 54 | 54 | 54 | 54 | 54 | 54 | 54 | 54 | 54 | 54 |
| mph | mph |
| 24 | 97 | 97 | 97 | 97 | 97 | 97 | 97 | 97 | 97 | 97 | 97 | 97 | 97 | 97 | 97 | 97 |
| 2x6 | 16 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 43 | 33 | 33 | 43 | 43 |
|  | 24 | 43 | 43 | 43 | 54 | 43 | 54 | 54 | 54 | 54 | 54 | 54 | 54 | 54 | 54 | 54 | 54 |
| 110 | 100 | 2x4 | 16 | 68 | 68 | 68 | 68 | 68 | 68 | 68 | 68 | 68 | 68 | 68 | 68 | 68 | 68 | 68 | 97 |
| mph | mph |
| 24 | 97 | 97 | -- | -- | -- | -- | -- | -- | -- | -- | -- | -- | -- | -- | -- | -- |
| 2x6 | 16 | 43 | 43 | 43 | 43 | 43 | 43 | 43 | 43 | 43 | 43 | 43 | 43 | 43 | 43 | 43 | 43 |
|  | 24 | 54 | 54 | 54 | 54 | 54 | 54 | 54 | 68 | 54 | 68 | 68 | 68 | 68 | 68 | 68 | 68 |
|  | 110 | 2x4 | 16 | 68 | 97 | 97 | 97 | 97 | 97 | 97 | 97 | 97 | 97 | 97 | 97 | 97 | 97 | 97 | 97 |
|  | mph |
| 24 | -- | -- | -- | -- | -- | -- | -- | -- | -- | -- | -- | -- | -- | -- | -- | -- |
| 2x6 | 16 | 43 | 43 | 43 | 43 | 43 | 43 | 43 | 43 | 43 | 43 | 43 | 54 | 43 | 43 | 54 | 54 |
|  | 24 | 68 | 68 | 68 | 68 | 68 | 68 | 68 | 68 | 68 | 68 | 68 | 68 | 68 | 68 | 68 | 97 |

For SI:  1 inch = 25.4 mm,    1 psf = 0.0479 kN/m2,    1 mph = 1.61 km/hr,  1 foot = 0.3 m.

1	Deflection criteria: L/240

2	Design load assumptions:

Second floor dead load is 10 psf  (0.48 kN/m2) 	Roof dead load is 12 psf  (0.58 kN/m2)

Second floor live load is 30 psf  (1.44 kN/m2)	Attic live load is 10 psf  (0.48 kN/m2)

3	For actual sizes of members, refer to Table 2.1.

4	Building width is in the direction of horizontal framing members supported by the wall studs.

5	Exterior load bearing walls with a minimum of 1/2 inch (13 mm) gypsum board on the inside and 7/16

inch (11 mm) OSB or plywood on the outside, and interior load bearing walls with a minimum of 1/2 inch

(13 mm) gypsum board on both sides may use the next thinner stud but not less than 33 mils (0.84 mm).

6	For second story floors with 40 psf live load, select the stud size from the next higher ground snow load

column.

Table 6.8

Steel Stud Thickness for 8' Walls Supporting Roof and Ceiling Only

(One Story or Second Floor of a Two Story Building)

50 ksi Steel

| Wind |
| --- |
| Mem | Member | Stud Thickness (mils)1,2 |
|  | Speed |
| ber | Spacing | Building Width (feet)4 |
|  | Size3 | (inches) | 24 |
| 28 |
| 32 |
| 36 |
|  | Exp. A/B | Exp. C |
|  | Ground Snow Load (psf) |
| Ground Snow Load (psf) |
| Ground Snow Load (psf) |
| Ground Snow Load (psf) |
|  | 20 | 30 | 50 | 70 | 20 | 30 | 50 | 70 | 20 | 30 | 50 | 70 | 20 | 30 | 50 | 70 |
| 70 |
| 2x4 | 16 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 |
| mph |
|  | 24 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 |
| 2x6 | 16 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 |
|  | 24 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 |
| 80 | 70 | 2x4 | 16 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 |
| mph | mph |
| 24 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 |
| 2x6 | 16 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 |
|  | 24 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 |
| 90 | 80 | 2x4 | 16 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 |
| mph | mph |
| 24 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 43 |
| 2x6 | 16 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 |
|  | 24 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 |
| 100 | 90 | 2x4 | 16 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 |
| mph | mph |
| 24 | 33 | 33 | 33 | 43 | 33 | 33 | 43 | 43 | 33 | 33 | 43 | 43 | 33 | 43 | 43 | 43 |
| 2x6 | 16 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 |
|  | 24 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 |
| 110 | 100 | 2x4 | 16 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 |
| mph | mph |
| 24 | 43 | 43 | 43 | 43 | 43 | 43 | 43 | 43 | 43 | 43 | 43 | 54 | 43 | 43 | 43 | 54 |
| 2x6 | 16 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 |
|  | 24 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 |
|  | 110 | 2x4 | 16 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 43 | 33 | 33 | 43 | 43 | 33 | 33 | 43 | 43 |
|  | mph |
| 24 | 43 | 54 | 54 | 54 | 54 | 54 | 54 | 54 | 54 | 54 | 54 | 54 | 54 | 54 | 54 | 54 |
| 2x6 | 16 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 |
|  | 24 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 |

For SI:   1 inch = 25.4 mm,    1 psf = 0.0479 kN/m2,    1 mph = 1.61 km/hr,  1 foot = 0.3 m.

1	Deflection criteria: L/240

2	Design load assumptions:		Roof dead load is 12 psf  (0.575 kN/m2)

Attic live load is 10 psf  (0.479 kN/m2)

3	For actual sizes of members, refer to Table 2.1.

4	Building width is in the direction of horizontal framing members supported by the wall studs.

Table 6.9

Steel Stud Thickness for 8' Walls Supporting One Floor, Roof and Ceiling

(First Story of a Two Story Building)

50 ksi Steel

| Wind |
| --- |
| Mem | Member | Required Stud Thickness (mils)1,2 |
|  | Exposure |
| ber | Spacing | Building Width (feet)4 |
|  | Size3 | (inches) | 24 |
| 28 |
| 32 |
| 36 |
|  | Exp. A/B | Exp. C |
|  | Ground Snow Load (psf) |
| Ground Snow Load (psf) |
| Ground Snow Load (psf) |
| Ground Snow Load (psf) |
|  | 20 | 30 | 50 | 70 | 20 | 30 | 50 | 70 | 20 | 30 | 50 | 70 | 20 | 30 | 50 | 70 |
| 70 |
| 2x4 | 16 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 43 |
| mph |
|  | 24 | 33 | 33 | 33 | 43 | 33 | 33 | 43 | 43 | 43 | 43 | 43 | 43 | 43 | 43 | 43 | 54 |
| 2x6 | 16 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 |
|  | 24 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 43 | 33 | 33 | 43 | 43 |
| 80 | 70 | 2x4 | 16 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 43 |
| mph | mph |
| 24 | 33 | 43 | 43 | 43 | 43 | 43 | 43 | 43 | 43 | 43 | 43 | 43 | 43 | 33 | 33 | 54 |
| 2x6 | 16 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 43 |
|  | 24 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 43 | 33 | 33 | 43 | 43 |
| 90 | 80 | 2x4 | 16 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 43 |
| mph | mph |
| 24 | 43 | 43 | 43 | 43 | 43 | 43 | 43 | 43 | 43 | 43 | 54 | 54 | 43 | 54 | 54 | 54 |
| 2x6 | 16 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 |
|  | 24 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 43 | 33 | 33 | 43 | 43 |
| 100 | 90 | 2x4 | 16 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 43 | 33 | 33 | 43 | 43 | 33 | 43 | 43 | 43 |
| mph | mph |
| 24 | 43 | 43 | 43 | 54 | 43 | 54 | 54 | 54 | 54 | 54 | 54 | 54 | 54 | 54 | 54 | 54 |
| 2x6 | 16 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 |
|  | 24 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 43 | 33 | 33 | 43 | 43 |
| 110 | 100 | 2x4 | 16 | 43 | 43 | 43 | 43 | 43 | 43 | 43 | 43 | 43 | 43 | 43 | 43 | 43 | 43 | 43 | 43 |
| mph | mph |
| 24 | 54 | 54 | 54 | 54 | 54 | 54 | 54 | 68 | 54 | 54 | 68 | 68 | 68 | 68 | 68 | 68 |
| 2x6 | 16 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 43 |
|  | 24 | 33 | 33 | 33 | 43 | 33 | 43 | 43 | 43 | 43 | 43 | 43 | 43 | 43 | 43 | 43 | 43 |
|  | 110 | 2x4 | 16 | 43 | 43 | 43 | 43 | 43 | 43 | 43 | 43 | 43 | 43 | 43 | 54 | 43 | 43 | 54 | 54 |
|  | mph |
| 24 | 54 | 68 | 68 | 68 | 68 | 68 | 68 | 68 | 68 | 68 | 68 | 68 | 68 | 68 | 68 | 68 |
| 2x6 | 16 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 |
|  | 24 | 43 | 43 | 43 | 43 | 43 | 43 | 43 | 43 | 43 | 43 | 43 | 43 | 43 | 43 | 43 | 43 |

For SI:  1 inch = 25.4 mm,    1 psf = 0.0479 kN/m2,    1 mph = 1.61 km/hr,  1 foot = 0.3 m.

1	Deflection criteria: L/240

2	Design load assumptions:

Second floor dead load is 10 psf  (0.48 kN/m2)	Attic live load is 10 psf  (0.48 kN/m2)

Second floor live load is 30 psf  (1.44 kN/m2)	Roof dead load is 12 psf  (0.575 kN/m2)

3	For actual sizes of members, refer to Table 2.1

4	Building width is in the direction of horizontal framing members supported by the wall studs.

Table 6.1

Steel Stud Thickness for 9' Walls Supporting Roof and Ceiling Only

(One Story or Second Floor of a Two Story Building)

50 ksi Steel

| Wind |
| --- |
| Mem | Member | Required Stud Thickness (mils)1,2 |
|  | Exposure |
| ber | Spacing | Building Width (feet)4 |
|  | Size3 | (inches) | 24 |
| 28 |
| 32 |
| 36 |
|  | Exp. A/B | Exp. C |
|  | Ground Snow Load (psf) |
| Ground Snow Load (psf) |
| Ground Snow Load (psf) |
| Ground Snow Load (psf) |
|  | 20 | 30 | 50 | 70 | 20 | 30 | 50 | 70 | 20 | 30 | 50 | 70 | 20 | 30 | 50 | 70 |
| 70 |
| 2x4 | 16 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 |
| mph |
|  | 24 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 |
| 2x6 | 16 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 |
|  | 24 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 |
| 80 | 70 | 2x4 | 16 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 |
| mph | mph |
| 24 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 |
| 2x6 | 16 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 |
|  | 24 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 |
| 90 | 80 | 2x4 | 16 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 |
| mph | mph |
| 24 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 43 | 33 | 33 | 33 | 43 | 33 | 33 | 43 | 43 |
| 2x6 | 16 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 |
|  | 24 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 |
| 100 | 90 | 2x4 | 16 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 |
| mph | mph |
| 24 | 43 | 43 | 43 | 43 | 43 | 43 | 43 | 43 | 43 | 43 | 43 | 43 | 43 | 43 | 43 | 43 |
| 2x6 | 16 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 |
|  | 24 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 |
| 110 | 100 | 2x4 | 16 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 43 | 33 | 33 | 43 | 43 |
| mph | mph |
| 24 | 43 | 43 | 54 | 54 | 43 | 54 | 54 | 54 | 54 | 54 | 54 | 54 | 54 | 54 | 54 | 54 |
| 2x6 | 16 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 |
|  | 24 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 |
|  | 110 | 2x4 | 16 | 43 | 43 | 43 | 43 | 43 | 43 | 43 | 43 | 43 | 43 | 43 | 43 | 43 | 43 | 43 | 43 |
|  | mph |
| 24 | 54 | 54 | 54 | 54 | 54 | 54 | 54 | 54 | 54 | 54 | 54 | 68 | 54 | 54 | 54 | 68 |
| 2x6 | 16 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 |
|  | 24 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 43 | 33 | 33 | 43 | 43 | 33 | 33 | 43 | 43 |

For SI:   1 inch = 25.4 mm,    1 psf = 0.0479 kN/m2,    1 mph = 1.61 km/hr,  1 foot = 0.3 m.

1	Deflection criteria: L/240

2	Design load assumptions:		Roof dead load is 12 psf  (0.575 kN/m2)

Attic live load is 10 psf  (0.479 kN/m2)

3	For actual sizes of members, refer to Table 2.1.

4	Building width is in the direction of horizontal framing members supported by the wall studs.

Table 6.11

Steel Stud Thickness for 9' Walls Supporting One Floor, Roof and Ceiling

(First Story of a Two Story Building)

50 ksi Steel

| Wind |
| --- |
| Mem | Member | Required Stud Thickness (mils)1,2 |
|  | Exposure |
| ber | Spacing | Building Width (feet)4 |
|  | Size3 | (inches) | 24 |
| 28 |
| 32 |
| 36 |
|  | Exp. A/B | Exp. C |
|  | Ground Snow Load (psf) |
| Ground Snow Load (psf) |
| Ground Snow Load (psf) |
| Ground Snow Load (psf) |
|  | 20 | 30 | 50 | 70 | 20 | 30 | 50 | 70 | 20 | 30 | 50 | 70 | 20 | 30 | 50 | 70 |
| 70 |
| 2x4 | 16 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 |
| mph |
|  | 24 | 33 | 33 | 33 | 43 | 33 | 43 | 43 | 43 | 43 | 43 | 43 | 43 | 43 | 43 | 43 | 43 |
| 2x6 | 16 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 |
|  | 24 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 43 |
| 80 | 70 | 2x4 | 16 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 |
| mph | mph |
| 24 | 43 | 43 | 43 | 43 | 43 | 43 | 43 | 43 | 43 | 43 | 43 | 43 | 43 | 43 | 54 | 54 |
| 2x6 | 16 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 |
|  | 24 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 43 |
| 90 | 80 | 2x4 | 16 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 43 | 33 | 33 | 33 | 43 | 43 |
| mph | mph |
| 24 | 43 | 43 | 43 | 43 | 43 | 43 | 43 | 54 | 43 | 54 | 54 | 54 | 54 | 54 | 54 | 54 |
| 2x6 | 16 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 |
|  | 24 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 43 |
| 100 | 90 | 2x4 | 16 | 33 | 33 | 33 | 43 | 33 | 33 | 43 | 43 | 43 | 43 | 43 | 43 | 43 | 43 | 43 | 43 |
| mph | mph |
| 24 | 54 | 54 | 54 | 54 | 54 | 54 | 54 | 54 | 54 | 54 | 54 | 54 | 54 | 54 | 54 | 68 |
| 2x6 | 16 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 |
|  | 24 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 43 | 33 | 33 | 43 | 43 | 43 | 43 | 43 | 43 |
| 110 | 100 | 2x4 | 16 | 43 | 43 | 43 | 43 | 43 | 43 | 43 | 43 | 43 | 43 | 43 | 43 | 43 | 43 | 43 | 54 |
| mph | mph |
| 24 | 54 | 54 | 68 | 68 | 68 | 68 | 68 | 68 | 68 | 68 | 68 | 68 | 68 | 68 | 68 | 68 |
| 2x6 | 16 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 |
|  | 24 | 43 | 43 | 43 | 43 | 43 | 43 | 43 | 43 | 43 | 43 | 43 | 43 | 43 | 43 | 43 | 43 |
|  | 110 | 2x4 | 16 | 43 | 43 | 43 | 54 | 43 | 43 | 54 | 54 | 54 | 54 | 54 | 54 | 54 | 54 | 54 | 54 |
|  | mph |
| 24 | 68 | 68 | 68 | 68 | 68 | 68 | 68 | 68 | 68 | 68 | 97 | 97 | 68 | 97 | 97 | 97 |
| 2x6 | 16 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 |
|  | 24 | 43 | 43 | 43 | 43 | 43 | 43 | 43 | 43 | 43 | 43 | 43 | 43 | 43 | 43 | 43 | 54 |

For SI:  1 inch = 25.4 mm,    1 psf = 0.0479 kN/m2,    1 mph = 1.61 km/hr,  1 foot = 0.3 m.

1	Deflection criteria: L/240

2	Design load assumptions:

Second floor dead load is 10 psf  (0.48 kN/m2)	Attic live load is 10 psf  (0.48 kN/m2)

Second floor live load is 30 psf  (1.44 kN/m2)	Roof dead load is 12 psf  (0.575 kN/m2)

3	For actual sizes of members, refer to Table 2.1.

4	Building width is in the direction of horizontal framing members supported by the wall studs.

Table 6.12

Steel Stud Thickness for 10' Walls Supporting Roof and Ceiling Only

(One Story or Second Floor of a Two Story Building)

50 ksi Steel

| Wind |
| --- |
| Mem | Member | Required Stud Thickness (mils)1,2 |
|  | Exposure |
| ber | Spacing | Building Width (feet)4 |
|  | Size3 | (inches) | 24 |
| 28 |
| 32 |
| 36 |
|  | Exp. A/B | Exp. C |
|  | Ground Snow Load (psf) |
| Ground Snow Load (psf) |
| Ground Snow Load (psf) |
| Ground Snow Load (psf) |
|  | 20 | 30 | 50 | 70 | 20 | 30 | 50 | 70 | 20 | 30 | 50 | 70 | 20 | 30 | 50 | 70 |
| 70 |
| 2x4 | 16 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 |
| mph |
|  | 24 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 43 |
| 2x6 | 16 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 |
|  | 24 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 |
| 80 | 70 | 2x4 | 16 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 |
| mph | mph |
| 24 | 33 | 33 | 33 | 43 | 33 | 33 | 33 | 43 | 33 | 33 | 43 | 43 | 33 | 33 | 43 | 43 |
| 2x6 | 16 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 |
|  | 24 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 |
| 90 | 80 | 2x4 | 16 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 |
| mph | mph |
| 24 | 43 | 43 | 43 | 43 | 43 | 43 | 43 | 43 | 43 | 43 | 43 | 43 | 43 | 43 | 43 | 54 |
| 2x6 | 16 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 |
|  | 24 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 |
| 100 | 90 | 2x4 | 16 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 43 | 33 | 33 | 33 | 43 |
| mph | mph |
| 24 | 43 | 43 | 54 | 54 | 43 | 43 | 54 | 54 | 43 | 54 | 54 | 54 | 54 | 54 | 54 | 54 |
| 2x6 | 16 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 |
|  | 24 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 |
| 110 | 100 | 2x4 | 16 | 43 | 43 | 43 | 43 | 43 | 43 | 43 | 43 | 43 | 43 | 43 | 43 | 43 | 43 | 43 | 43 |
| mph | mph |
| 24 | 54 | 54 | 54 | 68 | 54 | 54 | 68 | 68 | 54 | 54 | 68 | 68 | 54 | 68 | 68 | 68 |
| 2x6 | 16 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 |
|  | 24 | 33 | 33 | 33 | 43 | 33 | 33 | 43 | 43 | 33 | 33 | 43 | 43 | 33 | 43 | 43 | 43 |
|  | 110 | 2x4 | 16 | 43 | 43 | 54 | 54 | 43 | 43 | 54 | 54 | 43 | 54 | 54 | 54 | 54 | 54 | 54 | 54 |
|  | mph |
| 24 | 68 | 68 | 68 | 68 | 68 | 68 | 68 | 97 | 68 | 68 | 68 | 97 | 68 | 68 | 97 | 97 |
| 2x6 | 16 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 |
|  | 24 | 43 | 43 | 43 | 43 | 43 | 43 | 43 | 43 | 43 | 43 | 43 | 43 | 43 | 43 | 43 | 43 |

For SI:   1 inch = 25.4 mm,    1 psf = 0.0479 kN/m2,    1 mph = 1.61 km/hr,  1 foot = 0.3 m.

1	Deflection criteria: L/240

2	Design load assumptions:		Roof dead load is 12 psf  (0.575 kN/m2)

Attic live load is 10 psf  (0.479 kN/m2)

3	For actual sizes of members, refer to Table 2.1.

4	Building width is in the direction of horizontal framing members supported by the wall studs.

Table 6.13

Steel Stud Thickness for 10' Walls Supporting One Floor, Roof and Ceiling

(First Story of a Two Story Building)

50 ksi Steel

| Wind |
| --- |
| Mem | Member | Required Stud Thickness (mils)1,2 |
|  | Exposure |
| ber | Spacing | Building Width (feet)4 |
|  | Size3 | (inches) | 24 |
| 28 |
| 32 |
| 36 |
|  | Exp. A/B | Exp. C |
|  | Ground Snow Load (psf) |
| Ground Snow Load (psf) |
| Ground Snow Load (psf) |
| Ground Snow Load (psf) |
|  | 20 | 30 | 50 | 70 | 20 | 30 | 50 | 70 | 20 | 30 | 50 | 70 | 20 | 30 | 50 | 70 |
| 70 |
| 2x4 | 16 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 43 |
| mph |
|  | 24 | 43 | 43 | 43 | 43 | 43 | 43 | 43 | 43 | 43 | 43 | 54 | 54 | 43 | 54 | 54 | 54 |
| 2x6 | 16 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 |
|  | 24 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 43 | 33 | 33 | 33 | 43 |
| 80 | 70 | 2x4 | 16 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 43 | 33 | 33 | 43 | 43 | 43 | 43 | 43 | 43 |
| mph | mph |
| 24 | 43 | 43 | 54 | 54 | 54 | 54 | 54 | 54 | 54 | 54 | 54 | 54 | 54 | 54 | 54 | 54 |
| 2x6 | 16 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 |
|  | 24 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 43 | 33 | 33 | 43 | 43 |
| 90 | 80 | 2x4 | 16 | 33 | 33 | 43 | 43 | 43 | 43 | 43 | 43 | 43 | 43 | 43 | 43 | 43 | 43 | 43 | 43 |
| mph | mph |
| 24 | 54 | 54 | 54 | 54 | 54 | 54 | 54 | 54 | 54 | 54 | 68 | 68 | 54 | 68 | 68 | 68 |
| 2x6 | 16 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 |
|  | 24 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 43 | 33 | 43 | 43 | 43 | 43 | 43 | 43 | 43 |
| 100 | 90 | 2x4 | 16 | 43 | 43 | 43 | 43 | 43 | 43 | 43 | 43 | 43 | 43 | 43 | 54 | 43 | 43 | 54 | 54 |
| mph | mph |
| 24 | 54 | 54 | 68 | 68 | 68 | 68 | 68 | 68 | 68 | 68 | 68 | 68 | 68 | 68 | 68 | 97 |
| 2x6 | 16 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 |
|  | 24 | 43 | 43 | 43 | 43 | 43 | 43 | 43 | 43 | 43 | 43 | 43 | 43 | 43 | 43 | 43 | 43 |
| 110 | 100 | 2x4 | 16 | 54 | 54 | 54 | 54 | 54 | 54 | 54 | 54 | 54 | 54 | 54 | 54 | 54 | 54 | 54 | 54 |
| mph | mph |
| 24 | 68 | 68 | 97 | 97 | 97 | 97 | 97 | 97 | 97 | 97 | 97 | 97 | 97 | 97 | 97 | 97 |
| 2x6 | 16 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 33 | 43 |
|  | 24 | 43 | 43 | 43 | 43 | 43 | 43 | 43 | 43 | 43 | 43 | 43 | 54 | 43 | 43 | 54 | 54 |
|  | 110 | 2x4 | 16 | 54 | 54 | 54 | 54 | 54 | 54 | 54 | 54 | 54 | 54 | 68 | 68 | 54 | 68 | 68 | 68 |
|  | mph |
| 24 | 97 | 97 | 97 | 97 | 97 | 97 | 97 | 97 | 97 | 97 | 97 | 97 | 97 | 97 | 97 | 97 |
| 2x6 | 16 | 33 | 33 | 33 | 33 | 33 | 33 | 43 | 43 | 33 | 43 | 43 | 43 | 43 | 43 | 43 | 43 |
|  | 24 | 43 | 43 | 54 | 54 | 54 | 54 | 54 | 54 | 54 | 54 | 54 | 54 | 54 | 54 | 54 | 54 |

For SI:  1 inch = 25.4 mm,    1 psf = 0.0479 kN/m2,    1 mph = 1.61 km/hr,  1 foot = 0.3 m.

1	Deflection criteria: L/240

2	Design load assumptions:

Second floor dead load is 10 psf  (0.48 kN/m2)	Attic live load is 10 psf  (0.48 kN/m2)

Second floor live load is 30 psf  (1.44 kN/m2)	Roof dead load is 12 psf  (0.575 kN/m2)

3	For actual sizes of members, refer to Table 2.1.

4	Building width is in the direction of horizontal framing members supported by the wall studs.

Table 6.14

Wall Fastening Schedule

| Connection | Number & Type of Fasteners | Spacing of Fasteners |
| --- | --- | --- |
| Stud to top or bottom track | 2 # 8 screws | Each end of stud, one per flange |
| Structural sheathing (oriented strand board or plywood) to framing | # 8 screws1 |

6" on edges

| 12" on intermediate supports |
| --- |
| 1/2" Gypsum board to framing | # 6 screws | 12" oc. |

For SI:  1 inch = 25.4 mm

1	Head styles shall be bugle-head, flat-head, or similar head with a minimum head diameter

of 0.29 	inches (8 mm).

Table 6.15a

Allowable Header Spans for

Headers Supporting Roof and Ceiling Only1,2

33 ksi

| Nominal Member | 20 psf Ground Snow Load |
| --- | --- |
| 30 psf Ground Snow Load |
|  | Size3 | Building Width4 |
| Building Width4 |
| 24' | 28' | 32' | 36' | 24' | 28' | 32' | 36' |
| 2-2 x 4 x 33 | 3'-11" | 3'-8" | 3'-5" | 3'-3" | 3'-8" | 3'-5" | 3'-2" | 2'-10" |
| 2-2 x 4 x 43 | 4'-9" | 4'-5" | 4'-2" | 4'-0" | 4'-5" | 4'-2" | 3'-11" | 3'-9" |
| 2-2 x 4 x 54 | 5'-4" | 5'-0" | 4'-9" | 4'-6" | 5'-0" | 4'-8" | 4'-5" | 4'-2" |
| 2-2 x 4 x 68 | 6'-0" | 5'-7" | 5'-3" | 5'-0" | 5'-7" | 5'-3 | 4'-11" | 4'-8" |
| 2-2x 4 x 97 | 7'-1" | 6'-8" | 6'-3" | 5'-11" | 6'-8" | 6'-2" | 5'-10" | 5'-7" |
| 2-2x 6 x 33 | 3'-11" | 3'-5" | 3'-0" | 2'-9" | 3'-5" | 3'-0" | 2'-8" | 2'-5" |
| 2-2 x 6 x 43 | 6'-5" | 6'-0" | 5'-8" | 5'-5" | 6'-0" | 5'-8" | 5'-4" | 5'-0" |
| 2-2x 6 x 54 | 7'-3" | 6'-10" | 6'-5" | 6'-1" | 6'-9" | 6'-4" | 6'-0" | 5'-8" |
| 2-2 x 6 x 68 | 8'-2" | 7'-8" | 7'-2" | 6'-10" | 7'-7" | 7'-2" | 6'-9" | 6'-4" |
| 2-2 x 6 x 97 | 9'-9" | 9'-1" | 8'-7" | 8'-2" | 9'-1" | 8'-6" | 8'-0" | 7'-7" |
| 2-2 x 8 x 33 | 3'-0" | 2'-8" | 2'-4" | 2'-1" | 2'-7" | 2'-3" | -- | -- |
| 2-2 x 8 x 43 | 6'-8" | 5'-10" | 5'-2" | 4'-8" | 5'-10" | 5'-1" | 4'-6" | 4'-1" |
| 2-2x 8 x 54 | 9'-6" | 8'-10" | 8'-4" | 7'-11" | 8'-10" | 8'-3" | 7'-9" | 7'-5" |
| 2-2 x 8 x 68 | 10'-8" | 10'-0" | 9'-5" | 8'-11" | 9'-11" | 9'-4" | 8'-9" | 8'-4" |
| 2-2 x 8 x 97 | 12'-10" | 11'-11" | 11'-3" | 10'-8" | 11'-11" | 11'-2" | 10'-6" | 10'-0" |
| 2-2 x 10 x 43 | 5'-7" | 4'-10" | 4'-4" | 3'-11" | 4'-10" | 4'-3" | 3'-9" | 3'-5" |
| 2-2 x 10 x 54 | 10'-6" | 9'-8" | 8'-7" | 7'-9" | 9'-8" | 8'-5" | 7'-6" | 6'-9" |
| 2-2 x 10 x 68 | 12-7" | 11'-9" | 11'-1" | 10'-6" | 11'-9" | 10'-12" | 10'-4" | 9'-10" |
| 2-2 x 10 x 97 | 15'-2" | 14'-2" | 13'-4" | 12'-8" | 14'-1" | 13'-2" | 12'-5" | 11'-10" |
| 2-2 x 12 x 43 | 4'-9" | 4'-2" | 3'-8" | 3'-4" | 4'-2" | 3'-8" | 3'-3" | 2'-11" |
| 2-2 x 12 x 54 | 9'-6" | 8'-3" | 7'-4" | 6'-7" | 8'-3" | 7'-3" | 6'-5" | 5'-9" |
| 2-2 x 12 x 68 | 13'-5" | 12'-7" | 11'-10" | 11'-3" | 12'-6" | 11'-9" | 11'-1" | 10'-6" |
| 2-2 x 12 x 97 | 17'-5" | 16'-3" | 15'-4" | 14'-7" | 16'-3" | 15'-2" | 14'-4" | 13'-7" |

For SI:	1 inch = 25.4 mm,    1 psf = 0.0479 kN/m2,    1 foot = 0.3 m.

1		Deflection criteria: L/360 for live loads, L/240 for total loads.

2		Design load assumptions:

Roof dead load is 7 psf  (0.335 kN/m2)

Ceiling dead load is 5 psf (0.24 kN/m2)

Attic live load is 10 psf (0.479 kN/m2)

3		Refer to Table 2.1 for actual size.

4		Building width is in the direction of horizontal framing members supported by the header.

Table 6.15b

Allowable Header Spans for

Headers Supporting Roof and Ceiling Only1,2

33 ksi

| Nominal Member | 50 psf Ground Snow Load |
| --- | --- |
| 70 psf Ground Snow Load |
|  | Size3 | Building Width4 |
| Building Width4 |
| 24' | 28' | 32' | 36' | 24' | 28' | 32' | 36' |
| 2-2 x 4 x 33 | 3'-0" | 2'-7" | 2'-4" | 2'-1" | 2'-4" | 2'-1" | -- | -- |
| 2-2 x 4 x 43 | 3'-10" | 3'-7" | 3'-4" | 3'-2" | 3'-5" | 3'-2" | 3'-0" | 2'-9" |
| 2-2 x 4 x 54 | 4'-3" | 4'-0" | 3'-9" | 3'-7" | 3'-10" | 3'-7" | 3'-4" | 3'-2" |
| 2-2 x 4 x 68 | 4'-10" | 4'-6" | 4'-3" | 4'-0" | 4'-3" | 4'-0" | 3'-9" | 3'-7" |
| 2-2x 4 x 97 | 5'-8" | 5'-4" | 5'-0" | 4'-9" | 5'-1" | 4'-9" | 4'-5" | 4'-3" |
| 2-2x 6 x 33 | 2'-6" | 2'-2" | -- | -- | -- | -- |
| 2-2 x 6 x 43 | 5'-2" | 4'-10" | 4'-4" | 3'-11" | 4'-5" | 3'-10" | 3'-5" | 3'-1" |
| 2-2x 6 x 54 | 5'-10" | 5'-5" | 5'-1" | 4'-10" | 5'-2" | 4'-10" | 4'-7" | 4'-4" |
| 2-2 x 6 x 68 | 6'-6" | 6'-1" | 5'-9" | 5'-6" | 5'-10" | 5'-5" | 5'-1" | 4'-10" |
| 2-2 x 6 x 97 | 7'-10" | 7'-3" | 6'-10" | 6'-5" | 6'-11" | 6'-6" | 6'-1" | 5'-9" |
| 2-2 x 8 x 33 | -- | -- | -- | -- | -- | -- | -- | -- |
| 2-2 x 8 x 43 | 4'-3" | 3'-9" | 3'-4" | 3'-0" | 3'-4" | 2'-11" | 2'-7" | 2'-4" |
| 2-2x 8 x 54 | 7'-7" | 7'-1" | 6'-7" | 5'-11" | 6'-9" | 5'-10" | 5'-3" | 4'-8" |
| 2-2 x 8 x 68 | 8'-6" | 8'-0" | 7'-6" | 7'-2" | 7'-7" | 7'-1" | 6'-8" | 6'-4" |
| 2-2 x 8 x 97 | 10'-3" | 9'-7" | 9'-0" | 8'-7" | 9'-1" | 8'-6" | 8'-0" | 7'-7" |
| 2-2 x 10 x 43 | 3'-7" | 3'-1" | 2'-9" | 2'-6" | 2'-10" | 2'-6" | 2'-2" | -- |
| 2-2 x 10 x 54 | 7'-1" | 6'-2" | 5'-6" | 4'-11" | 5'-7" | 4'-11" | 4'-4" | 3'-11" |
| 2-2 x 10 x 68 | 10'-1" | 9'-5" | 8'-10" | 8'-5" | 8'-11" | 8'-4" | 7'-11" | 7'-6" |
| 2-2 x 10 x 97 | 12'-1" | 11'-4" | 10'-8" | 10'-1" | 10'-9" | 10'-1" | 9'-6" | 9'-0" |
| 2-2 x 12 x 43 | 3'-1" | 2'-8" | 2'-4" | 2'-2" | 2'-5" | 2'-1" | -- | -- |
| 2-2 x 12 x 54 | 6'-1" | 5'-4" | 4'-9" | 4'-3" | 4'-10" | 4'-2" | 3'-9" | 3'-4" |
| 2-2 x 12 x 68 | 10'-9" | 10'-1" | 9'-6" | 8'-6" | 9'-7" | 8'-5" | 7'-6" | 6'-9" |
| 2-2 x 12 x 97 | 13'-11" | 13'-0" | 12'-3" | 11'-8" | 12'-5" | 11'-7" | 10'-11" | 10'-4" |

For SI:	1 inch = 25.4 mm,    1 psf = 0.0479 kN/m2,  1 foot = 0.3 m.

1		Deflection criteria: L/360 for live loads, L/240 for total loads.

2		Design load assumptions:

Roof dead load is 7 psf  (0.335 kN/m2)

Ceiling dead load is 5 psf (0.24 kN/m2)

Attic live load is 10 psf (0.479 kN/m2)

3		Refer to Table 2.1 for actual size

4		Building width is in the direction of horizontal framing members supported by the header.

Table 6.16a

Allowable Header Spans for

Headers Supporting One Floor, Roof and Ceiling1,2

33 ksi

| Nominal Member | 20 psf Ground Snow Load |
| --- | --- |
| 30 psf Ground Snow Load |
|  | Size3 | Building Width4 |
| Building Width4 |
| 24' | 28' | 32' | 36' | 24' | 28' | 32' | 36' |
| 2-2 x 4 x 33 | 2'-3" | -- | -- | -- | 2'-2" | -- | -- | -- |
| 2-2 x 4 x 43 | 3'-4" | 3'-1" | 2'-11" | 2'-9" | 3'-3" | 3'-1" | 2'-11" | 2'-8" |
| 2-2 x 4 x 54 | 3'-9" | 3'-6" | 3'-4" | 3'-2" | 3'-8" | 3'-6" | 3'-3" | 3'-1" |
| 2-2 x 4 x 68 | 4'-2" | 3'-11" | 3'-9" | 3'-6" | 4'-1" | 4'-0" | 3'-8" | 3'-6" |
| 2-2x 4 x 97 | 4'-11" | 4'-8" | 4'-5" | 4'-2" | 4'-11" | 4'-7" | 4'-4" | 4'-2" |
| 2-2x 6 x 33 | -- | -- | -- | -- | -- | -- | -- | -- |
| 2-2 x 6 x 43 | 4'-2" | 3'-9" | 3'-4" | 3'-0" | 4'-1" | 3'-8" | 3'-3" | 3'-0" |
| 2-2x 6 x 54 | 5'-1" | 4'-9" | 4'-6" | 4'-3" | 5'-0" | 4'-8" | 4'-5" | 4'-3" |
| 2-2 x 6 x 68 | 5'-8" | 5'-4" | 5'-1" | 4'-10" | 5'-7" | 5'-3" | 5'-0" | 4'-9" |
| 2-2 x 6 x 97 | 6'-9" | 6'-4" | 6'-0" | 5'-9" | 6'-8" | 6'-4" | 6'-0" | 5'-8" |
| 2-2 x 8 x 33 | -- | -- | -- | -- | -- | -- | -- | -- |
| 2-2 x 8 x 43 | 3'-3" | 2'-10" | 2'-7" | 2'-4" | 3'-2" | 2'-9" | 2'-6" | 2'-3" |
| 2-2x 8 x 54 | 6'-5" | 5'-8" | 5'-1" | 4'-7" | 6'-3" | 5'-7" | 5'-0" | 4'-6" |
| 2-2 x 8 x 68 | 7'-5" | 7'-0" | 6'-7" | 6'-4" | 7'-4" | 6'-11" | 6'-6" | 6'-3" |
| 2-2 x 8 x 97 | 8'-11" | 8'-4" | 7'-11" | 7'-7" | 8'-9" | 8'-3" | 7'-10" | 7'-5" |
| 2-2 x 10 x 43 | 2'-8" | 2'-5" | 2'-2" | 2'-0" | 2'-8" | 2'-4" | 2'-1" | 2'-0" |
| 2-2 x 10 x 54 | 5'-4" | 4'-9" | 4'-3" | 3'-10" | 5'-3" | 4'-8" | 4'-2" | 3'-9" |
| 2-2 x 10 x 68 | 8'-9" | 8'-3" | 7'-10" | 7'-5" | 8'-8" | 8'-2" | 7'-8" | 7'-4" |
| 2-2 x 10 x 97 | 10'-6" | 9'-11" | 9'-4" | 8'-11" | 10'-5" | 9'-9" | 9'-3" | 8'-10" |
| 2-2 x 12 x 43 | 2'-4" | 2'-1" | -- | -- | 2'-3" | -- | -- | -- |
| 2-2 x 12 x 54 | 4'-7" | 4'-1" | 3'-8" | 3'-4" | 4'-6" | 4'-0" | 3'-7" | 3'-3" |
| 2-2 x 12 x 68 | 9'-3" | 8'-2" | 7'-4" | 6'-8" | 9'-0" | 8'-0" | 7'-2" | 6'-6" |
| 2-2 x 12 x 97 | 12'-1" | 11'-5" | 10'-9" | 10'-3" | 12'-0" | 11'-3" | 10'-8" | 10'-2" |

For SI:	1 inch = 25.4 mm,    1 psf = 0.0479 kN/m2,  1 foot = 0.3 m.

1		Deflection criteria: L/360 for live loads, L/240 for total loads.

2		Design load assumptions:	Roof dead load is 7 psf  (0.335 kN/m2)

Ceiling dead load is 5 psf (0.24 kN/m2)

Attic live load is 10 psf (0.479 kN/m2)

Second floor live load is 30 psf (1.437 kN/m2)

Second floor dead load is 10 psf (0.479 kN/m2)

Second floor wall dead load is 10 psf (0.479 kN/m2)

3		Refer to Table 2.1 for actual size.

4		Building width is in the direction of horizontal framing members supported by the header.

Table 6.16b

Allowable Header Spans for

Headers Supporting One Floor, Roof and Ceiling 1,2

33 ksi

| Nominal Member | 50 psf Ground Snow Load |
| --- | --- |
| 70 psf Ground Snow Load |
|  | Size3 | Building Width4 |
| Building Width4 |
| 24' | 28' | 32' | 36' | 24' | 28' | 32' | 36' |
| 2-2 x 4 x 33 | - | - | - | - | - | - | - | - |
| 2-2 x 4 x 43 | 3'-1" | 2'-11" | 2'-8" | 2'-5" | 2'-10" | 2'-6" | 2'-3" | 2'-1" |
| 2-2 x 4 x 54 | 3'-6" | 3'-3" | 3'-1" | 3'-0" | 3'-3" | 3'-0" | 2'-10" | 2'-9" |
| 2-2 x 4 x 68 | 3'-11" | 3'-8" | 3'-6" | 3'-4" | 3'-7" | 3'-5" | 3'-2" | 3'-1" |
| 2-2x 4 x 97 | 4'-8" | 4'-4" | 4'-2" | 3'-11" | 4'-3" | 4'-0" | 3'-10" | 3'-7" |
| 2-2x 6 x 33 | - | - | - | - | - | - | - | - |
| 2-2 x 6 x 43 | 3'-8" | 3'-3" | 2'-11" | 2'-8" | 3'-2" | 2'-9" | 2'-6" | 2'-3" |
| 2-2x 6 x 54 | 4'-9" | 4'-6" | 4'-3" | 4'-0" | 4'-4" | 4'-1" | 3'-11" | 3'-8" |
| 2-2 x 6 x 68 | 5'-4" | 5'-0" | 4'-9" | 4'-6" | 4'-11" | 4'-7" | 4'-4" | 4'-2" |
| 2-2 x 6 x 97 | 6'-4" | 6'-0" | 5'-8" | 5'-5" | 5'-10" | 5'-6" | 5'-3" | 4'-11" |
| 2-2 x 8 x 33 | -- | -- | -- | -- | -- | -- | -- | -- |
| 2-2 x 8 x 43 | 2'-10" | 2'-6" | 2'-3" | -- | 2'-5" | 2'-2" | -- | -- |
| 2-2x 8 x 54 | 5'-8" | 5'-0" | 4'-6" | 4'-1" | 4'-10" | 4'-3" | 3'-10" | 3'-5" |
| 2-2 x 8 x 68 | 7'-0" | 6'-7" | 6'-2" | 5'-11" | 6'-5" | 6'-0" | 5'-8" | 5'-5" |
| 2-2 x 8 x 97 | 8'-4" | 7'-10" | 7'-5" | 7'-1" | 7'-8" | 7'-3" | 6'-10" | 6'-6" |
| 2-2 x 10 x 43 | 2'-4" | 2'-1" | -- | -- | -- | -- | -- | -- |
| 2-2 x 10 x 54 | 4'-9" | 4'-2" | 3'-9" | 3'-5" | 4'-0" | 3'-6" | 3'-2" | 2'-10" |
| 2-2 x 10 x 68 | 8'-3" | 7'-9" | 7'-4" | 6'-10" | 7'-7" | 7'-1" | 6'-5" | 5'-9" |
| 2-2 x 10 x 97 | 9'-10" | 9'-3" | 8'-9" | 8'-4" | 9'-1" | 8'-7" | 8'-1" | 7'-8" |
| 2-2 x 12 x 43 | -- | -- | -- | -- | -- | -- | -- | -- |
| 2-2 x 12 x 54 | 4'-0" | 3'-7" | 3'-2" | 2'-11" | 3'-5" | 3'-0" | 2'-9" | 2'-5" |
| 2-2 x 12 x 68 | 8'-2" | 7'-2" | 6'-5" | 5'-10" | 6'-11" | 6'-1" | 5'-6" | 4'-11" |
| 2-2 x 12 x 97 | 11'-4" | 10'-8" | 10'-1" | 9'-8" | 10'-6" | 9'-0" | 9'-4" | 8'-10" |

For SI:	1 inch = 25.4 mm,    1 psf = 0.0479 kN/m2,  1 foot = 0.3 m.

1		Deflection criteria: L/360 for live loads, L/240 for total loads.

2		Design load assumptions:	Roof dead load is 7 psf  (0.335 kN/m2)

Ceiling dead load is 5 psf (0.24 kN/m2)

Attic live load is 10 psf (0.479 kN/m2)

Second floor live load is 30 psf (1.437 kN/m2)

Second floor dead load is 10 psf (0.479 kN/m2)

Second floor wall dead load is 10 psf (0.479 kN/m2)

3		Refer to Table 2.1 for actual size.

4		Building width is in the direction of horizontal framing members supported by the header.

Table 6.17a

Allowable Header Spans for

Headers Supporting One Floor, Roof and Ceiling1,2

First story of a two-story building with center load bearing Beam

33 ksi

| Nominal Member | 20 psf Ground Snow Load |
| --- | --- |
| 30 psf Ground Snow Load |
|  | Size3 | Building Width4 |
| Building Width4 |
| 24' | 28' | 32' | 36' | 24' | 28' | 32' | 36' |
| 2-2 x 4 x 33 | 2'-10" | 2'-6" | 2'-3" | - | 2'-7" | 2'-3" | - | - |
| 2-2 x 4 x 43 | 3'-9" | 3'-6" | 3'-4" | 3'-2" | 3'-7" | 3'-4" | 3'-2" | 3'-0" |
| 2-2 x 4 x 54 | 4'-2" | 4'-0" | 3'-9" | 3'-7" | 4'-0" | 3'-9" | 3'-7" | 3'-5" |
| 2-2 x 4 x 68 | 4'-8" | 4'-5" | 4'-2" | 4'-0" | 4'-6" | 4'-2" | 4'-0" | 3'-10" |
| 2-2x 4 x 97 | 5'-6" | 5'-3" | 5'-0" | 4'-9" | 5'-3" | 5'-0" | 4'-9" | 4'-6" |
| 2-2x 6 x 33 | 2'-5" | 2'-2" | - | - | 2'-2" | - | - | - |
| 2-2 x 6 x 43 | 3'-6" | 5'-1" | 4'-9" | 4'-3" | 4'-10" | 4'-3" | 3'-10" | 3'-6" |
| 2-2x 6 x 54 | 5'-8" | 5'-4" | 5'-1" | 4'-10" | 5'-5" | 5'-1" | 4'-10" | 4'-7" |
| 2-2 x 6 x 68 | 6'-5" | 6'-0" | 5'-9" | 5'-6" | 6'-1" | 5'-9" | 5'-5" | 5'-2" |
| 2-2 x 6 x 97 | 7'-8" | 7'-2" | 6'-10" | 6'-6" | 7'-3" | 6'-10" | 6'-6" | 6'-2" |
| 2-2 x 8 x 33 | - | - | - | - | - | - | - | - |
| 2-2 x 8 x 43 | 4'-2" | 3'-8" | 3'-3" | 3'-0" | 3'-8" | 3'-3" | 2'-11" | 2'-8" |
| 2-2x 8 x 54 | 7'-5" | 7'-0" | 6'-6" | 6'-0" | 7'-1" | 6'-6" | 5'-10" | 5'-4" |
| 2-2 x 8 x 68 | 8'-4" | 7'-11" | 7'-6" | 7'-1" | 7'-11" | 7'-6" | 7'-1" | 6'-9" |
| 2-2 x 8 x 97 | 10'-0" | 9'-9" | 9'-0" | 8'-6" | 9'-6" | 9'-0" | 8'-6" | 8'-1" |
| 2-2 x 10 x 43 | 3'-5" | 3'-0" | 2'-9" | 2'-6" | 3'-1" | 2'-9" | 2'-6" | 2'-3" |
| 2-2 x 10 x 54 | 6'-10" | 6'-0" | 5'-6" | 5'-0" | 6'-2" | 5'-5" | 4'-11" | 4'-5" |
| 2-2 x 10 x 68 | 9'-10" | 9'-4" | 8'-10" | 8'-5" | 9'-4" | 8'-10" | 8'-4" | 8'-0" |
| 2-2 x 10 x 97 | 11'-10" | 11'-2" | 10'-7" | 10'-1" | 11'-3" | 10'-7" | 10'-1" | 9'-7" |
| 2-2 x 12 x 43 | 2'-11" | 2'-7" | 2'-4" | 2'-1" | 2'-8" | 2'-4" | - | - |
| 2-2 x 12 x 54 | 5'-10" | 5'-2" | 4'-8" | 4'-3" | 5'-3" | 4'-8" | 4'-2" | 3'-10" |
| 2-2 x 12 x 68 | 10'-6" | 10'-0" | 9'-5" | 8'-6" | 9'-12" | 9'-5" | 8'-5" | 7'-8" |
| 2-2 x 12 x 97 | 13'-8" | 12'-10" | 12'-2" | 11'-8" | 13'-0" | 12'2" | 11'-7" | 11'-1" |

For SI:	1 inch = 25.4 mm,    1 psf = 0.0479 kN/m2,  1 foot = 0.3 m.

1		Deflection criteria: L/360 for live loads, L/240 for total loads.

2		Design load assumptions:	Roof dead load is 7 psf  (0.335 kN/m2)

Ceiling dead load is 5 psf (0.24 kN/m2)

Attic live load is 10 psf (0.479 kN/m2)

Second floor live load is 30 psf (1.437 kN/m2)

Second floor dead load is 10 psf (0.479 kN/m2)

Second floor wall dead load is 10 psf (0.479 kN/m2)

3		Refer to Table 2.1 for actual size.

4		Building width is in the direction of horizontal framing members supported by the header.

Table 6.17b

Allowable Header Spans for

Headers Supporting One Floor, Roof and Ceiling 1,2

First story of a two-story building with center load bearing Beam

33 ksi

| Nominal Member | 50 psf Ground Snow Load |
| --- | --- |
| 70 psf Ground Snow Load |
|  | Size 3 | Building Width 4 |
| Building Width 4 |
| 24' | 28' | 32' | 36' | 24' | 28' | 32' | 36' |
| 2-2 x 4 x 33 | 2'-2" | - | - | - | - | - | - | - |
| 2-2 x 4 x 43 | 3'-3" | 3'-1" | 2'-11" | 2'-8" | 3'-0" | 2'-9" | 2'-6" | 2'-3" |
| 2-2 x 4 x 54 | 3'-8" | 3'-5" | 3'-3" | 3'-1" | 3'-5" | 3'-2" | 3'-0" | 2'-10" |
| 2-2 x 4 x 68 | 4'-1" | 3'-10" | 3'-8" | 3'-6" | 3'-9" | 3'-7" | 3'-4" | 3'-2" |
| 2-2x 4 x 97 | 4'-10" | 4'-7" | 4'-4" | 4'-1" | 4'-6" | 4'-3" | 4'-0" | 3'-10" |
| 2-2x 6 x 33 | - | - | - | - | - | - | - | - |
| 2-2 x 6 x 43 | 4'-0" | 3'-7" | 3'-2" | 2'-11" | 3'-5" | 3'-1" | 2'-9" | 2'-6" |
| 2-2x 6 x 54 | 4'-11" | 4'-8" | 4'-5" | 4'-2" | 4'-7" | 4'-4" | 4'-1" | 3'-11" |
| 2-2 x 6 x 68 | 5'-7" | 5'-3" | 4'-11" | 4'-9" | 5'-2" | 4'-10" | 4'-7" | 4'-4" |
| 2-2 x 6 x 97 | 6'-8" | 6'-3" | 5'-11" | 5'-7" | 6'-2" | 5'-9" | 5'-6" | 5'-2" |
| 2-2 x 8 x 33 | - | - | - | - | - | - | - | - |
| 2-2 x 8 x 43 | 3'-1" | 2'-9" | 2'-5" | 2'-3" | 2'-8" | 2'-4" | - | - |
| 2-2x 8 x 54 | 6'-2" | 5'-5" | 4'-11" | 4'-5" | 5'-3" | 4'-8" | 4'-2" | 3'-9" |
| 2-2 x 8 x 68 | 7'-3" | 6'-10" | 6'-6" | 6'-2" | 6'-9" | 6'-4" | 6'-0" | 5'-8" |
| 2-2 x 8 x 97 | 8'-8" | 8'-2" | 7'-9" | 7'-5" | 8'-1" | 7'-7" | 7'-2" | 6'-10" |
| 2-2 x 10 x 43 | 2'-7" | 2'-3" | 2'-1" | - | 2'-3" | - | - | - |
| 2-2 x 10 x 54 | 5'-1" | 4'-6" | 4'-1" | 3'-8" | 4'-5" | 3'-11" | 3'-6" | 3'-2" |
| 2-2 x 10 x 68 | 8'-7" | 8'-1" | 7'-8" | 7'-3" | 7'-11" | 7'-6" | 7'-0" | 6'-4" |
| 2-2 x 10 x 97 | 10'-3" | 9'-8" | 9'-2" | 8'-9" | 9'-6" | 9'-0" | 8'-6" | 8'-1" |
| 2-2 x 12 x 43 | 2'-3" | - | - | - | - | - | - | - |
| 2-2 x 12 x 54 | 4'-5" | 3'-11" | 3'-6" | 3'-2" | 3'-9" | 3'-4" | 3'-0" | 2'-8" |
| 2-2 x 12 x 68 | 8'-10" | 7'-10" | 7'-0" | 6'-4" | 7'-7" | 6'-9" | 6'-0" | 5'-5" |
| 2-2 x 12 x 97 | 11'-10" | 11'-2" | 10'-7" | 10'-1" | 11'-0" | 10'-4" | 9'-9" | 9'-4" |

For SI:	1 inch = 25.4 mm,    1 psf = 0.0479 kN/m2,  1 foot = 0.3 m.

1		Deflection criteria: L/360 for live loads, L/240 for total loads.

2		Design load assumptions:	Roof dead load is 7 psf  (0.335 kN/m2)

Ceiling dead load is 5 psf (0.24 kN/m2)

Attic live load is 10 psf (0.479 kN/m2)

Second floor live load is 30 psf (1.437 kN/m2)

Second floor dead load is 10 psf (0.479 kN/m2)

Second floor wall dead load is 10 psf (0.479 kN/m2)

3		Refer to Table 2.1 for actual size.

4		Building width is in the direction of horizontal framing members supported by the header.

Table 6.18

Total Number of Jack and King Studs Required at Each End of an Opening

| Size of Opening | 24" o.c. Stud Spacing |
| --- | --- |
| 16" o.c. Stud Spacing |
| No. of Jack Studs | No. of King Studs | No. of Jack Studs | No. of King Studs |
| Up to 3'-6" | 1 | 1 | 1 | 1 |
| > 3'-6" to 5'-0" | 1 | 2 | 1 | 2 |
| > 5'-0" to 5'-6" | 1 | 2 | 2 | 2 |
| > 5'-6" to 8'-0" | 1 | 2 | 2 | 2 |
| > 8'-0" to 10'-6" | 2 | 2 | 2 | 3 |
| > 10'-6" to 12'-0" | 2 | 2 | 3 | 3 |
| > 12'-0" to 13'-0" | 2 | 3 | 3 | 3 |
| > 13'-0" to 14'-0" | 2 | 3 | 3 | 4 |
| > 14'-0" to 16'-0" | 2 | 3 | 3 | 4 |
| > 16'-0" to 18'-0" | 3 | 3 | 4 | 4 |

For SI:	1 inch = 25.4 mm,    1 foot = 0.3 m.

Table 6.19

Number of Screws Required for Header to King Stud Connection

| Header Span |
| --- |
| Wind Speed (mph), Exposure & Seismic Zones 1,2,3 |
|  | Up to 70 A/B or Zones 0, 1, 2,3 or 4 | Up to 90 A/B or 70 C | Up to 100 A/B or 90C | Up to 110 C |
| £ 4' |
| 4 - #8 screws | 4 - #8 screws | 6 - #8 screws | 8 - #8 screws |
| > 4' to 8' |
| 4 - #8 screws | 4 - #8 screws | 8 - #8 screws | 12 - #8 screws |
| > 8' to 12' |
| 4 - #8 screws | 6 - #8 screws | 10 - #8 screws | 16 - #8 screws |
| > 12' to 16' |
| 4 - #8 screws | 8 - #8 screws | 12 - #8 screws | 20 - #8 screws |

For SI:	1 inch = 25.4 mm,  1 foot = 0.3 m,  1 mph = 1.61 km/hr.

1		For headers located on the first floor of a two-story building, the total number of screws

may be reduced by 2 screws, but the total number of screws shall be no less than 4.

2		For roof slopes of 6:12 or greater, the required number of screws may be reduced by 1/2,

but the total number of screws shall be no less than 4.

3		All screw sizes shown are minimums.

Table 6.20

Minimum Percentage of Full Height

Structural Sheathing Along Exterior Wall Lines1,2,3,4

| Wall Condition | Roof Slope | Wind Speed (mph) and Exposure |
| --- | --- | --- |

Up To 70 C or 90 A/B

| or Seismic Zones 0, 1, & 2 |
| --- |
| Up To 90 C or 100 A/B |
|  | Endwall | Sidewall | Endwall | Sidewall |
| One-Story or | 3:12 | 30% | 30% | 30% | 30% |
| Second Floor of | 6:12 | 30% | 30% | 40% | 30% |
| Two-Story | 9:12 | 45% | 30% | 75% | 50% |
| Construction | 12:12 | 60% | 40% | 100% | 70% |
| First Floor of | 3:12 | 50% | 35% | 80% | 55% |
| Two-Story | 6:12 | 55% | 40% | 90% | 60% |
| Construction | 9:12 | 75% | 50% | Design Required |
| 12:12 | 95% | 65% |

For SI:	1 mph = 49 m/sec,  1 inch = 25.4 mm, 1 foot = 304.8 mm

1	Sidewalls shall be those walls parallel to the ridge and endwalls shall be those walls perpendicular to 	the 	ridge.  If sidewalls are shorter in length than endwalls, then the higher percentage value shall be used for 	both walls.

2	Linear interpolation shall be permitted for values of the roof slope and wind speeds other than 	shown.

3	A 48-inch-wide (1219 mm) panel of structural sheathing shall be located at each end of a wall or as near 	thereto as possible.  Individual segments of wall (i.e. between openings) with full-height sheathing shall be 	at least 48 inches (1219 mm) in length to count toward the length of full-height sheathing required by the 	tabulated percentages.

4	Percentages are given as percentages of the total wall length.  For example, a 48-foot (14.6 m) long wall 	that requires 30% of full-height sheathing would result in 0.30x48 = 14.4 feet (4.4 m) of wall with full-	height sheathing.  In addition to the remainder of the wall without openings, areas above or 	below 	openings would also be sheathed.

7.0	NON-STRUCTURAL WALLS

7.1	Non-Load Bearing Studs

Non-load bearing steel framing shall comply with ASTM C 645 [11] and shall have a minimum base metal thickness of 18 mils (0.45 mm).

.

7.2	Construction Details

Figure 7.1 is provided for informational purposes only.  Alternate framing details may be used when appropriate.

Figure 7.1		Typical Interior Non-Load Bearing Wall Detail

8.0	STEEL ROOF FRAMING

8.1	Roof Construction

Steel roof systems constructed in accordance with this section shall consist of both ceiling joists and rafters in accordance with Figures 8.1 through 8.7 or trusses in accordance with Section 8.9.  Steel roof framing materials shall comply with the provisions of Section 2.0.  Connections shall comply with Tables 8.1 through 8.3 and with other requirements in this section.

8.1.1	Applicability Limits

The applicability limits of Section 1.3 and Table 1.1 shall apply.

8.1.2	In-line Framing

Ceiling joists shall be located directly in-line with load bearing studs below with a maximum tolerance of 3/4-inch (19 mm) between the centerlines of the stud and the ceiling joist.

8.2	Allowable Ceiling Joist Spans

The maximum clear span of cold-formed steel ceiling joists shall be determined in accordance with Figure 8.1 and Tables 8.4 through 8.11.  Ceiling joists shall have a minimum bearing length of 1-1/2 inch (38 mm) and shall be connected to rafters (heel joint) in accordance with Figure 8.2 and Table 8.2. When continuous joists are used across interior bearing supports, the interior bearing supports shall be located within 2 feet (610 mm) of mid-span of the ceiling joist, and the individual spans shall not exceed the applicable spans in Tables 8.4 through 8.11.  Where required in Tables 8.4 through 8.11, bearing stiffeners shall be installed at each bearing and concentrated load location in accordance with Section 2.9 and Figure 8.4.  When the attic is to be used as an occupied space, the ceiling joists shall be designed in accordance with Section 5.0.

8.3	Ceiling Joist Bracing

The bottom flanges of steel ceiling joists shall be laterally braced by the application of gypsum board installed with minimum #6 screws in accordance with applicable building code requirements or with 1-1/2 inch x 33 mil (38 mm x 0.84 mm) continuous steel strapping installed perpendicular to the joist run at a maximum spacing of 4 feet (1.2 m).  Straps shall be fastened to the bottom flange at each joist with at least one #8 screw and shall be fastened to blocking with at least two #8 screws.  Blocking or bridging (X-bracing) shall be installed between joists at a maximum spacing of 12 feet (3.7m) measured along a line of continuous strapping (perpendicular to the joist run).  Blocking or bridging shall also be located at the termination of all straps.

The top flanges of steel ceiling joists shall be laterally braced with a minimum 33 mil (0.84 mm) C-shaped member, 33 mil (0.84 mm) track section, or 1-1/2 inch x 33 mil (38 mm x 0.84 mm) continuous steel strapping as required in Tables 8.4 through 8.11.  Lateral bracing shall be installed perpendicular to the ceiling joist run in accordance with Figure 8.1.  C-shaped members (i.e. studs), tracks, or straps shall be fastened to the top flange at each joist with at least one #8 screw and shall be fastened to blocking with at least two #8 screws.  Blocking or bridging (X-bracing) shall be installed between joists in-line with strap bracing at a maximum spacing of 12 feet (3.7 m) measured perpendicular to the joists, and at the termination of all straps.  The third point bracing span values from Tables 8.4 through 8.11 shall be used for straps installed at closer spacings than third point bracing, or when sheathing is applied to the top of the ceiling joists.

8.4	Allowable Rafter Spans

The horizontal projection of the rafter span, as shown in Figure 8.1,  shall not exceed the limits set forth in Table 8.12.  Wind speeds shall be converted to equivalent ground snow load in accordance with Table 8.13.  Rafter spans shall be selected based on the higher of the ground snow load or the equivalent snow load converted from the wind speed.  When used to achieve reduced rafter sizes, a rafter support brace shall be a minimum of 2 x 4 x 33 mil C-shaped member with maximum length of 8 feet (2.4 m) and shall be connected to a ceiling joist and rafter with 4 # 10 screws at each end.

Rafters shall be connected to a parallel ceiling joist to form a continuous tie between exterior walls in accordance with Figure 8.1, Figure 8.2 and Table 8.2.  Rafters shall be connected to a ridge member with a minimum 2-inch x 2-inch (51 mm x 51 mm) clip angle fastened with minimum #10 screws to the ridge member in accordance with Figure 8.3 and Table 8.3.  The clip angle shall have a steel thickness equivalent to or greater than the rafter thickness and shall extend the depth of the rafter member.  The ridge member shall be fabricated from a C-shaped member and a track section, which shall have a minimum size and steel thickness equivalent to or greater than the adjacent rafters and shall be installed in accordance with Figure 8.3.  The rafter member shall extend the full depth of the sloped rafter cut.

8.4.1	Roof Overhangs

Roof overhangs shall not exceed 24 inches (610 mm) in accordance with Figure 8.1.

8.5	Rafter Bottom Flange Bracing.

The bottom flanges of steel rafters shall be continuously braced with a minimum 33 mil (0.84 mm) C-shaped member, 33 mil (0.84 mm) track section, or 1-1/2 inch x 33 mil (38 mm x 0.836 mm) steel strapping at a maximum spacing of 8 feet (2.4 m) as measured parallel to the rafters.  Bracing shall be installed in accordance with Figure 8.1.  The C-shaped member, track section, or straps shall be fastened to the bottom flange of each rafter with at least one #8 screw and shall be fastened to blocking with at least two #8 screws.  Blocking or bridging (X-bracing) shall be installed between rafters in-line with the continuous bracing at a maximum spacing of 12 feet (3.7 m) measured perpendicular to the rafters.  The ends of continuous bracing shall be fastened to blocking or anchored to a stable building component with at least two #8 screws.

8.6	Splicing

Rafters and other structural members shall not be spliced with the exception of ceiling joist splices over load bearing walls.  Splices in ceiling joists shall be supported at interior bearing points and shall be constructed in accordance with Figure 8.5.  Spliced ceiling joists shall be connected with the same number and size of screws on each side of the splice as required for the ceiling joist to rafter connection (Table 8.2).  Splicing of tracks used as a facia connected to the ends of rafters shall conform with Figure 5.11.

8.7	Framing of Openings

Openings in roof and ceilings shall be framed with headers and trimmers between ceiling joists or rafters.  Header joist spans shall not exceed 4 feet (1.2 m).  Header and trimmer joists shall be fabricated from joist and track members having a minimum size and thickness at least equivalent to the adjacent ceiling joists or rafters and shall be installed in accordance with Figures 8.6 and 8.7.  Each header joist shall be connected to trimmer joist with a minimum of four 2-inch x 2-inch (51 x 51 mm) clip angles.  Each clip angle shall be fastened to both the header and trimmer joists with four #8 screws, evenly spaced, through each leg of the clip angle.  The clip angles shall have a steel thickness not less than that of the ceiling joist or rafter.

8.8	Roof Trusses

Trusses shall be engineered and installed in accordance with the applicable building code requirements and good practices. Roof bracing shall be installed in accordance with the truss design.  All trusses shall be aligned with load carrying members (i.e. studs) in the wall.  Refer to AISI publication RG-9518 [17] for additional guidance.

8.9	Roof Tie-Downs

In high wind conditions, an approved uplift connector (i.e. strap or bracket) shall be used to attach individual ceiling joists or rafters to a wall stud below.  Approved uplift connectors shall meet or exceed the uplift loads specified in Table 8.14.

Figure 8.1	Steel Roof Construction

Figure 8.2	Heel Joint Connection

Figure 8.3		Ridge Member Connection

Figure 8.4	Bearing Stiffener

Figure 8.5	Spliced Ceiling Joists

Figure 8.6	Roof or Ceiling Opening

Figure 8.7	Header to Trimmer Detail

Table 8.1

Roof Framing Fastening Schedule

| Description of Building Elements | Number and Size of Fasteners | Number and Spacing of Fasteners |
| --- | --- | --- |
| Ceiling joist to top track of load bearing wall1 | 2 - No. 10 screws | Each joist |

Roof sheathing (oriented strand board or plywood) to rafters

No. 8 screws

|  | 6" o.c. on edges and 12" o.c. at interior supports. (6" o.c. at gable end truss) |
| --- | --- |
| Truss to bearing wall 1 | 2 - No. 10 screws | Each truss |
| Gable end truss to endwall top track | No. 10 screws | 12" oc. |
| Rafter to ceiling joist or ridge member | Minimum No. 10 screws | See Tables 8.2 and 8.3 |

For SI:	1 inch = 25.4 mm,    1 foot = 0.3 m,    1 psf = 0.0479 kN/m2.

1		Screws shall be applied through the flanges of the truss or ceiling joist or a 54 mil clip

angle shall be used with 2 # 10 screws in each leg.  See Section 8.10 for additional

requirements to resist uplift forces.

Table 8.2

Number of Screws Required For Ceiling Joist to Rafter Connections1

| Roof | Building Width (feet) |
| --- | --- |
|  | Slope | 24' |
| 28' |
| 32' |
| 36' |
| Ground Snow Load (psf) |
| Ground Snow Load (psf) |
| Ground Snow Load (psf) |
| Ground Snow Load (psf) |
| 20 | 30 | 50 | 70 | 20 | 30 | 50 | 70 | 20 | 30 | 50 | 70 | 20 | 30 | 50 | 70 |
| 3/12 | 5 | 6 | 9 | 12 | 6 | 7 | 10 | 13 | 7 | 8 | 12 | 15 | 8 | 9 | 13 | 17 |
| 4/12 | 4 | 5 | 7 | 9 | 5 | 6 | 8 | 10 | 6 | 6 | 9 | 12 | 6 | 7 | 10 | 13 |
| 5/12 | 4 | 4 | 6 | 7 | 4 | 5 | 7 | 9 | 5 | 5 | 8 | 10 | 5 | 6 | 9 | 11 |
| 6/12 | 3 | 4 | 5 | 7 | 4 | 4 | 6 | 8 | 4 | 5 | 7 | 9 | 4 | 5 | 7 | 10 |
| 7/12 | 3 | 3 | 5 | 6 | 3 | 4 | 5 | 7 | 4 | 4 | 6 | 8 | 4 | 5 | 7 | 9 |
| 8/12 | 3 | 3 | 4 | 5 | 3 | 3 | 5 | 6 | 3 | 4 | 5 | 7 | 4 | 4 | 6 | 8 |
| 9/12 | 2 | 3 | 4 | 5 | 3 | 3 | 4 | 6 | 3 | 4 | 5 | 6 | 3 | 4 | 6 | 7 |
| 10/12 | 2 | 3 | 4 | 5 | 3 | 3 | 4 | 5 | 3 | 3 | 5 | 6 | 3 | 4 | 5 | 7 |
| 11/12 | 2 | 3 | 4 | 4 | 3 | 3 | 4 | 5 | 3 | 3 | 5 | 6 | 3 | 4 | 5 | 6 |
| 12/12 | 2 | 3 | 3 | 4 | 2 | 3 | 4 | 5 | 3 | 3 | 4 | 6 | 3 | 4 | 5 | 6 |

For SI:	1 inch = 25.4 mm,    1 foot = 0.3 m,    1 psf = 0.0479 kN/m2.

1		Screws shall be # 10 minimum.

Table 8.3

Number of Screws Required at Each Leg of Clip Angle

For Rafter to Ridge Member Connection1

| Building Width | Ground Snow Load (psf) |
| --- | --- |
| (feet) | 0 to 20 | 21 to 30 | 31 to 50 | 51 to 70 |
| 24 | 2 | 3 | 4 | 4 |
| 28 | 2 | 3 | 4 | 5 |
| 32 | 3 | 3 | 4 | 5 |
| 36 | 3 | 4 | 5 | 6 |

For SI:	1 foot = 0.3 m,    1 psf = 0.0479 kN/m2.

1	Screws shall be #10 minimum.

Table  8.4

Allowable Spans For Cold-Formed Steel Ceiling Joists (33 ksi)

Single Spans With Bearing Stiffeners

10 Lbs. per Sq. Ft. Live Load (No Attic Storage) 1,2,3

| Nominal | Lateral Support of Top (Compression) Flange |
| --- | --- |
|  | Joist Size 4 | Unbraced |
| Mid-Span Bracing |
| Third-Point Bracing |
| Spacing (inches) |
| Spacing (inches) |
| Spacing (inches) |
| 16 | 24 | 16 | 24 | 16 | 24 |
| 2 x 4 x 33 | 9'-2" | 8'-3" | 11'-9" | 10'-1" | 11'-9" | 10'-4" |
| 2 x 4 x 43 | 9'-11" | 8'-10" | 12'-10" | 11'-2" | 12'-10" | 11'-2" |
| 2 x 4 x 54 | 10'-8" | 9'-6" | 13'-9" | 12'-0" | 13'-9" | 12'-0" |
| 2 x 4 x 68 | 11'-7" | 10'-4" | 14'-8" | 12'-10" | 14'-8" | 12'-10" |
| 2 x 4 x 97 | 13'-7" | 12'-0" | 16'-2" | 14'-1" | 16'-2" | 14'-1" |
| 2 x 6 x 33 | 10'-5" | 9'-5" | 14'-5" | 12'-8" | 16'-4" | 13'-10" |
| 2 x 6 x 43 | 11'-2" | 10'-1" | 15'-7" | 13'-10" | 18'-0" | 15'-5" |
| 2 x 6 x 54 | 12'-0" | 10'-9" | 16'-7" | 14'-9" | 19'-5" | 16'-8" |
| 2 x 6 x 68 | 12'-11" | 11'-7" | 17'-8" | 15'-10" | 20'-11" | 18'-1" |
| 2 x 6 x 97 | 14'-11" | 13'-2" | 19'-10" | 17'-8" | 23'-2" | 20'-3" |
| 2 x 8 x 33 | 11'-8" | 10'-6" | 16'-5" | 14'-9" | 19'-5" | 16'-7" |
| 2 x 8 x 43 | 12'-6" | 11'-3" | 17'-6" | 15'-10" | 21'-2" | 18'-7" |
| 2 x 8 x 54 | 13'-4" | 11'-11" | 18'-7" | 16'-9" | 22'-7" | 20'-0" |
| 2 x 8 x 68 | 14'-3" | 12'-9" | 19'-8" | 17'-8" | 23'-11" | 21'-4" |
| 2 x 8 x 97 | 16'-2" | 14'-5" | 21'-10" | 19'-6" | 26'-3" | 23'-6" |
| 2 x 10 x 43 | 13'-4" | 12'-1" | 18'-9" | 16'-11" | 22'-11" | 20'-6" |
| 2 x 10 x 54 | 14'-2" | 12'-9" | 19'-10" | 17'-10" | 24'-2" | 21'-9" |
| 2 x 10 x 68 | 15'-2" | 13'-7" | 21'-0" | 18'-11" | 25'-6" | 23'-0" |
| 2 x 10 x 97 | 17'-1" | 15'-2" | 23'-2" | 20'-9" | 27'-11" | 25'-1" |
| 2 x 12 x 43 | 14'-1" | 12'-8" | 19'-10" | 17'-11" | 24'-3" | 21'-6" |
| 2 x 12 x 54 | 15'-0" | 13'-5" | 20'-11" | 18'-11" | 25'-7" | 23'-1" |
| 2 x 12 x 68 | 15'-11" | 14'-4" | 22'-2" | 19'-11" | 27'-0" | 24'-4" |
| 2 x 12 x 97 | 17'-10" | 15'-11" | 24'-4" | 21'-10" | 29'-4" | 26'-5" |

For SI:	1 inch = 25.4 mm,    1 foot = 0.3 m,    1 psf = 0.0479 kN/m2.

1		Bearing stiffeners shall be installed at all bearing and concentrated load locations.

2		Deflection criteria:  L/240 for total loads.

3		Ceiling dead load = 5 psf (0.24 kN/m2)

4		Refer to Table 2.1 for actual size.

Table  8.5

Allowable Spans For Cold-Formed Steel Ceiling Joists (33 ksi)

Two Equal Spans With Bearing Stiffeners

10 Lbs. per Sq. Ft. Live Load (No Attic Storage) 1,2,3,4,5

| Nominal | Lateral Support of Top (Compression Flange) |
| --- | --- |
|  | Joist Size 6 | Unbraced |
| Mid-Span Bracing |
| Third-Point Bracing |
| Spacing (inches) |
| Spacing (inches) |
| Spacing (inches) |
| 16 | 24 | 16 | 24 | 16 | 24 |
| 2 x 4 x 33 | 12'-4" | 10'-11" | 13'-5" | 10'-11" | 13'-5" | 10'-11" |
| 2 x 4 x 43 | 13'-6" | 12'-1" | 16'-4" | 13'-4" | 16'-4" | 13'-4" |
| 2 x 4 x 54 | 14'-9" | 13'-1" | 18'-4" | 15'-0" | 18'-4" | 15'-0" |
| 2 x 4 x 68 | 16'-4" | 14'-5" | 19'-8" | 16'-9" | 19'-8" | 16'-9" |
| 2 x 4 x 97 | 19'-6" | 17'-2" | 21'-8" | 18'-11" | 21'-8" | 18'-11" |
| 2 x 6 x 33 | 14'-0" | 12'-7" | 18'-2" | 14'-10" | 18'-2" | 14'-10" |
| 2 x 6 x 43 | 15'-2" | 13'-7" | 20'-11" | 18'-1" | 22'-1" | 18'-1" |
| 2 x 6 x 54 | 16'-5" | 14'-8" | 22'-5" | 19'-5" | 24'-11" | 20'-4" |
| 2 x 6 x 68 | 17'-11" | 15'-11" | 24'-1" | 21'-5" | 28'-0" | 22'-10" |
| 2 x 6 x 97 | 21'-2" | 18'-8" | 27'-7" | 24'-5" | 31'-1" | 27'-2" |
| 2 x 8 x 33 | 15'-7" | 14'-1" | 21'-3" | 15'-10" | 21'-3" | 15'-10" |
| 2 x 8 x 43 | 16'-10" | 15'-1" | 23'-6" | 21'-2" | 27'-6" | 22'-5" |
| 2 x 8 x 54 | 18'-1" | 16'-2" | 24'-11" | 22'-5" | 30'-2" | 26'-6" |
| 2 x 8 x 68 | 19'-7" | 17'-6" | 26'-8" | 23-'11" | 32'-2" | 28'-7" |
| 2 x 8 x 97 | 22'-10" | 20'-2" | 30'-2" | 26'-10" | 35'-10" | 31'-11" |
| 2 x 10 x 43 | 17'-11" | 16'-2" | 25'-1" | 22'-7" | 30'-6" | 24'-9" |
| 2 x 10 x 54 | 19'-3" | 17'-3" | 26'-7" | 23'-11" | 32-'4" | 29'-1" |
| 2 x 10 x 68 | 20'-9" | 18'-6" | 28'-5" | 25'-6" | 34'-4" | 30'-10" |
| 2 x 10 x 97 | 23'-11" | 21'-2" | 31'-10" | 28'-4" | 38'-0" | 34'-0" |
| 2 x 12 x 43 | 18'-11" | 17'-0" | 26'-6" | 23'-10" | 32'-4" | 24'-5" |
| 2 x 12 x 54 | 20'-2" | 18'-1" | 28'-1" | 25'-3" | 34'-2" | 30'-9" |
| 2 x 12 x 68 | 21'-9" | 19'-5" | 29'-10" | 26'-10" | 36'-2" | 32'-7" |
| 2 x 12 x 97 | 24'-10" | 22'-1" | 33'-4" | 29'-9" | 39'-10" | 35'-8" |

For SI:	1 inch = 25.4 mm,   1 foot = 0.3 m,    1 psf = 0.0479 kN/m2.

1		Table provides the maximum ceiling joist span in feet and inches to either side of the

interior support.

2		Bearing stiffeners shall be installed at all bearing and concentrated load locations.

3		Deflection criteria:  L/240 for total loads.

4		Ceiling dead load = 5 psf (0.24 kN/m2)

5		Interior supports for multiple span joists shall consist of structural walls or beams. Interior 		supports shall be located within 2 feet (610 mm) of mid span provided that each of the

resulting spans do not exceed the maximum applicable span shown in the table above.

6		Refer to Table 2.1 for actual sizes.

Table 8.6

Allowable Spans For Cold-Formed Steel Ceiling Joists (33 ksi)

Single Spans With Bearing Stiffeners

20 Lbs. per Sq. Ft. Live Load (Limited Attic Storage) 1,2,3

| Nominal Joist | Lateral Support of Top (Compression Flange) |
| --- | --- |
|  | Size 4 | Unbraced |
| Mid-Span Bracing |
| Third-Point Bracing |
| Spacing (inches) |
| Spacing (inches) |
| Spacing (inches) |
| 16 | 24 | 16 | 24 | 16 | 24 |
| 2 x 4 x 33 | 8'-0" | 7'-0" | 9'-8" | 8'-1" | 9'-11" | 8'-3" |
| 2 x 4 x 43 | 8'-8" | 7'-8" | 10'-9" | 9'-1" | 10'-10" | 9'-5" |
| 2 x 4 x 54 | 9'-3" | 8'-3" | 11'-7" | 9'-11" | 11'-7" | 10'-1" |
| 2 x 4 x 68 | 10'-0" | 8'-11" | 12'-5" | 10'-10" | 12'-5" | 10'-10" |
| 2 x 4 x 97 | 11'-7" | 10'-3" | 13'-7" | 11'-11" | 13'-7" | 11'-11" |
| 2 x 6 x 33 | 9'-2" | 8'-3" | 12'-2" | 10'-5" | 13'-3" | 11'-0" |
| 2 x 6 x 43 | 9'-10" | 8'-10" | 13'-4" | 11'-6" | 14'-9" | 12'-5" |
| 2 x 6 x 54 | 10'-5" | 9'-5" | 14'-4" | 12'-6" | 16'-1" | 13'-7" |
| 2 x 6 x 68 | 11'-3" | 10'-0" | 15'-4" | 13'-5" | 17'-5" | 14'-10" |
| 2 x 6 x 97 | 12'-9" | 11'-4" | 17'-1" | 15'-1" | 19'-7" | 16'-9 |
| 2 x 8 x 33 | 10'-3" | 9'-3" | 14'-4" | 12'-5" | 15'-11" | 13'-4" |
| 2 x 8 x 43 | 10'-11" | 9'-10" | 15'-5" | 13'-8" | 17'-11" | 15'-5" |
| 2 x 8 x 54 | 11'-8" | 10'-6" | 16'-3" | 14'-7" | 19'-3" | 16'-8" |
| 2 x 8 x 68 | 12'-5" | 11'-2" | 17'-3" | 15'-6" | 20'-7" | 18'-0" |
| 2 x 8 x 97 | 13'-11" | 12'-5" | 18'-7" | 17'-0" | 22'-9" | 20'-1" |
| 2 x 10 x 43 | 11'-9" | 10'-7" | 16'-6" | 14'-10" | 19'-10" | 17'-1" |
| 2 x 10 x 54 | 12'-5" | 11'-2" | 17'-5" | 15'-8" | 21'-1" | 18'-7" |
| 2 x 10 x 68 | 13'-3" | 11'-10" | 18'-5" | 16'-7" | 22'-4" | 19'-11" |
| 2 x 10 x 97 | 14'-9" | 13'-2" | 20'-2" | 18'-1" | 24'-4" | 21'-10" |
| 2 x 12 x 43 | 12'-5" | 11'-2" | 17'-5" | 15'-8" | 20'-9" | 18'-0" |
| 2 x 12 x 54 | 13'-1" | 11'-9" | 18'-5" | 16'-7" | 22'-5" | 20'-1" |
| 2 x 12 x 68 | 13'-11" | 12'-6" | 19'-5" | 17'-6" | 23'-8" | 21'-3" |
| 2 x 12 x 97 | 15'-5" | 13'-10" | 21'-2" | 19'-0" | 25'-8" | 23'-1" |

For SI:	1 inch = 25.4 mm,    1 foot = 0.3 m,    1 psf = 0.0479 kN/m2.

1	Bearing stiffeners shall be installed at all bearing and concentrated load locations.

2	Deflection criteria:  L/240 for total loads.

3	Ceiling dead load = 5 psf (0.24 kN/m2)

4	Refer to Table 2.1 for actual size.

Table 8.7

Allowable Spans For Cold-Formed Steel Ceiling Joists (33 ksi)

Two Equal Spans With Bearing Stiffeners

20 Lbs. per Sq. Ft. Live Load (Limited Attic Storage) 1,2,3,4,5

| Nominal | Lateral Support of Top (Compression Flange) |
| --- | --- |
|  | Joist Size 6 | Unbraced |
| Mid-Span Bracing |
| Third-Point Bracing |
| Spacing (inches) |
| Spacing (inches) |
| Spacing (inches) |
| 16 | 24 | 16 | 24 | 16 | 24 |
| 2 x 4 x 33 | 10'-5" | 8'-6" | 10'-5" | 8'-6" | 10'-5" | 8'-6" |
| 2 x 4 x 43 | 11'-8" | 10'-4" | 12'-8" | 10'-4" | 12'-8" | 10'-4" |
| 2 x 4 x 54 | 12'-9" | 11'-3" | 14'-3" | 11'-7" | 14'-3" | 11'-7" |
| 2 x 4 x 68 | 14'-0" | 12'-4" | 15'-11" | 13'-0" | 15'-11" | 13'-0" |
| 2 x 4 x 97 | 16'-7" | 14'-5" | 18'-3" | 15'-5" | 18'-3" | 15'-5" |
| 2 x 6 x 33 | 12'-3" | 11'-0" | 14'-1" | 11'-0" | 14'-1" | 11'-0" |
| 2 x 6 x 43 | 13'-3" | 11'-10" | 17'-2" | 14'-0" | 17'-2" | 14'-0" |
| 2 x 6 x 54 | 14'-3" | 12'-9" | 19'-2" | 15'-9" | 19'-4" | 15'-9" |
| 2 x 6 x 68 | 15'-6" | 13'-9" | 20'-9" | 17'-8" | 21'-8" | 17'-8" |
| 2 x 6 x 97 | 18'-0" | 15'-11" | 23'-7" | 20'-6" | 25'-11" | 21'-1" |
| 2 x 8 x 33 | 13'-8" | 10'-9" | 14'-8" | 10'-9" | 14'-8" | 10'-9" |
| 2 x 8 x 43 | 14'-9" | 13'-3" | 20'-6" | 17-5" | 21'-3" | 17'-5" |
| 2 x 8 x 54 | 15'-9" | 14'-1" | 21'-10" | 19'-6" | 25'-2" | 20'-6" |
| 2 x 8 x 68 | 17'-0" | 15'-2" | 23'-3" | 20'-10" | 27'-8" | 23'-2" |
| 2 x 8 x 97 | 19'-6" | 17'-3" | 26'-0" | 23'-2" | 30'-11" | 27'-0" |
| 2 x 10 x 43 | 15'-9" | 14'-2" | 22'-0" | 17'-3" | 23'-0" | 17'-3" |
| 2 x 10 x 54 | 16'-9" | 15'-0" | 23'-4" | 21'-0" | 27'-11" | 22'-10" |
| 2 x 10 x 68 | 18'-0" | 16'-1" | 24'-9" | 22'-3" | 30'-0" | 26'-7" |
| 2 x 10 x 97 | 20'-6" | 18'-2" | 27'-6" | 24'-7" | 33'-0" | 29'-6" |
| 2 x 12 x 43 | 16'-7" | 14'-11" | 22'-7" | 16'-7" | 22'-7" | 16'-7" |
| 2 x 12 x 54 | 17'-7" | 15'-10" | 24'-7" | 22'-2" | 30'-0" | 24'-9" |
| 2 x 12 x 68 | 18'-10" | 16'-11" | 26'-1" | 23'-5" | 31'-8" | 28'-5" |
| 2 x 12 x 97 | 21'-5" | 19'-0" | 28'-10" | 25'-10" | 34'-8" | 34'-1" |

For SI:	1 inch  = 25.4 mm,    1 foot = 0.3 m,    1 psf = 0.0479 kN/m2.

1		Table provides the maximum ceiling joist span in feet and inches to either side of the

interior support.

2		Bearing stiffeners shall be installed at all bearing and concentrated load locations.

3		Deflection criteria:  L/240 for total loads.

4		Ceiling dead load = 5 psf (0.24 kN/m2)

5		Interior supports for multiple span joists shall consist of structural walls or beams. Interior			supports shall be unocated within  2 feet (610 mm) of mid span provided that each of the 			resulting spans do not exceed the maximum applicable span shown in the table above.

6		Refer to Table 2.1 for actual sizes.

Table  8.8

Allowable Spans For Cold-Formed Steel Ceiling Joists (33 ksi)

Single Spans Without Bearing Stiffeners

10 Lbs. per Sq. Ft. Live Load (No Attic Storage) 1,2

| Nominal | Lateral Support of Top (Compression) Flange |
| --- | --- |
|  | Joist Size 3 | Unbraced |
| Mid-Span Bracing |
| Third-Point Bracing |
| Spacing (inches) |
| Spacing (inches) |
| Spacing (inches) |
| 16 | 24 | 16 | 24 | 16 | 24 |
| 2 x 4 x 33 | 9’-2” | 8’-3” | 11’-9” | 10’-0” | 11’-9” | 10’-0” |
| 2 x 4 x 43 | 9’-11” | 8’-10” | 12’-10” | 11’-2” | 12’-0” | 11’-2” |
| 2 x 4 x 54 | 10’-8” | 9’-6” | 13’-9” | 12’-0” | 13’-9” | 12’-0” |
| 2 x 4 x 68 | 11’-7” | 10’-4” | 14’-8” | 12’-10” | 14’-8” | 12’-10” |
| 2 x 4 x 97 | 13’-7” | 12’-0” | 16’-2” | 14’-1” | 16’-2” | 14’-1” |
| 2 x 6 x 33 | 10’-5” | 9’-5” | 14’-5” | 10’-0” | 15’-1” | 10’-0” |
| 2 x 6 x 43 | 11’-2” | 10’-1” | 15’-7” | 13’-10” | 18’-0” | 15’-5” |
| 2 x 6 x 54 | 12’-0” | 10’-9” | 16’-7” | 14’-9” | 19’-5” | 16’-8” |
| 2 x 6 x 68 | 12’-11” | 11’-7” | 17’-8” | 15’-10” | 20’-11” | 18’-1” |
| 2 x 6 x 97 | 14’-11” | 13’-2” | 19’-10” | 17’-8” | 23’-2” | 20’-3” |
| 2 x 8 x 33 | - | - | - | - | - | - |
| 2 x 8 x 43 | 12’-6” | 11’-3” | 17’-6” | 15’-10” | 21’-2” | 17’-9” |
| 2 x 8 x 54 | 13’-4” | 11’-11” | 18’-7” | 16’-9” | 22’-7” | 20’-0” |
| 2 x 8 x 68 | 14’-3” | 12’-9” | 19’-8” | 17’-8” | 23’-11” | 21’-4” |
| 2 x 8 x 97 | 16’-2” | 14’-5” | 21’-10” | 19’-6” | 26’-3” | 23’-6” |
| 2 x 10 x 43 | - | - | - | - | - |
|  | 2 x 10 x 54 | 14’-2” | 12’-9” | 19’-10” | 17’-10” | 24’-2” | 21’-9” |
| 2 x 10 x 68 | 15’-2” | 13’-7” | 21’-0” | 18’-11” | 25’-6” | 23’-0” |
| 2 x 10 x 97 | 17’-1” | 15’-2” | 23’-2” | 20’-9” | 27’-11” | 25’-1” |
| 2 x 12 x 43 | - | - | - | - | - | - |
| 2 x 12 x 54 | - | - | - | - | - | - |
| 2 x 12 x 68 | 15’-11” | 14’-4” | 22’-2” | 19’-11” | 27’-0” | 24’-4” |
| 2 x 12 x 97 | 17’-10” | 15’-11” | 24’-4” | 21’-10” | 29’-4” | 26’-5” |

For SI:	1 inch = 25.4 mm,    1 foot = 0.3 m,    1 psf = 0.0479 kN/m2.

1		Deflection criteria:  L/240 for total loads.

2		Ceiling dead load = 5 psf (0.24 kN/m2)

3		Refer to Table 2.1 for actual size.

Table  8.9

Allowable Spans For Cold-Formed Steel Ceiling Joists (33 ksi)

Two Equal Spans Without Bearing Stiffeners

10 Lbs. per Sq. Ft. Live Load (No Attic Storage) 1,2,3,4

Nominal

|  | Lateral Support of Top (Compression Flange) |
| --- | --- |
|  | Joist Size 5 | Unbraced |
| Mid-Span Bracing |
| Third-Point Bracing |
| Spacing (inches) |
| Spacing (inches) |
| Spacing (inches) |
| 16 | 24 | 16 | 24 | 16 | 24 |
| 2 x 4 x 33 | 11’-6” | 8’-9” | 11’-6” | 8’-9” | 11’-6” | 8’-9” |
| 2 x 4 x 43 | 13’-6” | 11’-8” | 15’-2” | 11’-8” | 15’-2” | 11’-8” |
| 2 x 4 x 54 | 14’-9” | 13’-1” | 18’-2” | 14’-2” | 18’-2” | 14’-2” |
| 2 x 4 x 68 | 16’-4” | 14’-5” | 19’-8” | 16’-7” | 19’-8” | 16’-7” |
| 2 x 4 x 97 | 19’-6” | 17’-2” | 21’-8” | 18’-11” | 21’-8” | 18’-11” |
| 2 x 6 x 33 | 13’-8” | 10’-1” | 13’-8” | 10’-1” | 13’-8” | 10’-1” |
| 2 x 6 x 43 | 15’-2” | 13’-7” | 18’-8” | 14’-0” | 18’-8” | 14’-0” |
| 2 x 6 x 54 | 16’-5” | 14’-8” | 22’-5” | 17’-6” | 22’-11” | 17’-6” |
| 2 x 6 x 68 | 17’-11” | 15’-11” | 24’-1” | 21’-5” | 27’-9” | 21’-7” |
| 2 x 6 x 97 | 21’-2” | 18’-8” | 27’-7” | 24’-5” | 31’-1” | 27’-2” |
| 2 x 8 x 33 | - | - | - | - | - | - |
| 2 x 8 x 43 | 16’-10” | 15’-1” | 20’-7” | 15’-3” | 20’-7” | 15’-3” |
| 2 x 8 x 54 | 18’-1” | 16’-2” | 24’-11” | 20’-3” | 26’-11” | 20’-3” |
| 2 x 8 x 68 | 19’-7” | 17’-6” | 26’-8” | 23’-11” | 32’-2” | 25’-11” |
| 2 x 8 x 97 | 22’-10” | 20’-2” | 30’-2” | 26’-10” | 35’-10” | 31’-11” |
| 2 x 10 x 43 | - | - | - | - | - |
|  | 2 x 10 x 54 | 19’-3” | 17’-3” | 26’-7” | 20’-11” | 28’-1” | 20’-11” |
| 2 x 10 x 68 | 20’-9” | 18’-6” | 28’-5” | 25’-6” | 34’-4” | 28’-5” |
| 2 x 10 x 97 | 23’-11” | 21’-2” | 31’-10” | 28’-4” | 38’-0” | 34’-0” |
| 2 x 12 x 43 | - | - | - | - | - | - |
| 2 x 12 x 54 | - | - | - | - | - | - |
| 2 x 12 x 68 | 21’-9” | 19’-5” | 29’-10” | 26’-10” | 36’-2” | 29’-0” |
| 2 x 12 x 97 | 24’-10” | 22’-1” | 33’-4” | 29’-9” | 39’-10” | 35’-8” |

For SI:	1 inch = 25.4 mm,   1 foot = 0.3 m,    1 psf = 0.0479 kN/m2.

1		Table provides the maximum ceiling joist span in feet and inches to either side of the

interior support.

2		Deflection criteria:  L/240 for total loads.

3		Ceiling dead load = 5 psf (0.24 kN/m2)

5		Interior supports for multiple span joists shall consist of structural walls or beams.  Interior 		supports shall be located within 2 feet (610 mm) of mid span provided that each of the 			resulting spans do not exceed the maximum applicable span shown in the table above.

5		Refer to Table 2.1 for actual sizes.

Table 8.10

Allowable Spans For Cold-Formed Steel Ceiling Joists (33 ksi)

Single Spans Without Bearing Stiffeners

20 Lbs. per Sq. Ft. Live Load (Limited Attic Storage) 1,2

| Nominal Joist | Lateral Support of Top (Compression Flange) |
| --- | --- |
|  | Size 3 | Unbraced |
| Mid-Span Bracing |
| Third-Point Bracing |
| Spacing (inches) |
| Spacing (inches) |
| Spacing (inches) |
| 16 | 24 | 16 | 24 | 16 | 24 |
| 2 x 4 x 33 | 8'-0" | 6'-0" | 9'-0" | 6'-0" | 9'-0" | 6'-0" |
| 2 x 4 x 43 | 8'-8" | 7'-8" | 10'-9" | 9'-1" | 10'-10" | 9'-5" |
| 2 x 4 x 54 | 9'-3" | 8'-3" | 11'-7" | 9'-11" | 11'-7" | 10'-1" |
| 2 x 4 x 68 | 10'-0" | 8'-11" | 12'-5" | 10'-10" | 12'-5" | 10'-10" |
| 2 x 4 x 97 | 11'-7" | 10'-3" | 13'-7" | 11'-11" | 13'-7" | 11'-11" |
| 2 x 6 x 33 | 9'-0" | 6'-0" | 9'-0" | 6'-0" | 9'-0" | 6'-0" |
| 2 x 6 x 43 | 9'-10" | 8'-10" | 13'-4" | 11'-6" | 14'-9" | 11'-8" |
| 2 x 6 x 54 | 10'-5" | 9'-5" | 14'-4" | 12'-6" | 16'-1" | 13'-7" |
| 2 x 6 x 68 | 11'-3" | 10'-0" | 15'-4" | 13'-5" | 17'-5" | 14'-10" |
| 2 x 6 x 97 | 12'-9" | 11'-4" | 17'-1" | 15'-1" | 19'-7" | 16'-9 |
| 2 x 8 x 33 | - | - | - | - | - | - |
| 2 x 8 x 43 | 10'-11" | 9'-0" | 14'-7" | 10'-0" | 16'-0" | 10'-8" |
| 2 x 8 x 54 | 11'-8" | 10'-6" | 16'-3" | 14'-7" | 19'-3" | 16'-8" |
| 2 x 8 x 68 | 12'-5" | 11'-2" | 17'-3" | 15'-6" | 20'-7" | 18'-0" |
| 2 x 8 x 97 | 13'-11" | 12'-5" | 18'-11" | 17'-0" | 22'-9" | 20'-1" |
| 2 x 10 x 43 | - | - | - | - | - | - |
| 2 x 10 x 54 | 12'-5" | 11'-2" | 17'-5" | 15'-8" | 21'-1" | 16'-9" |
| 2 x 10 x 68 | 13'-3" | 11'-10" | 18'-5" | 16'-7" | 22'-4" | 19'-11" |
| 2 x 10 x 97 | 14'-9" | 13'-2" | 20'-2" | 18'-1" | 24'-4" | 21'-10" |
| 2 x 12 x 43 | - | - | - | - | - | - |
| 2 x 12 x 54 | - | - | - | - | - | - |
| 2 x 12 x 68 | 13'-11" | 12'-6" | 19'-5" | 17'-6" | 23'-8" | 21'-3" |
| 2 x 12 x 97 | 15'-5" | 13'-10" | 21'-2" | 19'-0" | 25'-8" | 23'-1" |

For SI:	1 inch = 25.4 mm,    1 foot = 0.3 m,    1 psf = 0.0479 kN/m2.

1	Deflection criteria:  L/240 for total loads.

2	Ceiling dead load = 5 psf (0.24 kN/m2)

3	Refer to Table 2.1 for actual size.

Table 8.11

Allowable Spans For Cold-Formed Steel Ceiling Joists (33 ksi)

Two Equal Spans Without Bearing Stiffeners

20 Lbs. per Sq. Ft. Live Load (Limited Attic Storage) 1,2,3,4

| Nominal | Lateral Support of Top (Compression Flange) |
| --- | --- |
|  | Joist Size 5 | Unbraced |
| Mid-Span Bracing |
| Third-Point Bracing |
| Spacing (inches) |
| Spacing (inches) |
| Spacing (inches) |
| 16 | 24 | 16 | 24 | 16 | 24 |
| 2 x 4 x 33 | 8'-1" | 6'-0" | 8'-1" | 6'-0" | 8'-1" | 6'-0" |
| 2 x 4 x 43 | 10'-10" | 8'-3" | 10'-10" | 8'-3" | 10'-10" | 8'-3" |
| 2 x 4 x 54 | 12'-9" | 10'-2" | 13'-3" | 10'-2" | 13'-3" | 10'-2" |
| 2 x 4 x 68 | 14'-0" | 12'-4" | 15'-9" | 12'-5" | 15'-9" | 12'-5" |
| 2 x 4 x 97 | 16'-7" | 14'-5" | 18'-3" | 15'-2" | 18'-3" | 15'-2" |
| 2 x 6 x 33 | 9'-3" | 6'-9" | 9'-3" | 6'-9" | 9'-3" | 6'-9" |
| 2 x 6 x 43 | 13'-0" | 9'-8" | 13'-0" | 9'-8" | 13'-0" | 9'-8" |
| 2 x 6 x 54 | 14'-3" | 12'-4" | 16'-4" | 12'-4" | 16'-4" | 12'-4" |
| 2 x 6 x 68 | 15'-6" | 13'-9" | 20'-3" | 15'-7" | 20'-3" | 15'-7" |
| 2 x 6 x 97 | 18'-0" | 15'-11" | 23'-7" | 20'-6" | 25'-10" | 21'-0" |
| 2 x 8 x 33 | - | - | - | - | - | - |
| 2 x 8 x 43 | 14'-0" | 10'-2" | 14'-0" | 10'-2" | 14'-0" | 10'-2" |
| 2 x 8 x 54 | 15'-9" | 13'-10" | 18'-9" | 13'-10" | 18'-9" | 13'-10" |
| 2 x 8 x 68 | 17'-0" | 15'-2" | 23'-3" | 18'-3" | 24'-2" | 18'-3" |
| 2 x 8 x 97 | 19'-6" | 17'-3" | 26'-0" | 23'-2" | 30'-11" | 25'-11" |
| 2 x 10 x 43 | - | - | - | - | - | - |
| 2 x 10 x 54 | 16'-9" | 14'-1" | 19'-4" | 14'-1" | 19'-4" | 14'-1" |
| 2 x 10 x 68 | 18'-0" | 16'-1" | 24'-9" | 19'-8" | 26'-4" | 19'-8" |
| 2 x 10 x 97 | 20'-6" | 18'-2" | 27'-6" | 24'-7" | 33'-0" | 29'-0" |
| 2 x 12 x 43 | - | - | - | - | - | - |
| 2 x 12 x 54 | - | - | - | - | - | - |
| 2 x 12 x 68 | 18'-10" | 16'-11" | 26'-1" | 19'-10" | 26'-1" | 19'-10" |
| 2 x 12 x 97 | 21'-5" | 19'-0" | 28'-10" | 25'-10" | 34'-8" | 31'-1" |

For SI:	1inch = 25.4 mm,    1 foot = 0.3 m,    1 psf = 0.0479 kN/m2.

1		Table provides the maximum ceiling joist span in feet and inches to either side of the

the interior support.

2		Deflection criteria:  L/240 for total loads.

3		Ceiling dead load = 5 psf (0.24 kN/m2)

5		Interior supports for multiple span joists shall consist of structural walls or beams. Interior   		supports shall be located within 2 feet (610 mm) of mid span provided that each of the

resulting spans do not exceed the maximum applicable span shown in the table above.

5		Refer to Table 2.1 for actual sizes.

Table 8.12

Allowable Horizontal Rafter Spans1,2,3

33 ksi

| Nominal | Ground Snow Loads |
| --- | --- |
|  | Joist Size 4 | 20 psf Ground |
| 30 psf Ground |
| 50 psf Ground |
| 70 psf Ground |
| Spacing (inches) |
| Spacing (inches) |
| Spacing (inches) |
| Spacing (inches) |
| 16 | 24 | 16 | 24 | 16 | 24 | 16 | 24 |
| 2 x 6 x 33 | 12'-8" | 10'-4" | 11'-9" | 9'-7" | 9'-11" | 8'-1" | 8'-10" | 7'-2" |
| 2 x 6 x 43 | 15'-5" | 12' -7" | 14'-3" | 11'-8" | 12'-1" | 9'-10" | 10'-8" | 8'-9" |
| 2 x 6 x 54 | 13'-0" | 14'-2" | 16'-1" | 13'-1" | 13'-8" | 11'-2" | 12'-1" | 9'-10" |
| 2 x 6 x 68 | 18'-1" | 15'-10" | 17'-3" | 14'-9" | 15'-4" | 12'-6" | 13'-6" | 11'-1" |
| 2 x 6 x 97 | 20'-1" | 17'-6" | 19'-1" | 16'-8" | 17'-1" | 14' | 15'-7" | 13'-2" |
| 2 x 8 x 33 | 15'-5" | 11'-5" | 14'-4" | 9'-10" | 10'-7" | 7'-1" | 8'-3" | 5'-6" |
| 2 x 8 x 43 | 19'-1" | 15'-7' | 17'-9" | 14'-6" | 15'-1" | 12'-3" | 13'-3" | 10'-9" |
| 2 x 8 x 54 | 22'-7" | 18'-5" | 21'-0" | 17'-1" | 17'-9" | 14'-6" | 15'-9" | 12-10" |
| 2 x 8 x 68 | 24'-7" | 20'-9" | 23'-4" | 19'-3" | 20'-0" | 16'-4" | 17'-8" | 14'-5" |
| 2 x 8 x 97 | 27'-3" | 23'-9" | 26'-0" | 22'-8" | 23'-3" | 19'-7" | 21'-3" | 17'-4" |
| 2 x 10 x 43 | 21'-2" | 17'-3" | 19'-8" | 16'-0" | 16'-8" | 13'-1" | 14'-9" | 10'-3" |
| 2 x 10 x 54 | 25'-1" | 20'-6" | 23'-3" | 19'-0" | 19'-9" | 16'-1" | 17'-5" | 14'-3" |
| 2 x 10 x 68 | 29'-6" | 24'-6" | 27'-9" | 22'-9" | 23'-8" | 19'-3" | 21'-0" | 17'-1" |
| 2 x 10 x 97 | 32'-0" | 28'-8" | 31'-3" | 27'-3" | 28'-0" | 23'-2" | 25'-1" | 20'-6" |
| 2 x 12 x 43 | 23'-0" | 18'-2" | 21'-4" | 15'-7" | 16'-9" | 11'-3" | 13'-2" | 8'-9" |
| 2 x 12 x 54 | 27'-3" | 22'-3" | 25'-3" | 20'-7" | 21'-5" | 17'-6" | 18'-11 | 15'-5" |
| 2 x 12 x 68 | 32'-1" | 26'-2" | 29'-9" | 24'-3" | 25'-3" | 20'-7" | 22'-4" | 18'-2" |
| 2 x 12 x 97 | 38'-4" | 33'-6" | 36'-6" | 31'-6" | 32'-8" | 26'-9" | 29'-0" | 23'-7" |

For SI:	1 inch = 25.4 mm,    1 foot = 0.3 m,    1 psf = 0.0479 kN/m2.

1		Table provides the maximum horizontal rafter span in feet and inches for slopes from 3:12 to

12:12.

2		Deflection criteria:  L/240 for live loads and L/180 for total loads.

3		Roof dead load = 12 psf (0.575 kN/m2)

4		Refer to Table 2.1 for actual member size.

Table 8.13

Wind Speed to Equivalent Snow Load Conversion 1

| Roof Slope | Equivalent Ground Snow Load (psf) |
| --- | --- |
| Wind Speed (mph) Exposure C |
| 70 | 80 | 90 | 100 | 110 |
|  | 3 / 12 | 20 | 20 | 20 | 30 | 50 |
|  | 4 / 12 | 20 | 20 | 30 | 50 | 50 |
|  | 5 / 12 | 20 | 20 | 30 | 50 | 50 |
|  | 6 / 12 | 20 | 20 | 30 | 50 | 70 |
|  | 7 / 12 | 30 | 30 | 50 | 70 | 70 |
|  | 8 / 12 | 30 | 30 | 50 | 70 |
| 9 / 12 | 30 | 50 | 50 | 70 |
| 10 / 12 | 30 | 50 | 50 | Design Required |
| 11 / 12 | 30 | 50 | 70 |
|  | 12 / 12 | 50 | 50 | 70 |
| Wind Speed (mph) Exposure B |
| 70 | 80 | 90 | 100 | 110 |
|  | 3 / 12 | 20 | 20 | 20 | 30 | 50 |
|  | 4 / 12 | 20 | 20 | 20 | 30 | 50 |
|  | 5 / 12 | 20 | 20 | 20 | 30 | 50 |
|  | 6 / 12 | 20 | 20 | 20 | 50 | 50 |
|  | 7 / 12 | 20 | 30 | 30 | 5 0 | 70 |
|  | 8 / 12 | 20 | 30 | 50 | 50 | 70 |
|  | 9 / 12 | 30 | 30 | 50 | 70 | 70 |
|  | 10 / 12 | 30 | 30 | 50 | 70 | Design |
|  | 11 / 12 | 30 | 50 | 50 | 70 | Required |
|  | 12 / 12 | 30 | 50 | 50 |

For SI:	1 mph = 1.61 km/hr,   1 psf = 0.0479 kN/m2.

1	Exposure C category shall be used if site wind exposure is unknown.

Table 8.14

Uplift Loads on Roof-to-Wall Connections

for Selection of Roof Tie-Downs (lbs/ft)1,2,3

| Wind Speed (mph) and Exposure Category |
| --- |
|  | Up to 70 C or 90 A/B | 90 C or 110 A/B | 100 C | 110 C |
| N/R | 100 lbs/ft. | 200 lbs/ft. | 300 lbs/ft. |

For SI:	1 inch = 25.4 mm,  1 lb. = 4.4 N.

1	N/R = uplift connector not required.

2	For 16-inch ( 406 mm) and 24-inch ( 610 mm) rafter spacing, the uplift load shall be multiplied by 1.3 and 2.0, respectively.

3	Uplift connectors shall be provided in addition to other fastening requirements.

9.0	MECHANICAL, UTILITIES, AND INSULATION

9.1	Plumbing

Plumbing shall comply with the applicable plumbing code.  Copper and plastic pipes shall be separated from the steel framing by non-conductive grommets or other approved methods.  A list of the appropriate types of plastic insulators and grommets for web holes which are pre-punched is generally available from the steel supplier.

9.2	Electrical Systems

Electrical system installation shall comply with the latest edition of the National Electric Code.  Snap-in plastic insulators, grommets, conduit, or other approved wire protection methods shall be used to protect the plastic sheathing on electrical cables when passing through holes in steel framing members (i.e. punchouts in studs and joists).

9.3	HVAC Systems and Duct Work

HVAC installation shall comply with the applicable mechanical code and energy code.

9.4	Insulation

Insulation of steel frame exterior walls, floors, and roofs shall comply with the applicable energy code.  All types of insulation are compatible with steel framing (e.g. batt insulation, spray-applied foam, foam plastic board, etc.).  In many climates, a layer of exterior foam sheathing is required to meet energy code.  Suggested insulation R-values for walls in various areas of the country can be found in AISI publication #RG-9405 Thermal Design Guide for Exterior Walls [18].

10.0	GENERAL CONSTRUCTION GUIDELINES

(	Each stud, joist, and track member shall bear the Manufacturer’s name, logo or initials, base metal 	thickness (uncoated), minimum specified yield strength, and minimum coating designation.

(	All structural members shall be aligned vertically (in-line framing) to transfer all loads to the foundation.

Track members shall not be used individually for any load carrying applications without an

approved design

Studs, tracks, and other steel members should be in good condition.  Bent, warped, split, or

otherwise damaged members shall be replaced.

(	Bearing surfaces for joists, rafters, and trusses shall be uniform and level.

(	All load bearing studs, including king and jack studs, shall be seated in the tracks with a maximum gap of 1/8 inch (0.32 mm) between the end of the stud and the web of the track.

(	Adequate temporary construction bracing of wall, floor, and roof framing shall be provided until permanent bracing  has been installed.

Any corrections which involve cutting, drilling, or relocation of any truss member or component

shall not be made without notifying the truss manufacturer of the need for and extent of the

modifications.  All major corrections, cutting, or drilling of truss members without the approval of

a qualified design professional shall be prohibited.

11.0	REFERENCES

[1]	Specification For The Design Of Cold Formed Steel Structural Members	(August 19, 1986 	Edition with December 11, 1989 Addendum). American Iron and Steel Institute (AISI), 	Washington, DC. 1989.

[2]	Minimum Design Load for Buildings and Other Structures (ASCE 7-93). American Society

of Civil Engineers, New York, NY. 1993.

[3]	Standard Building Code. Southern Building Code Congress International, Inc. (SBCCI).

Birmingham, Alabama. 1994.

[4]	Uniform Building Code.  International Conference of Building Officials (ICBO).  Whittier, California.  1994.

[5]	The BOCA National Building Code.  Building Officials & Code Administrators International,

Inc. (BOCA). Country Club Hills, Illinois. 1993.

[6]	Commentary on the Prescriptive Method for Residential Cold-Formed Steel Framing. Second Edition.  Prepared for the US Department of HUD by the National Association of Home Builders Research Center.  Upper Marlboro, Maryland. July 1997.

[7]	ASTM A 370- 96 Standard Test Methods and Definitions for Mechanical Testing of Steel Products, American Society for Testing and Materials (ASTM), West Conshohocken, PA. 1996.

[8]	ASTM A 653 / A 653M - 1996  Standard Specification for Steel Sheet, Zinc-Coated (Galvanized) or Zinc-Iron Alloy-Coated (Galvannealed) by the Hot-Dip Process, American Society for Testing and Materials (ASTM), West Conshohocken, PA. 1996.

[9]	ASTM A 792 / A 792M Standard Specification for Steel Sheet, 55% Aluminum-Zinc Alloy-Coated by the Hot-Dip Process, American Society for Testing and Materials (ASTM), West Conshohocken, PA. 1996.

[10]	ASTM A 875 / A 875M Standard Specification for Steel Sheet, Zinc-5% Aluminum Alloy Metallic-Coated by the Hot-Dip Process, American Society for Testing and Materials (ASTM), West Conshohocken, PA. 1996.

[11]	ASTM C 955-96a Standard Specification for Load-Bearing (Transverse and Axial) Steel Studs, Runners (Tracks), and Bracing or Bridging for Screw Application of Gypsum Board and Metal Plaster Bases, American Society for Testing and Materials (ASTM), West Conshohocken, PA. 1996.

[12]	ASTM C 645 - 96a  Standard Specification for Nonstructural Steel Framing Members, American Society for Testing and Materials (ASTM), West Conshohocken, PA. 1996.

[13]	ASTM B633 -85 e1 Standard Specification for Electrodeposited Coatings of Zinc on Iron and Steel, American Society for Testing and Materials (ASTM), West Conshohocken, PA. 1994.

[14]	SAE J-78-1979, Steel Self Drilling Tapping Screws, Society of Automotive Engineers, 1979.

[15]	ASTM C 954-96ae1 Standard Specification for Steel Drill Screws for the Application of Gypsum Panel Products or Metal Plaster Bases to Steel Studs From 0.033 in. (0.84 mm) to 0.112 in. (2.84 mm) in Thickness, American Society for Testing and Materials (ASTM), West Conshohocken, PA. 1996.

[16]	ASTM Standard A 307 - 94  Standard Specification for Carbon Steel Bolts and Studs, 60000 PSI Tensile Strength, American Society for Testing and Materials (ASTM), ASTM, West Conshohocken, PA. 1994.

[17]	AISI Publication RG-9518, Design Guide For Cold-Formed Steel Trusses, American Iron and Steel Institute (AISI), Washington DC.  December 1995.

[18]	AISI Publication RG-9405, Thermal Design Guide For Exterior Walls, American Iron and Steel Institute (AISI), Washington DC.  December 1995.